## Slide 1: Old and new latency requirements
Date: 2018-11-12
Name | Affiliation | Address | Phone | Email
Kazuyuki Sakoda | Sony | 1730 N. First Street, San Jose CA 95112 |  | kazuyuki.sakoda(at)sony.com
William Carney | Sony |  |  | William.Carney(at)sony.com

## Slide 2: Introduction
Today, many devices handle video streaming via 802.11 WLAN. Most of them are not latency sensitive
However, some video applications require low latency capability
In many of these case, the latency requirements are derived from the video frame rate
60Hz framerate is commonly used, i.e., 16.7[msec] per frame
To accommodate end-end signal processing in a video frame, we need to make sure that the signal processing delay plus transmission latency is less than 16.7 [msec]
For these applications, ideally, 10[msec] one-way or roundtrip delay should be considered as a targeted specification

## Slide 3: Interactive Experience Requires Low Latency Capability
In general, low latency requirements will arise when there is a control loop in the system
Case B: interactive video
Case A: video subscription
This case, latency should be constrained by video frame rate
Video server
AP
Smartphone, TV (dongle)
Human
Video content
Feedback input
Renderer
Human

## Slide 4: Why does the video frame rate matter? (1)
High quality VR headset
60Hz/16.7msec
Video content
Feedback input
= Head tracker
Renderer
Human
= Move

## Slide 5: Why does the video frame rate matter? (2)
HDMI cable replacement
Video content
Feedback input
= game commander
Renderer
Human

## Slide 6: Why does the video frame rate matter? (3)
The interactive video application requires low latency transmission capability
The video contents needs to be updated per feedback from the user reaction. This is the source of the latency requirement
As of today, we should target 60Hz video frame rate (1 video picture per 16.7msec)
Transmission needs to be completed in 5msec or 10msec, depending on the applications

## Slide 7: The requirement has been there…
802.11ad functional requirements [1]
802.11ac functional requirements and evaluation methodology [2]

## Slide 8: The requirement has been there…
802.11ax usage models [3]

## Slide 9: The requirement has been there…
802.11ay evaluation methodology [4]

## Slide 10: The requirement has been there…
802.11ay use case [5]

## Slide 11: The requirement has been there…
These requirements are well known in the 802.11 community, but there has not been much effort to take these requirements seriously until RTA discussions

## Slide 12: Summary
It is recommended that RTA considers real time video application as a part of the target applications
The target latency requirement for the real time video application is derived from video frame rate of 60Hz
It is further recommended to define latency target to be 10 [msec] roundtrip or 5 [msec] one way for these applications

## Slide 13: References
[1] 11-09/0094r0, “TGad Functional Requirements,” Eldad Perahia
[2] 11-09/0451r16, “Tgac Functional Requirements and Evaluation Methodology,” Peter Loc, et.al.
[3] 11-13/0657r6, “Usage models for IEEE 802.11 High Efficiency WLAN study group (HEW SG) – Liaison with WFA,” Laurent Cariou
[4] 11-15-0866r2, “TGay Evaluation Methodology,” Laurent Cariou, et.al.
[5] 11-15/0625r7, “IEEE 802.11 TGay Use Cases,” Rob Sun, et.al.