## Slide 1: HARQ Feasibility for EHT
Date: 2018-11-09
Authors:
Name | Affiliations | Address | Phone | email
Yan Zhang Hongyuan Zhang Sudhir Srinivasa Liwen Chu Rui Cao Jinjing Jiang Mao Yu | Marvell |  |  | Hongyuan@marvell.com

## Slide 2: HARQ Overview
HARQ is claimed as a major feature differentiation of cellular over WLAN.
Compared with ARQ (simple retransmission as in current 802.11 MAC), HARQ enables soft combining or additional parity at Rx to improve link level reliability on retransmissions.
HARQ may significantly enhance user experience on top of the current 802.11 retransmission schemes.
  Much higher chance that a retransmission may get through without rate drop.
  User experience enhancement especially when the connection is weak or experiencing interferences.
  HARQ may be of less use when link is already strong or stable (e.g. close range, and/or clean environment)
Notes: Following are some schemes used in dense Wifi deployments:
Usage of directional antennas.
  APs will be using same BW (higher BW available).
  On the intersection area, the CCI (if both APs are transmitting) is more.
Usage Band planning
  Because of CCI, the band which is used by adjacent AP need to have higher separation.
  Planning of band for each AP based on the location is required.
Spatial diversity
  Use higher number of antenna to exploit the spatial diversity in the channel.
  Requires more hardware and high cost.
  Pcell
    Use multiple-antenna placed at widely different location and use BF scheme to direct the transmission
Proposed Solution (SDM)
  Similar to Pcell but use different APs to attain the effect of multiple antennas.
  The co-operation of APs will be done as required.
  Can be implemented using software update.

## Slide 3: HARQ Choices
HARQ with two flavors:
  Chase combining (CC)-retry the same coded MPDU.
  Incremental redundancy (IR)—retry with additional parity.
HARQ-CC is easier to work with the current 802.11 re-transmission mechanism (at MPDU level).
HARQ-IR may require FEC design changes and other major PHY/MAC changes, but could be more efficient than CC.

## Slide 4: Retransmissions
Baseline 802.11 retransmission : retry the failed MPDU(s) in the next AMPDU, likely aggregated with fresh MPDUs; when FER is high or when retransmissions keep failing, rate is dropped.
  How much rate drop may be determined by FER.
When combining HARQ with 802.11 AMPDU retransmissions, the chance of rate drop gets much lower due to improved FER—see simulation results.
This enhances user experience (or link reliability) especially for cases:
  Long range/weak signal strength
  OBSS or other interferences “come and go”.
  Channel variation, e.g. due to movements (people walking around)

## Slide 5: Simulations
20MHz 1x1 DNLOS channel (per channel normalization)
4x HE-LTF, MCS0-11
BCC and LDPC
Same channel realization and scrambling for (re)transmissions if HARQ is applied.
Artificial frequency diversity :
  BCC interleaver or LPDC mapper patterns are shifted across the (re)transmissions to maximize the frequency domain distance of the same coded bit.
  DTM, or NCOL, NROW, NROT are still the same as 11ax

## Slide 6: PHY Link Level Simulation Results (DNLOS)
Refer to Appendix for all the curves
HARQ retransmission dB gain over ARQ @ %1 PER for selected cases:
 | 2 Transmissions no freq diversity | 2 Transmissions freq diversity | 4 Transmissions no freq diversity | 4 Transmissions freq diversity
LDPC, MCS0 | 2dB | 5.5dB | 3.5dB | 7.5dB
LDPC, MCS4 | 2.5dB | 5.5dB | 4.5dB | 8dB
LDPC, MCS7 | 3dB | 9dB | 5dB | 13dB
LDPC, MCS9 | 3dB | 9dB | 5dB | 13dB
BCC, MCS0 | 2dB | 4dB | 4dB | 6.5dB
BCC, MCS4 | 2dB | 8dB | 5dB | 12.5dB
BCC, MCS7 | 3dB | 9dB | 5dB | 15dB
BCC, MCS9 | 3dB | 10dB | 6dB | 15dB

## Slide 7: Discussions
The gain shown in previous page is conditioned on when retransmission happens.
  i.e. the gain means that “How much more reliable that a retransmission may be sent throughput without rate drop”.
In real scenarios, especially for weak or unstable connection (channel variation, interference, etc), frequent retransmissions may happen anyway.

## Slide 8: Conclusions
HARQ may potentially bring big improvement on link reliability, enabling EHT to claim a major differentiation feature from previous gens.
Simulations show good link level (PER) improvement on the transmissions.
Next: throughput study, complexity/cost evaluation (IR vs CC, how to work with current PHY and MAC, etc)

## Slide 9: Appendix: PER Curves

## Slide 10: LDPC MCS0 (500bytes)

## Slide 11: LDPC MCS1 (500 bytes)

## Slide 12: LDPC MCS2 (500 bytes)

## Slide 13: LDPC MCS3 (500 bytes)

## Slide 14: LDPC MCS4 (1000 bytes)

## Slide 15: LDPC MCS5 (1000bytes)

## Slide 16: LDPC MCS6 (1000 bytes)

## Slide 17: LDPC MCS7 (1500bytes)

## Slide 18: LDPC MCS8 (2000 bytes)

## Slide 19: LDPC MCS9 (2000 bytes)

## Slide 20: LDPC MCS10 (3000 bytes)

## Slide 21: LDPC MCS11 (3000 bytes)

## Slide 22: BCC MCS0 (500bytes)

## Slide 23: BCC MCS1 (500 bytes)

## Slide 24: BCC MCS2 (500 bytes)

## Slide 25: BCC MCS3 (500 bytes)

## Slide 26: BCC MCS4 (1000 bytes)

## Slide 27: BCC MCS5 (1000bytes)

## Slide 28: BCC MCS6 (1000 bytes)

## Slide 29: BCC MCS7 (1500bytes)

## Slide 30: BCC MCS8 (2000 bytes)

## Slide 31: BCC MCS9 (2000 bytes)