## Slide 1: AANI SC Update to 802.11 WG Related to 802.11ax IMT-2020 Performance Evaluations
Date: 2018-11-12
Authors:

## Slide 2: Abstract
This document provides a summary of the activity of the AANI SC related to 802.11ax IMT-2020 performance evaluation and provides a motion to approve an outgoing LS to 3GPP and 3GPP SA TSG and copied to the 802 EC, 802.1, WFA, and WBA

## Slide 3: AANI SC Historical Contributions addressing 802.11ax performance relative to the IMT-2020 EMBB requirements:
11-18/0256r0 “802.11ax for IMT-2020”
11-18/0517r0 “802.11ax for IMT-2020 eMBB Indoor Hotspot and Dense Urban”
11-18/0915r1 “Benchmarking of 802.11ax against eMBB Indoor Hotspot requirements using IMT-2020 simulation methodology”
11-18/1240r0 “802.11ax for IMT-2020 eMBB Indoor Hotspot”
11-18/1573r1 “Summary of 802.11ax Self Evaluation for IMT-2020 EMBB Indoor Hotspot and Dense Urban Test Environments”
11-18/1340r2 “Proposed LS to 3GPP/WFA/WBA/WifiForward on the studies done regarding benchmarking of 802.11ax capabilities”

## Slide 4: New contributions addressing 802.11ax performance relative to the IMT-2020 EMBB requirements:
Discussion on draft LS:
  11-18/1340r4 – “Proposed LS to 3GPP/WFA/WBA/WifiForward on the studies done regarding benchmarking of 802.11ax capabilities” – updated to r5, r6
802.11 technical performance relative to IMT-2020 requirements
  11-18/1573r3 – “Summary of 802.11ax Self Evaluation for IMT-2020 EMBB Indoor Hotspot and Dense Urban Test Environments – updated to r4
  11-18/0915r2 – “Benchmarking of 802.11ax against eMBB Indoor Hotspot requirements using IMT-2020 simulation methodology”
  11-18/1240r3 – “802.11ax for IMT-2020 eMBB Indoor Hotspot”

## Slide 5: 11-18/1573r6 – “Summary of 802.11ax Self Evaluation for IMT-2020 EMBB Indoor Hotspot and Dense Urban Test Environments”
The following slides provide the Evaluation Summary for eMBB, taken from 11-18/1573r6

## Slide 6
 | Metric | ITU-R Evaluation Method | Minimum Requirement | 802.11ax Performance
1 | Peak data rate | Analytical | DL/UL : 20/10 Gbps | DL/UL : 20.78 Gbps [Note 1]
2 | Peak spectral efficiency | Analytical | DL/UL : 30/15 bits/s/Hz | DL/UL : 58.01 bits/s/Hz [Note 2]
3 | User experienced data rate | Analytical for single band and single layer; Simulation for multi-layer | Not applicable for Indoor Hotspot | Not applicable
4 | 5th percentile user spectral efficiency | Simulation | DL/UL : 0.3/0.21 bits/s/Hz | DL/UL : 0.45/0.52 bits/s/Hz [Note 3]
5 | Average spectral efficiency | Simulation | DL/UL : 9/6.75 bits/s/Hz/TRxP | DL/UL : 9.82/13.7 bits/s/Hz/TRxP [Note 3]
6 | Area traffic capacity | Analytical | DL : 10 Mbit/s/m2 | Required DL bandwidth = 170 MHz with 3 TRxP/site. [Note 4]
7 | Mobility | Simulation | UL : 1.5 bits/s/Hz | UL : 9.4 bits/s/Hz
8 | Bandwidth | Inspection | 100 MHz, scalable | 20/40/80/80+80/160 MHz
9 | User plane latency | Analytical | DL/UL : 4 ms | DL/UL : 80 us [Note 5]

## Slide 7
Notes:
Assumes a three carrier configuration: 8x8 HE160 + 8x8 HE160 + 8x8 HE40.
Assumes an 8x8 configuration.
Assumes 2-Factor MU-MIMO without any multi-user scheduling gain.
Some of the 802.11ax configurations that satisfy an Area Traffic Capacity of 10 Mbits/m2 are 8x8HE160 + 8x8HE40 or 8x8HE160 + 8x8HE160. There can be other configurations too.
Assumes the smallest IP packet size without payload as required by 4.7.1 [1] and SIFS delay

## Slide 8: Approval of Draft LS
Motion:
Approve the liaison statement in 11/18/1340r8 from IEEE 802.11 to 3GPP and 3GPP SA TSG and copied to the 802 EC, 802.1, WFA, and WBA, providing the 802.11 study results benchmarking 802.11ax capabilities to meet some performance requirements of IMT-2020, granting the WG chair editorial license.
Moved by Joseph Levy on behalf of AANI SC
  Result in the AANI SC:
  Moved: Andrew Myles
  Seconded: Michael Fischer
  Results: Y/N/A 19/0/0
Note: the red lined version, as modified during the AANI SC session (Monday PM2), of the LS is available in: 11-18/1340r7 (previous version 11-18/1340r5 and 11-18/1340r6 have header errors)

## Slide 9: References