## Slide 1: Beam Tracking Mandatory?
Date: 2019-01-03
Authors:

## Slide 2: Abstract
In this document we examine whether beam tracking should remain mandatory as it is now in the 11md draft, or should we make it or parts of it optional.

## Slide 3: What is DMG beam tracking - TX
RX beam tracking is a procedure (in 11md draft) that allows for requesting an RX training field in the next PPDU using PHY header signalling.
A STA requests RX beam training by setting Beam Tracking Requested to 1, Packet Type to 0 and TRN-LEN>0
TRN field (for RX) is appended to the next PPDU from the peer STA.
The intent is to allow the RX side of the link to adapt antenna pattern around current RX AWV.

## Slide 4: What is DMG beam tracking - TX
DMG TX Beam tracking is a process by which a STA appends a TRN field to a PPDU (without including a BRP frame) and signals that it requests TX training by using the PHY header (Beam Tracking Requested=1, Packet Type=1, TRN-LEN >0.
The responder is expected to send feedback.
It allows the STA to perform TX beam training (when the peer STA uses the same RX pattern used to RX data.

## Slide 5: Recap
In Short, beam tracking allows for some beam forming training, around the current pattern for both TX and RX without interrupting data transmission.
Other applications may be possible.

## Slide 6: Mandatory Today?
It looks like Beam Tracking is mandatory in both RX and TX according to table 10-29.

## Slide 7: Some texts try’s to make “unsupported”
This text in 9.4.2.127.4 claims that if this field is 0, Beam tracking is unsupported.
There is no normative behavior associated with this field – as to making the BF optional – there is plenty of other text that makes Beam Tracking Mandatory.

## Slide 8: This is 11md?
Yes, but we are the experts on DMG, the decision should come from here.
  We can provide a “liaison” to 11md – they will vote on text changes
Are we fixing history?
  In a way, but there ambiguity in the text that need to be fixed.

## Slide 9: Options
Make All beam tracking optional - add a capability field to DMG beamforming.
Make RX tracking mandatory (to transmit the TRN field) but TX tracking optional
  RX tracking is relatively simple
  TX tracking require creating the FB and pushing it inside normal data traffic.
Keep Beam tracking mandatory
  Delete the option of setting Beam Tracking Time Limit to 0

## Slide 10: SP
Do you support:
Option1: Beam Tracking Fully optional
Option2: Beam Tracking Mandatory for RX BT and optional for BT
Option3: Beam Tracking Fully Mandatory

## Slide 11: References