## Slide 1: Potential PHY Designs for NGV
Date: 2019-01-14
Authors:

## Slide 2: Introduction
NGV PAR specifies the goal of achieving 2x throughput and 3dB better sensitivity [1].
WLAN standard has evolved after 11p, adopting many advanced technologies (e.g. LDPC, Midamble, etc) to gain higher throughput and better reliability.
802.11bd can leverage the evolution of the 802.11 technologies to achieve the goal.
In this contribution, we investigate the promising PHY technologies for 802.11bd.

## Slide 3: Candidate PHY Designs
OFDM Numerology
  Leverage mature 802.11ac OFDM numerology to achieve better OFDM efficiency than 11p
FEC Coding: LDPC
  LDPC achieves prominent SNR gain over convolutional codes (BCC)
Midamble
  Midamble is an effective technique adopted in 802.11ax to mitigate Doppler impact.
Higher QAM
  Higher QAM is the low-hanging fruit to boost peak throughput.
NGV 20MHz PPDU
  2x throughput can be achieved by introducing 20MHz PPDU.

## Slide 4: OFDM Numerology
OFDM tone spacing: ∆f
  ∆f >> maximum Doppler frequency fd to guarantee low Inter-carrier-interference (ICI) level [2].
  OFDM symbol duration = 1/∆f.
    The longer symbol duration, better OFDM efficiency is achieved (fixed cyclic prefix (CP) duration)
    But more channel variation from the training symbol will be observed.
OFDM tone plan
  802.11ac OFDM tone plan achieves better OFDM efficiency than 11a.
  For example, SigBW=10MHz, CP=1.6us
OFDM Numerology | NFFT | NSD | Tone spacing | Downclock Ratio | Efficiency
11a/g 20MHz | 64 | 48 | 156.25kHz | 2 | 60%
11ac 20MHz | 64 | 52 | 156.25kHz | 2 | 65%
11ac 40MHz | 128 | 108 | 78.125kHz | 4 | 75%
11ac 80MHz | 256 | 234 | 39.0625kHz | 8 | 86%

## Slide 5: Simulations
Simulation settings
  10MHz DSRC channel
  1x1, 1SS
  11ac LDPC coding
  Midamble: uses VHT-LTF
  Number of data bits: 1000 Bytes
  CFO: uniformly distributed between [-20, 20]ppm
  Ideal timing
  Car2Car Doppler channel model [3]
  11ac OFDM numerology:
    20MHz downclock by 2
    40MHz downclock by 4
    80MHz downclock by 8

## Slide 6: OFDM Numerology: Highway NLOS
In high Doppler channel: 11ac 20MHz DC2 is a good candidate for all MCS with dense Midamble.

## Slide 7: OFDM Numerology: Highway LOS
In medium Doppler channel: 11ac 20MHz DC2 is a good candidate for all MCS with medium Midamble period

## Slide 8: OFDM Numerology: Rural LOS
In low Doppler channel: 11ac 20MHz DC2 is a good candidate for all MCS with sparse Midamble

## Slide 9: FEC Coding
LDPC has been introduced to WiFi since 802.11n.
Prominent coding gain is achieved compared with BCC in 802.11a [4].
It is the low-hanging fruit for 802.11bd to achieve better sensitivity by adopting LDPC codes.
The same LDPC code design as 802.11n/ac can be used.

## Slide 10: Midamble
In 11p, no Doppler mitigation techniques are standardized at the transmitter.
  For applications with short messages (Basic Safety Message(BSM)), the decoder may tolerate low-to-medium Doppler for low MCS.
  Receiver DFE-based tracking can also help in high-Doppler environments, but it is limited due to implementation complexity.
Midamble is a simple and effective technique to address Doppler
  It has been standardized in 802.11ax for outdoor applications.
  The midambles are training symbols that are inserted in-between data symbols for the receiver to update the channel along the packet.

## Slide 11: Midamble Design
In a NGV frame with Midamble,
  the Midamble field can be the same as NGV LTF.
  The midambles are inserted periodically, every M data symbols.
  Channel update based on Midabmles can limit the channel variation/aging of Doppler channel with the Midamble period.
  Midamble period can be determined based on channel Doppler.
M Data Symbols
Preamble
Midamble
M Data Symbols
Midamble
L Data Symbols
…
NGV LTF

## Slide 12: NGV vs 11p: Sensitivity (Highway NLOS)
In high-Doppler channel: NGV can achieve 2.5dB SNR gain with LDPC and Midamble for QPSK-1/2.

## Slide 13: NGV vs 11p: Sensitivity (Highway LOS)
In medium-Doppler channel: NGV can achieve 1.7dB SNR gain with LDPC and Midamble for QPSK-1/2.

## Slide 14: NGV vs 11p: Sensitivity (Rural LOS)
In low-Doppler channel: NGV can achieve 1.5dB dB SNR gain with LDPC and Midamble for QPSK-1/2.

## Slide 15: Higher QAM
Higher than 64 QAM modulation schemes are standardized since 802.11ac.
Higher QAM can simply increase the peak throughput.
With the help of Midamble, channel aging is constrained within each Midamble period. Higher QAM can be supported for NGV.
Higher QAM can offset the efficiency loss due to Midamble airtime.
One good candidate is 802.11ac 256QAM with coding rate ¾.

## Slide 16: NGV vs 11p: Tput (Highway NLOS)
In high-Doppler channel: >2 times peak throughput gain can be achieve with LDPC + Midamble + 256QAM.

## Slide 17: NGV vs 11p: Tput (Highway LOS)
In medium-Doppler channel: 20% peak throughput gain can be achieved with LDPC + Midamble + 256QAM.

## Slide 18: NGV vs 11p: Tput (Rural LOS)
In low-Doppler channel: ~30% peak throughput gain can be achieved with LDPC + Midamble + 256QAM.

## Slide 19: DSRC Channel Usage
802.11p defines signal format for 5MHz, 10MHz and 20MHz BW, by using corresponding downclocked version of 11a 20MHz [5].
FCC designates the usage of the 10MHz DSRC channels [6].
20MHz is not practically used in the fields, and not compatible with 10MHz channels.
Ch. 178:Control Channel: WAVE Service Advertisements
Ch. 172: Collision Avoidance Safety
Ch. 184: Public Safety

## Slide 20: NGV 20MHz PPDU
802.11bd can define a new 20MHz PPDU
  The new 20MHz PPDU occupies two adjacent 10MHz DSRC channels. for example, CH 175 and 181 in US.
    This format can achieve 2x throughput of 10MHz 11p.
  Frame format:
    Legacy portion uses duplicate 10MHz 11p preamble format.
    20MHz NGV data portion can use 11ac 20MHz OFDM numerology or 11ac 40MHz DC2 OFDM numerology, etc.
  Coexist with10MHz DSRC operation, including 11p.
    11p receivers can avoid detecting both 10 and 20MHz preamble for CCA.
    only detect OFDM signal on its own operating 10MHz.
Legacy portion
Legacy portion
20MHz NGV data portion
10MHz
10MHz

## Slide 21: Summary
We investigated several PHY techniques for 802.11bd to achieve the goals set in the PAR.
802.11ac 20MHz OFDM numerology is shown as a good choice for 10MHz DSRC channel for its efficiency and Doppler resilience.
LDPC and Midamble can be adopted in 802.11bd to achieve substantial SNR gains and Doppler mitigation.
256QAM is a good advance of modulation for throughput boost.
NGV 20MHz PPDU is also defined to achieve 2x peak throughput.

## Slide 22: Reference
[1] Bo Sun and etc., “802.11 NGV SG Proposed PAR”, IEEE 802.11-18/0861r9.
[2] Rui Cao and etc., “Doppler Impact on OFDM Numerology for NGV”, 11-18/1553
[3] Hongyuan Zhang and etc. “C2C Channel Model Overview”, 11-18/0858r0
[4] Aleksandar Purkovic, and etc., “LDPC vs Convolutional Codes for 802.11n applications performance comparison”, 11-04/0071r01.
[5] 802.11REVmd, D1.6
[6] John Kenny, “DSRC Application Tutorial”, 11-13/0541r01.

## Slide 23: APPENDIX

## Slide 24: OFDM Numerology: Packet Efficiency
Packet Efficiency = OFDM efficiency * Midamble efficiency
Period 1 2 4 8
20MHz 0.3250 0.4333 0.5200 0.5778
40MHz 0.3750 0.5000 0.6000 0.6667
80MHz 0.4300 0.5733 0.6880 0.7644

## Slide 25: OFDM Numerology: Highway NLOS

## Slide 26: OFDM Numerology: Highway LOS

## Slide 27: OFDM Numerology: Rural LOS

## Slide 28: PER: Highway NLOS
In high-Doppler channel: NGV can achieve 3~5dB dB SNR gain at low MCS, and can support up to 256QAM.

## Slide 29: PER: Highway LOS
In medium-Doppler channel: NGV can achieve 2~5dB dB SNR gain at low MCS with LDPC and Midamble, and support up to 256QAM.

## Slide 30: PER: Rural LOS
In low-Doppler channel: NGV can achieve 2~5dB dB SNR gain with LDPC and Midamble at all MCSs, and support 256QAM.