## Slide 1: Seamless Evolution from DSRC to IEEE NGV
Date: January 14, 2019
Author:

## Slide 2: Outline
Part I: IEEE DSRC to IEEE NGV seamless evolution
Part II: Regulatory status for DSRC in US

## Slide 3: Message from May 2018 – 1st NGV SG meeting … CAUTION – DANGEROUS ROAD AHEAD

## Slide 4
January 2019 update …
NGV SG successfully navigated danger
“Road improvements” are going well
TGbd needs to remain committed to backward compatibility, interoperability, co-existence
TGbd

## Slide 5: IEEE Next Generation V2X (My description to external groups)
Goal:
Update DSRC
Introduce PHY/MAC improvements, new use cases
Preserve value and investment in DSRC
Seamless evolution path
  in contrast to lack of evolution path for non-IEEE technologies

## Slide 6: Evolution: A right way and a wrong way
IEEE NGV will enhance the value of current and near term investments in DSRC
Long term success of DSRC/NGV is tied to widespread deployment of interoperable technology
If not handled correctly, evolution could reduce incentive to deploy any V2X, threatening all of V2X
  Example: if reaching other stakeholders requires deploying multiple, incompatible technologies in a vehicle
  Example: if evolution requires fragmenting the spectrum, and inefficiently duplicating services in multiple fragments
IEEE NGV is committed to evolving the right way, preserving and enhancing the investments in DSRC

## Slide 7: Traditional wireless evolution
11ac STA
11ac STA
11ac AP
Send/receive 11ac/11n/11a
Some control over STAs
4G UE
4G UE
3G UE
2G UE
4G Base Station/eNB
Send/receive 4G/3G/2G
Master
Network backhaul
UE = slave
11n STA
11a STA
Distinct channels
Network backhaul
Same channels
In Cellular or 802.11 evolution, base station/AP mediates across generations
Devices connect to the cloud, seldom to other devices on same local network
Communication is dominated by unicast
One Cellular/802.11 difference: cellular uses distinct channels for generations while 802.11 has same channel co-existence across generations
Cellular Evolution
802.11 Evolution

## Slide 8: Challenges of V2X evolution
V2X is ad hoc, no base station or access point to mediate or translate across generations
Vehicles/Roadside infrastructure have very long lifetimes, ~5 to 10x consumer electronics
Therefore, interoperability is more important than marginal performance
There will always be something “newer and better”.
  “It’s better” is not enough
  We cannot change MAC/PHY technology every few years
OBU
OBU
PED
RSU
OBU
OBU
PED
RSU
X
V2X is this …
Not this …
OBU = onboard unit, RSU = roadside unit, PED = pedestrian/personal unit

## Slide 9: Key: True Backward Compatibility
Same-channel co-existence
  Mutual detection and deferral in CSMA/CA. Implies re-using 802.11p preamble in NGV transmissions for mutual sensing
  Fair sharing. Implies parity for detection sensitivities and channel access priorities
Interoperability-as-needed
  IEEE NGV devices must be able to transmit packets that 802.11p devices can decode, when needed
  IEEE NGV devices can always decode 802.11p transmissions
Note contrast with “system backward compatibility” claimed if a device (system) merely supports multiple protocols in different channels. System backward compatibility tells you nothing about the protocols.

## Slide 10: Interoperability as needed
NGV
DSRC
NGV
NGV
DSRC
DSRC
DSRC
NGV
With DSRC neighbors, broadcast using DSRC
Depending on situation, may also send additional NGV information
  NGV appendix or
  NGV duplicated message
Conditions may include channel load (congestion level)
DSRC
DSRC
DSRC
DSRC
NGV
NGV
NGV
NGV
NGV
NGV
NGV
NGV
NGV
NGV
NGV
NGV
NGV
With only NGV neighbors,
or if unicast to NGV device,
or if industry consensus to use only NGV for a given use case:
Transmit using NGV.
Packet-by-packet decision
Seamless
Evolution
DSRC

## Slide 11: Automotive Liaison Responses
A consistent message from automotive stakeholders
Car2Car Communications Consortium
  “NGV-conformant device must interoperate with IEEE 802.11p devices”
  “NGV transmissions must be detectable … by IEEE 802.11p devices”
  “NGV device must … convey … that it is NGV-capable”
  “NGV amendment can provide a seamless evolution path”
SAE DSRC TC
  “At least one mode of direct interoperability”
  “Same-channel fair co-existence”
  “Capability identification”
  “form the basis for a seamless evolution strategy”
IEEE 1609 WG
  “Interoperability, co-existence, backward compatibility and fairness between legacy devices and NGV devices … should be requirements”
  “form the basis for a seamless evolution strategy”

## Slide 12: Work to do
As we introduce MAC/PHY enhancements …
Maintain
  Same-channel, fair co-existence
  Bi-directional interoperability
    NGV always decodes 802.11p
    NGV transmits in 802.11p decodable form as needed
Provide NGV capability indicator
  Preferably in 802.11bd amendment, second choice is at higher layer
  Extensible to accommodate future generation indications
Provide rules for packet-by-packet transmission
  When to use mode that is decodable by 802.11p?
  Some of these rules will be specified by higher layer profiles (e.g. IEEE 1609, SAE, ETSI, Car2Car Profiles)
  If some rules are universal, then specify in IEEE 802.11bd
  Rule specification may be split among SDOs. Liaisons needed.

## Slide 13: Outline
Part I: IEEE DSRC to IEEE NGV seamless evolution
Part II: Regulatory status for DSRC in US

## Slide 14: US ITS Regulations
FCC regulates spectrum
USDOT/NHTSA may regulate safety
FCC provided service rules in 2003
  Only DSRC can be deployed – regulations are intentionally not neutral
  DSRC is co-primary with FSS and Radar
  Band plan (CFR47 Parts 90 (RSU) and 95 (OBU):
FCC added safety-only Ch. 172/184 restrictions in 2006
FCC started U-NII proceeding in 2013
Reserved
5 MHz
CH
172
V2V
Safety
10
MHz
CH
174
Service
10
MHz
CH
176
Service
10
MHz
CH
178
Control
10
MHz
CH
180
Service
10
MHz
CH
182
Service
10
MHz
CH
184
Public
Safety
10
MHz
5.850 GHz
5.925 GHz
DSRC Spectrum

## Slide 15: U-NII-4 Proceeding
Only remaining open issue from 2013 5 GHz NPRM
802.11 hosted “Tiger Team” 2013-15
Two proposals recognized in 2016 FCC Public Notice:
  Detect and Vacate: Detect DSRC in lower 4 channels, no DSRC rule change
  Re-channelization: changes to DSRC band plan
Three phase test plan
  Phase I lab test results published, comments collected
  Phase II and III outdoor vehicle testing in planning stage with US DOT
Reserved
5 MHz
Non-Safety
20 MHz
CH
180
Safety
10
MHz
CH
182
Safety
10
MHz
CH
184
Safety
10
MHz
5.850 GHz
5.925 GHz
DSRC Spectrum under re-channelization
Non-Safety
20 MHz
CH 173
CH 177
Compress all safety into 3 channels
U-NII-4

## Slide 16: 5GAA Waiver Request
Asks FCC to allow “Cellular V2X” protocol in 5.9 GHz
  3GPP 4G “LTE V2X” to duplicate services supported by DSRC
  Allow in upper 20 MHz of band (5905-5925 MHz)
  DSRC to be prohibited from those 20 MHz
  5GAA will ask for more spectrum for new C-V2X in “near future”
  FCC comments due Jan. 18
5.9 GHz band if waiver granted
Reserved
5 MHz
CH
172
V2V
Safety
10
MHz
CH
174
Service
10
MHz
CH
176
Service
10
MHz
CH
178
Control
10
MHz
CH
180
Service
10
MHz
LTE V2X
(No DSRC)
20
MHz
5.850 GHz
5.925
GHz
Truncated DSRC Spectrum
C-V2X
Spectrum
Reserved
5 MHz
CH
172
V2V
Safety
10
MHz
LTE V2X
(No DSRC)
20 MHz
DSRC
Spectrum
New Radio C-V2X?
(No DSRC?)
20 MHz?
20 MHz?
New Radio C-V2X?
(No DSRC?)
C-V2X Spectrum?
5GAA Request
Now
5GAA Request
“Near Future”?

## Slide 17: U-NII-4/5GAA Conflicts
Clearly conflicts exist between U-NII access to 5.9 GHz and 5GAA request to open ITS licensing to non-DSRC
Reserved
5 MHz
CH
172
V2V
Safety
10
MHz
CH
174
Service
10
MHz
CH
176
Service
10
MHz
CH
178
Control
10
MHz
CH
180
Service
10
MHz
LTE V2X
(No DSRC)
20
MHz
5.850 GHz
5.925
GHz
Truncated DSRC Spectrum
C-V2X
Spectrum
Reserved
5 MHz
CH
172
V2V
Safety
10
MHz
LTE V2X
(No DSRC)
20 MHz
DSRC
Spectrum
New Radio C-V2X?
(No DSRC?)
20 MHz?
20 MHz?
New Radio C-V2X?
(No DSRC?)
C-V2X Spectrum?
5GAA Request
Now
5GAA Request
“Near Future”?
Reserved
5 MHz
Non-Safety
20 MHz
CH
180
Safety
10
MHz
CH
182
Safety
10
MHz
CH
184
Safety
10
MHz
5.850 GHz
5.925 GHz
DSRC Spectrum under re-channelization
Non-Safety
20 MHz
CH 173
CH 177
Compress all safety into 3 channels
U-NII-4

## Slide 18: US DOT V2X RFC
US DOT issued Request for Comments on 9 questions
Comments due Feb. 24 (extended by gov’t shutdown)
Questions are all about having multiple ITS protocols
One perspective (clearly there are others):
  Introducing incompatible non-DSRC protocols creates disincentive to invest in any V2X protocol. Risk collapse of entire V2X ecosystem.
    Band fragmentation
    Spectral inefficiency
    Extra equipment costs
  Disruptive and potentially harmful as an evolution strategy
  IEEE NGV seamless evolution, with same-channel coexistence/interoperability is more attractive
    No band fragmentation
    No spectral inefficiency
    No extra equipment costs

## Slide 19: Conclusion
TGbd scope includes this requirement:
  This amendment shall provide interoperability, coexistence, backward compatibility, and fairness with deployed OCB (Outside the Context of a BSS) devices.
Key auto stakeholders (SAE, IEEE 1609, C2C-CC) say that these principles provide the basis for seamless evolution from DSRC to IEEE NGV
Seamless evolution enhances the incentives to invest in DSRC today and NGV in the future.
Efforts by others to bring a disruptive evolution to the 5.9 GHz band place a spotlight on TGbd amendment
It is critical that TGbd abide by these principles as we produce this amendment