## Slide 1: Drone Use Case Followup
Date: 2018-11-15
Authors:
Notes: Hello everyone. I am Akira Kishida from NTT.
I’d like to introduce my presentation entitled as “Discussion on Target Use Cases of RTA”.
The document number is 1978r0.

## Slide 2: Abstract
This presentation is follow up on our previous presentation concerning RTA use case of drone [1]. The details given in this presentation are described to the RTA Report draft [2].
Notes: This presentation introduces key use cases of RTA for industrial business. That is, Haptic technology and drone control.
In these use cases, high stability is required while required data rate is low. On the other hand, in case of pushing “rich” contents such as video streaming, high data rate is required.
Then, we also discuss use cases that require both low latency and high data rate such as AR/VR, 4K/8K video streaming.
We think that some of real time gaming would be “rich” contents in the near future.
Therefore, we should decide whether high data rate RTA (or Real Time Applications) should be included in the scope of RTA TIG or not.

## Slide 3: Drone control
Drones are widely used in various businesses and entertainment.
  Gartner mentions that worldwide production of drones neared 3 million units in 2017 [3].
  Agriculture, inspection, aerial photography, survey, route guiding, logistics, inventory management, entertainment, e-Sports, digital signage, security for example [4].
Almost commercial drones employ Wi-Fi for their communication method.
  Wi-Fi is universal unlicensed wireless system and can be easily utilized and operated.
Notes: According to the draft of Report of RTA, real-time gaming, robotics and industrial automation are the targets as use cases so far.
These use cases require low data rate and requirements concerning stability such as jitter and packet loss are very important.
Then, we introduce some additional use cases to robotics and industrial automation with similar requirement, that is, Haptic technology and Drone control.
We believe that “Guaranteed” communication might be promising in Wi-Fi systems and will be demanded.

## Slide 4: Examples of drone use cases and requirements
Use cases | Distance | Maximum delay
Inspection from the air | ~ 300 m | ~ 100 ms
Route guiding | ~ 1 km | ~ 100 ms
Logistics (outdoors) | ~ 5 km | ~ 100 ms
Logistics (indoor) | ~ 100 m | ~ 100 ms
Security patrol | ~ 1 km | ~ 100 ms
Gaming device | TBD | TBD
Digital signage | ~ 100 m | TBD
Real-time distribution of images | ~ 100 m | TBD
Given the Wi-Fi capabilities, only use cases with short communication ranges should be considered in the scope of 802.11 and the RTA TIG.
Notes: According to the draft of Report of RTA, real-time gaming, robotics and industrial automation are the targets as use cases so far.
These use cases require low data rate and requirements concerning stability such as jitter and packet loss are very important.
Then, we introduce some additional use cases to robotics and industrial automation with similar requirement, that is, Haptic technology and Drone control.
We believe that “Guaranteed” communication might be promising in Wi-Fi systems and will be demanded.

## Slide 5: Drones for digital signage
Drones can be used for digital signage. These drones running on ground perform public viewing by making a concerted move [5].
  In this case, multiple drones must be controlled at the same time.
Photos by Swarm arena / Ars Electronica Futurelab, https://flic.kr/p/28tPf9k
Notes: According to the draft of Report of RTA, real-time gaming, robotics and industrial automation are the targets as use cases so far.
These use cases require low data rate and requirements concerning stability such as jitter and packet loss are very important.
Then, we introduce some additional use cases to robotics and industrial automation with similar requirement, that is, Haptic technology and Drone control.
We believe that “Guaranteed” communication might be promising in Wi-Fi systems and will be demanded.

## Slide 6: Architecture of drone use case (1)
There are several architectures for drone control.
  Standalone (single drone)
    Most of commercial drones adopt this architecture.
    A drone plays a roll of the AP and a controller (e.g. a smartphone or a console) becomes the STA.
    Only one drone can be managed per a single controller.
Notes: According to the draft of Report of RTA, real-time gaming, robotics and industrial automation are the targets as use cases so far.
These use cases require low data rate and requirements concerning stability such as jitter and packet loss are very important.
Then, we introduce some additional use cases to robotics and industrial automation with similar requirement, that is, Haptic technology and Drone control.
We believe that “Guaranteed” communication might be promising in Wi-Fi systems and will be demanded.

## Slide 7: Architecture of drone use case (2)
  Standalone (multiple drones)
    The drones are desirable to be the STAs and a controller should be the AP.
    Due to sharing a same channel with the multiple drones and the AP, functions that ensure reliability will be needed in this architecture.
Notes: According to the draft of Report of RTA, real-time gaming, robotics and industrial automation are the targets as use cases so far.
These use cases require low data rate and requirements concerning stability such as jitter and packet loss are very important.
Then, we introduce some additional use cases to robotics and industrial automation with similar requirement, that is, Haptic technology and Drone control.
We believe that “Guaranteed” communication might be promising in Wi-Fi systems and will be demanded.

## Slide 8: Architecture of drone use case (3)
  Network control
    The drone has a possibility to become the AP or the STA. However, it is desirable that the drone plays a roll of the AP.
    To control drones over the network remotely, network delay should be considered.
Notes: According to the draft of Report of RTA, real-time gaming, robotics and industrial automation are the targets as use cases so far.
These use cases require low data rate and requirements concerning stability such as jitter and packet loss are very important.
Then, we introduce some additional use cases to robotics and industrial automation with similar requirement, that is, Haptic technology and Drone control.
We believe that “Guaranteed” communication might be promising in Wi-Fi systems and will be demanded.

## Slide 9: Communication functions for drone control
Following functions provided by Wi-Fi should be considered for target use cases of drone.
  Tele control
    Controlling motions and functions of the drone. A few Kbps of data rate is required.
  Data transmission
    Monitoring information from sensors in a drone or information of the status of the drone itself. A few Kbps~Mbps of data rate is required.
  Picture / video transfer
    Transferring recorded pictures or videos by the drone. More than tens of Mbps of data rate is required.
Notes: According to the draft of Report of RTA, real-time gaming, robotics and industrial automation are the targets as use cases so far.
These use cases require low data rate and requirements concerning stability such as jitter and packet loss are very important.
Then, we introduce some additional use cases to robotics and industrial automation with similar requirement, that is, Haptic technology and Drone control.
We believe that “Guaranteed” communication might be promising in Wi-Fi systems and will be demanded.

## Slide 10: Challenges for drone control
Stable operation of drone control
  Tele control is important for stable operation for drone control.
  Although tele control does not require high data rate and strict latency requirements compared to past IEEE 802.11 standards' CSD, loss of tele control might cause unintended motion of drones.
  We have to consider the fact that drone is a moving STA.
Simultaneous transmissions of tele control and video/data transfer
  Coexistence of tele control and high data rate transmission such as video transfer should be considered.
Notes: According to the draft of Report of RTA, real-time gaming, robotics and industrial automation are the targets as use cases so far.
These use cases require low data rate and requirements concerning stability such as jitter and packet loss are very important.
Then, we introduce some additional use cases to robotics and industrial automation with similar requirement, that is, Haptic technology and Drone control.
We believe that “Guaranteed” communication might be promising in Wi-Fi systems and will be demanded.

## Slide 11: Conclusions
We investigated drone use cases and proposes that only use cases with short communication ranges should be target for 802.11 and the RTA.
Several architectures for drone should be considered for each use case.
Increase reliability for tele control is required for drone control
  To solve these issues, Further investigations of potential technical features should be required.
    For example, priority control, separation of control messages and data messages or protection mechanism for control messages.
Notes: Then, we summarize this presentation.
Two additional use cases are introduced. That is, Haptic technology and drone control .
In these use cases, high stability is required while required data rate is low.
Moreover, in case of pushing “rich” contents such as video streaming, high data rate is required.
We should decide whether high data rate RTA (Real Time Applications) should be included in the scope of RTA TIG or not.
Discussions of AR/VR are already in progress in EHT SG.
And some of real-time gaming might require high data rate in the future.

## Slide 12: References
[1] Akira Kishida, et al., “Discussion on Target Use Cases of RTA,” IEEE 802.11-18-1978r4
[2] Kate Meng , et al., “RTA report draft,” IEEE 802.11-18-2009r3
[3] Gartner, “Almost 3 Million Personal and Commercial Drones Will Be Shipped in 2017,” Feburuary 2017.
[4] Impress Corporation, “World Drone Market Report 2017,” December 2016.
[5] SWARM ARENA, https://ars.electronica.art/futurelab/project/swarm-arena/.