## Slide 1: 11az related bits in the Extended Capabilities element
Date: 2019-01-14
Authors:

## Slide 2: Motivation/Background
A set of bits in the context of .11az needs to be added to the Extended Capabilities element
The criteria for a bit to be added to the Extended Capabilities element is “does the ISTA need this information in order to determine if a .11az negotiation should be initiated with the corresponding RSTA?”
In this presentation, we
  Identify the bits that need to be added to Extended Capabilities element

## Slide 3: Terminology
Roles
  Initiator: the implementation is an initiator (ISTA)
  Responder: the implementation is a responder (RSTA)
Ranging from an ISTA’s perspective
  Active: the implementation actively exchanges frames for ranging
  Passive: the implementation only receives/listens
Ranging Mode
  TB
  nTB
  scheduled EDCA (aka FTM): ranging over 2.4, 5 and 60 GHz using scheduled (for burst periods) and EDCA (for gaining access to the media in order to transmit FTM frames)

## Slide 4: Bit(s) in Extended Capabilities element (included in 2.4/5GHz Beacons)
Feature:
Bit-70: [FTM] Responder
  the implementation is a responder only EDCA FTM (2.4/5 GHz)
Bit-71: [FTM] initiator
  the implementation is an initiator only for EDCA FTM (2.4/5 GHz)
Bit-<ANA+1>: nTB Ranging Responder
Bit-<ANA+2>: TB Ranging Responder
Bit <ANA+3>: Secure LTF Support (support for Secure nTB and TB ranging), (.11az D0.6)
Bit-<ANA+4>: TB Passive Ranging Responder (.11az D0.6)
Bit-<ANA+5>: TB Passive Ranging Initiator (.11az D0.6)
Policy:
Bit <ANA+6>: RSTA requires ISTA-to-RSTA LMR – RSTA policy
Bit <ANA+7>: RSTA requires PMF protected IFTMR/IFTM and LMR exchange (TB and nTB)
Color Coding: Existing bits; Proposed bits to be added

## Slide 5: nTB Ranging Responder
The implementation is a non-Trigger Based Ranging Responder
  Supports the role of a Responder for the Range Measurement procedure described in Cl. 11.22.6.4.4

## Slide 6: TB Ranging Responder
The implementation is a Trigger Based Ranging Responder
  Supports the role of a Responder for the Range Measurement procedure described in Cl. 11.22.6.4.3

## Slide 7: Secure TB and nTB Range Measurement
The implementation supports Secure Range Measurement
  Supports the Secure Range Measurement procedures described in Cl. 11.22.6.4.6
  Non-Trigger Based and/or Trigger Based, depending on the setting of nTB Ranging Responder and TB Ranging Responder bits

## Slide 8: RSTA requires ISTA-to-RSTA LMR
This describes RSTA Policy (not capability)
RSTA indicates that it would honor Initial Fine Timing Measurement Request from ISTAs if and only if they were to indicate support for ISTA-to-RSTA LMR capability (in IFTMR)
  Reject/Ignore IFTMR that does not indicate support for ISTA-to-RSTA LMR support
Implicitly indicates that the RSTA is capable of obtaining the ISTA-to-RSTA LMR
  Does it mean that the RSTA is mandated to receive the ISTA-to-RSTA LMR?

## Slide 9: RSTA requires PMF protected IFTMR/IFTM and LMR exchange (TB and nTB)
This is a policy (not capability)
RSTA indicates that would honor Initial Fine Timing Measurement Request from ISTAs if and only if a security context is successfully negotiated between the ISTA and RSTA.
  Security Context is established either by association or PASN
IFTMR/IFTM and LMR exchanges are ‘Integrity Protected’
Can be used with or without ‘Secure TB and nTB Range Measurement’ enabled

## Slide 10: Straw Poll
We support adding the following bits to the Extended Capabilities element:
  nTB Ranging Responder
  TB Ranging Responder
  RSTA requires ISTA-to-RSTA LMR – RSTA policy
  RSTA requires PMF protected IFTMR/IFTM and LMR exchange (TB and nTB)
Y: N: Abstain:

## Slide 11: Backup