## Slide 1: How to simplify MAC simulations in TGbb
Date: 2019-01-16
Author:

## Slide 2
This presentation aims at making progress with the evaluation methodology in TGbb.
Abstract

## Slide 3
How would Wi-Fi MAC perform over a LC PHY?
What about hidden terminal problem, initial access, role of RTS/CTS, role of directional LC channels?
How do classical OBSS handover and interference management for Wi-Fi would compare against more modern schemes, such as defined in 11ai or more advanced assumptions made in the distributed MU MIMO approach currently developed in 802.15.13?
Should we evaluate all of them in TGbb following a new evaluation methodology?
Answering these basic questions may take years
Typical questions on Wi-Fi MAC layer performance over LC

## Slide 4
In doc. 11-18/1429r0-r4, TGbb discussed an individual contribution made by the Chair developed out of a similar document developed by TGax
In a straw poll made in Sept 2018 [1], the group indicated this is not the right starting point for TGbb methodology
This opinion of the group was ignored and the Chair came up with further iterations of the same text which resulted in further discussions where it seems no consensus is found
The situation should be improved, i.e. the valuable agenda time should be used for the discussion of technical proposals and consensus building among group members
What is our problem with the evaluation methodology in TGbb?

## Slide 5
Most LC channels are modeled fair enough as pure LOS
TGbb has already accepted an analytical channel and blocking model that greatly simplified the simulation of dynamic LC channels in mobile scenarios [2]
Let’s make a simplifying assumption also for the PHY
If the channel is assumed LOS only, the existing Wi-Fi PHYs could just be reused
Simplified channel, no multipath  flat fading model is valid
The concept of bit-interleaved coded modulation so far used in all the Wi-Fi PHYs will work very well also for LC
Suggested way forward

## Slide 6: How to reuse existing Wi-Fi PHYs for LC
Look at home networking standards, like ITU-T G.hn [3]
Coax-, power- and phone-lines need a real-valued channel
TGbb will use it the same way for LC
Take a complex-valued OFDM signal from any Wi-Fi PHY
Use digital up-conversion and move the signal on an upshift- frequency FUS = B/2 where B is e.g. 20, 40, 80, 160 MHz
Use the real value of resulting waveform  We are done!
Re(.)

## Slide 7: What is the value of this approach?
Any existing Wi-Fi PHY will work properly over the analytical system-level channel model defined in TGbb
Any existing evaluation framework for 802.11 MAC will provide useful results also over LC channels
TGbb could reuse existing system-level simulators for 802.11 and test the performance immediately over LC
TGbb does not need a new evaluation framework for the MAC and can focus on its own core business
This is building a new PHY that is optimized for LC!
This new PHY should properly address particular effects of LC frontends, non-linear LEDs, optical NLOS channels etc.

## Slide 8: Motion
Delete the content on system-level simulation methodology in doc. 11-18/1429r4 and focus this document on evaluation methodology for the new PHY to be defined in TGbb.
Moved by Volker
Seconded by
Y/N/A = _/_/_

## Slide 9
References
[1] https://mentor.ieee.org/802.11/dcn/18/11-18-1602-03-00bb-tgbb-meeting-minutes-for-september-2018.docx
[2] https://mentor.ieee.org/802.11/dcn/18/11-18-2037-01-00bb-analytical-channel-and-blockage-model.docx
[3] ITU-T recommendation G. 9660-2015