## Slide 1
CID 16444 and 15178 discussion--Why 11ax should maintain current data channel access rules on 6GHz
Date: 2019-01-15
Authors:
Name | Affliation | Address | Phone | Email
Guoqing Li | Apple |  |  | Guoqing_li@apple.com
Jarkko Kneck |  |  |  | 
Chris Hartman |  |  |  | 
Yong Liu |  |  |  | 
Qi Wang |  |  |  | 
Laurent | Intel |  |  | 
Robert Stacey |  |  |  | 
Thomas Derham | Broadcom |  |  | 
Tomo Adachi | Toshiba |  |  | 
Saishankar Nandagopalan | Cypreess |  |  | 
Sean Coffey | RealTek |  |  | 
James Yee | MediaTek |  |  | 
Baron Stehphane | Cannon |  |  | 
Biger Pascal |  |  |  | 

## Slide 2: Overview
In recent meetings, several contributions have been proposed regarding data channel access rules for 6GHz with somewhat similar principle: add more restrictions/disable STA’s EDCA usage on 6GHz and mostly rely on AP’s scheduling for data access
  18/1471r0
  18/1827r1
  18/1828r2
This contribution provides a different view from the contributions above, and discuss why more EDCA restricting is not the right choice for 11ax on 6GHz
In the rest of the slides, we use UL OFDMA as an example of UL MU

## Slide 3: Considerations
Here, we want to discuss several aspects
  Multi-radio multi-protocol coexistence
  Diverse set of performance metrics for future devices
  “Fear of medium pollution”

## Slide 4: Coexistence Issues with UL MU
UL OFDMA is a very different transmission mode from legacy transmission mode in several ways:
  Tx power is controlled by AP
  # of STS (Tx antennas) is controlled by AP
  MCS is controlled by AP
  Start of Tx is controlled by AP
  Duration of Tx is controlled by AP
    Padding is needed if there is not enough data
  Mandatory response to trigger frame even if there is no real data from the device
As pointed out in 16/0657r0, without control over these aspects, the STA loses much of its flexibility to cope with various coex conditions

## Slide 5: Coexistence Issues with UL MU(cont.)
In some conditions, the STA cannot conform to the requirements of UL OFDMA, and it is better to let the device to operate in SU transmission mode
  When the coex conditions go away the device can get back to the UL MU operation
Therefore, we should still allow UL MU Disable to be used in such cases
As devices and applications are getting more complicated in future, the multi-radio multi-protocol coex scenarios will only get more complex
Putting the device in a single operation mode, which is fully controlled by AP, strips away the freedom and flexibility it has today to manage the various conditions that are only known to the device, not the AP

## Slide 6: A Diverse Set of Performance Metrics Need to be Considered
Throughput and spectrum efficiency are certainly important design criteria, which is the driving factor for no//limited-EDCA principle
However, the success of Wi-Fi depends not only on network efficiency, but also on the success of the client devices in a diverse set of performance metrics
For example, stability, power, latency and jitter are all important performance metrics for devices, and UL OFDMA may not result in the optimal performance in all the KPI metrics in all operating cases
Therefore, putting the device in a single mode, a purely scheduled access in a brute force way, adds extreme high risks to device performance, which will jeopardize the success of Wi-Fi in 6GHz

## Slide 7: “Fear of Medium Pollution”
The design philosophy of “no EDCA on 6GHz’ starts with the assumption that 6GHz is a greenfield and we should eliminate congestions from individual STAs to make it as clean as possible
In general, we agree with this philosophy. However, 6GHz is expected to be a much cleaner spectrum than 2.4/5GHz with the existing 11ax spec
  IEEE spec eliminates legacy devices on 6GHz, so pretty much all devices are UL OFDMA capable
  Furthermore, the group has adopted lots of restrictions to probe request/response in the medium
There are already many tools in 11ax spec to allow AP to reach the optimal mode even with the presence of some SU users such as EDCA parameters , MU EDCA parameters and higher trigger frame access rules
We believe that with existing tools and the scanning rule improvement and 11ax being mandatory on 6GHz, we do not need to take a radical throughput-only-driven approach for future Wi-Fi design

## Slide 8: Recommendation
We recommend 11ax spec does not change data channel access rules in 6GHz