## Slide 1: MAC Service Updates for NGV
Date: 2019-05-07
Authors:

## Slide 2: Abstract
The V2X protocol stacks perform several functions that are normally within the 802.11 MAC at higher layers. Furthermore, the rules that these functions must follow differ between the various, regional V2X standards (SAE, ETSI, etc.). NGV must provide a means by which these higher layers can provide the necessary control information downward and receive the necessary status information upward. This is most easily accomplished by modifying the MAC SAP to add NGV-specific parameters to the MAC data service primitives. This cannot be accomplished via the MLME SAP because there is no way to synchronize between primitives at the two SAPs.

## Slide 3: Introduction
IEEE 802.11p is used as the access layer of several V2X regional standards such as ITS-G5 in Europe or SAE in the US. IEEE 802.11bd needs to be an enhancement to this access layer.
On top of the IEEE 802.11-based access layer, regional standards define a set of rules for decentralized congestion control (DCC), packet generation and dissemination.
  Many of the specific rules differ between the various regional standards
TGbd exists to standardize the PHY and MAC layers, collectively referred to as the “access layer”, as an enhancement to IEEE 802.11p.
  It is necessary for TGbd to an appropriate interface to the higher ITS layers

## Slide 4: What 802.11bd Needs to Provide to Upper Layers
802.11bd needs to be a standard with a number of parameters and encoding options, providing a toolbox that can support a wide range of regional deployment configurations.
  For instance ITS-G5 requires IEEE 802.11p PPDUs to be encoded with QPSK ½ (6 Mb/s transmit rate), whereas SAE adjusts the data rate based on congestion level
  For instance in ITS-G5 the CAM message generation is triggered by the vehicle dynamics (“enough” change in location, headings or speed) while SAE transmissions have often a more periodic nature (often transmitted at 10 Hz)
Today, 802.11 does not provide a means by which higher layers can control things such as data rate/format (MCS) on an MPDU-by-MPDU basis.

## Slide 5: Providing Access to the NGV Toolbox
The most appropriate means by which to provide higher layers with access to this “NGV Toolbox” is by extending the MAC Data Service.
  The MLME SAP is not appropriate because it has no sense of time, and it is not possible to synchronize the effects of primitives at the MLME SAP with those at the MAC SAP.
  Creation of a new SAP would be possible, but is much more complex and does not appear to provide any advantages.
  Leaving this issue to solutions outside of the standard is almost certain to result in “no” votes at SA ballot (and, perhaps letter ballot).

## Slide 6: Extending the MAC Data Service Primitives
The best way to extend MAC Data Service is to define a new, NGV-specific parameter to each of the MAC Data Service primitives:
  MA-UNITDATA.request (source address, destination address, routing information, data, priority, service class, V2X request vector)
  MA-UNITDATA.indication (source address, destination address, routing information, data, reception status, priority, service class, V2X status vector)
  MA-UNITDATA-STATUS.indication (source address, destination address, transmission status, provided priority, provided service class, V2X status vector)
A V2X vector parameter shall be present at NGV stations and absent otherwise.
  By defining the new parameter as a vector, and describing the elements of these vectors in separate sub-clauses, the editorial impact on existing clause 5 text is minimized.

## Slide 7: V2X Request Vector Contents
The V2X Request Vector allows the higher layers to control the format and encoding of the 802.11bd transmission
The elements of the V2X Request Vector include:
  Transmission format (data rate/MCS
  Additional coding options (CC, LDPC, etc.)
  Additional spatial stream options (MIMO, STBC, etc.)
  Aggregation permitted
  PHY options (channel, power level, etc.)
  … whatever else needs to be controlled under the final set of NGV MAC and PHY options)
A value that permits selection within the MAC will exist for each element

## Slide 8: V2X Status Vector Contents
The V2X Status Vector allows the higher layers to control the format and encoding of the 802.11bd transmission
The elements of the V2X Status Vector include:
  Transmission format used (data rate/MCS)
  Additional coding options used (CC, LDPC, etc.)
  Additional spatial stream options used (MIMO, STBC, etc.)
  MSDU was part of an aggregate
  Channel Busy Percentage (CBR/CBP)
  TechPercentage (see 11/19-0082)
  Number of stations detected during measurement of Channel Busy and TechPercentage

## Slide 9: V2X MLME SAP Extension
IEEE 1609.4 includes a set of primitives extending the MLME_SAP. These appear as MLMEX-primitives in Clause 7 of IEEE 1609.4-2016
  As a minimum, the MLME_SAP in 802.11bd needs to include a generic means for the MAC at an NGV station to accept these sorts of primitives.
  It is unclear whether it is appropriate (or desirable) to include the full set of MLMEX primitives in 802.11bd
    The exact set of extensions required vary with regional ITS standards
    The behaviors of the various regional MLME extensions should probably remain in the higher-layer standards documents, rather than having redundant definitions in documents that are maintained by different organizations, and are updated according to different schedules
    Defining the full set of MLMEX primitives will also necessitate adding quite a bit of normative text elsewhere in the MAC that may complicate and/or delay the work of TGbd

## Slide 10: V2X Parameters in MIB
Some of the NGV-specific parameters are (generally) static, and can be managed via the MLME SAP rather than the V2X vector. These include:
  NGV activation (the NGV equivalent of dot11OCBactivated)
  NGV capability
  NGV bands supported
  Period over which to measure Channel Busy Percentage and TechPercentage (see 11-19/0082, default value one second)
  OperationalRateSet (already present)