## Slide 1: 11bd Frame Format
Date: 2019-03-11
Authors:

## Slide 2: Introduction
In this contribution, we will discuss the coexistence and backward compatibility from PPDU format perspective.
We propose the preamble design for 11bd PPDU for each 10MHz bandwidth.
We also extend that to 20MHz signal bandwidth.

## Slide 3: Coexistence and Backward Compatibility
In 11bd PAR [1], it states that,
  “This amendment shall provide interoperability, coexistence, backward compatibility, and fairness with deployed OCB (Outside the Context of a BSS) devices.”
11bd devices shall be able to decode 11p PPDU operating in the same channel.
11p devices can reliably detect the preamble of 11bd PPDU to correctly defer its transmission within the packet duration.

## Slide 4: 11p PPDU
11p adopts 11a PPDU format.
Receiver recovers timing with LSTF, and obtains channel estimation on LLTF.
PPDU duration is obtained in the LENGTH field in LSIG, and it is used to determine CSMA backoff.
LLTF
DATA
LSTF
LSIG

## Slide 5: 10MHz 11bd PPDU
Propose 10MHz 11bd PPDU to pre-append legacy preamble fields,
  including LSTF + LLTF + LSIG
  LSIG LENGTH field is set to signal the entire 11bd PPDU duration.
  Coexistence and backward compatibility with 10MHz DSRC operation, including 11p.
    11p receivers will be able to detect the LSIG LENGTH field for CCA.
NGV Portion
10MHz
L-LTF
L-STF
L-SIG

## Slide 6: 20MHz 11bd PPDU
As discussed in [2, 3], 20MHz 11bd PPDU can achieve 2x throughput compared to 11p 10MHz DSRC operation.
Propose to duplicate 10MHz legacy preamble in the two 10MHz sub-channels.
  Can achieve coexistence and backward compatibility with 11p 10MHz DSRC operation.
  11p receiver only needs to detect 10MHz preamble and OFDM signal on its operating channel for CCA.
Propose to use the same tone spacing in NGV portion as in 10MHz 11bd PPDU.
NGV portion
10MHz
10MHz
L-LTF
L-STF
L-SIG
L-LTF
L-STF
L-SIG

## Slide 7: Summary
In this contribution, we propose to pre-append 10MHz 11p preamble to 11bd PPDU.
This design can achieve good coexistence and backward compatibility with 11p 10MHz DSRC operation.
We also discussed 20MHz 11bd PPDU design, and duplicated 10MHz 11p preamble is suggested.

## Slide 8: Reference
[1] Bo Sun and etc., “802.11 NGV SG Proposed PAR”, IEEE 802.11-18/0861r9.
[2] Rui Cao and etc., “Potential PHY Designs for NGV”, IEEE 802.11-19/0016r0.
[3] Dongguk Lim and etc., “Consideration on Features for 11bd”, 802.11-19/0009r0.

## Slide 9: Straw Poll 1
Do you agree to add the following text into Section 3 of SFD?
“A NGV PPDU in 10MHz bandwidth is composed by a legacy portion and a NGV portion, where the legacy portion is composed by L-STF, L-LTF and L-SIG fields, as shown in the figure below.”
Y:
N:
A:
NGV Portion
10MHz
L-LTF
L-STF
L-SIG

## Slide 10: Straw Poll 2
Do you agree that 11bd shall define 20MHz PPDU?
Y:
N:
A:

## Slide 11: Straw Poll 3
Do you agree to add the following text into Section 3 of SFD?
“An NGV PPDU in 20MHz bandwidth has the same tone spacing as an NGV PPDU in 10MHz bandwidth, and its legacy portion is composed by duplicated legacy portion of NGV PPDUs with 10MHz bandwidth, as shown in the figure below”
Y:
N:
A:
NGV portion
10MHz
10MHz
L-LTF
L-STF
L-SIG
L-LTF
L-STF
L-SIG