## Slide 1: Consideration on HARQ
Date: 2019-03-11
Authors:
Name | Affiliation | Address | Phone | Email
Jinmin Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | jinmin1230.kim@lge.com
Taewon Song |  |  |  | taewon.song@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
In last meeting, many contributions show the benefits and higher performance of HARQ
  Goodput is used as a major performance metric for comparison between HARQ & ARQ
We also think it is clear that HARQ can enhance EHT performance in respect of throughput and quality of user experience
In this contribution, we simulate with more details and share consideration points based on our simulation results

## Slide 3: HARQ Issues
So far, several issues regarding HARQ were raised as follows:
  Link adaptation method
  Effect of preamble detection error
  HARQ method
    Chase combining
    Incremental redundancy
  Frequency diversity
  Number of retransmission
  Contaminated LLR caused by collision
We will deal with these issues except collision issue in this contribution
  We haven’t decided the collision scenario yet and need more study for this problem
    Actually, the performance in collision case depends on the scenario(e.g. how many collision occurs, how strong interference is, how many interferers are, etc.)

## Slide 4: Simulation Assumptions
Simulation assumptions
  802.11ax, 20 MHz, Regular GI, 4x HE-LTF, TGnD channel
  SISO, BCC, MCS 0~7
    Optimal / sub-optimal selection for best goodput
    Goodput = total number of correctly decoded data bits / total air time
      For total air time, PHY and MAC overhead is considered (PHY preamble, back-off, IFS, ACK)
  Packet length = 1000 bytes, Single MPDU per PPDU
  Up to 2 or 4 (re)transmissions
  Same channel realization is applied across all (re)transmissions
  No impairments, ideal Channel Estimation, ideal ACK/NACK feedback

## Slide 5: Link adaptation
Based on our simulation results, the gain from HARQ is dependent on link adaptation method
For the performance comparison, we use 2 types of link adaptation
  Optimal MCS selection: select MCS for maximizing goodput
  Sub-optimal MCS selection: select MCS with <10% PER and highest goodput based on long-term SNR measurement
    Since Wi-Fi system is not easy to report and utilize instantaneous CSI feedback in real environment, we think long-term SNR measurement is more practical than short-term measurement

## Slide 6
  In optimal selection case, HARQ shows better performance over entire SNR range
  In sub-optimal selection case,
    ARQ shows step curve due to MCS change at specific SNR region
      At the SNR region where <10%PER is satisfied, a new MCS is applied and this leads to a large increase of goodput performance
    HARQ shows < 4dB gain and has smoother curve. It means HARQ enables sophisticated link adaptation without additional MCS definition
Optimal MCS selection
(w/o overhead)
Sub-optimal MCS selection
(w/o overhead)
56% Tput gain@5dB
1.2dB SNR gain
4dB SNR gain
Simulation parameter
BCC IR for HARQ
Preamble error is considered
Frequency diversity scheme is applied

## Slide 7: Effect of Preamble Detection Error
We simulate how much performance degradation occurs when preamble detection error is considered
  In our simulation, if there is an error of either L-SIG or HE-SIG, received packet is not combined with previous packet with correctly decoded L-SIG and HE-SIG.
Results:
  Performance degradation occurs only in low SNR range
  Moreover, HARQ still shows better performance than ARQ even in low SNR range
  The same trend is also observed in the sub-optimal MCS selection case
1dB SNR gap
Zoom in
Simulation parameter
BCC IR for HARQ
Overhead is not considered
Frequency diversity scheme is applied
Optimal MCS selection

## Slide 8: HARQ Method
CC(Chase combining)
  Chase combining is easily implemented regardless of channel coding method.
IR(Incremental redundancy)
  Generally, IR has higher performance gain than CC
  However, there are some issues depending on coding method
  For BCC,
    Using different puncturing pattern in each reTX can be considered to make new parity bits.[1] And, we also use this method in this contribution
  For LDPC,
    Aggressive puncturing method [2]
    Re-design of the LDPC code [3]
We simulate CC & IR only in BCC and share our observation in the next page
  Regarding IR in LDPC, we need more time to investigate in respect of performance, HW complexity and drafting work.

## Slide 9
In respect of PER,
  IR has better performance than CC except MCS 0, 1 and 3(CR= ½)
    MCS 0, 1 and 3 has exactly same performance between CC and IR
    Since mother coderate of BCC is ½, there is no chance to use different puncturing pattern in MCS0, 1 and 3
Dot line: CC
Solid line: IR
In respect of goodput,
  Without considering PHY&MAC overhead, HARQ IR shows slightly better performance.(see Appendix 1)
  However, considering overhead, CC & IR have almost same performance.
    Performance gains from PER & reduced number of reTX are not enough to represent goodput gain graphically
- With PHY&MAC overhead
- Sub-optimal MCS selection
So, we need to consider how to enhance IR performance

## Slide 10: Frequency diversity
Frequency diversity using different interleaving in each retransmission brings more gains in respect of PER & goodput
  It can be implemented without significantly increasing HW complexity
So, we think it is desirable to use frequency diversity scheme when we introduce HARQ into Wi-Fi
Dot line: w/o Freq. DIV
Solid line: w/ Freq. DIV
Simulation parameter
BCC IR for HARQ
Up to 2 (re)TXs
Overhead is considered
Sub-optimal MCS

## Slide 11: How many reTX is required?
Even if multiple reTXs enhance the PER performance, a total of 2 TXs are enough to achieve reasonable goodput performance
  Multiple reTXs also increase PHY & MAC overhead
Also, based on other scenario results (see Appendix 2), we can figure out that multiple reTXs don’t bring good enough performance
So, the maximum number of retransmission should be carefully considered with following points
  Goodput/PER performance, HW complexity, air-time occupancy, power saving, etc.
Dot line: 2TXs
Solid line: 4TXs
Simulation parameter
BCC IR for HARQ
Up to 2/4 (re)TXs
Overhead is considered
Optimal MCS

## Slide 12: Summary
We simulate HARQ scheme with more details and share our results
  HARQ can show better & smoother curve in goodput performance than ARQ. It enable sophisticated link adaptation without additional MCS definition.
    Depending on link adaptation method or simulation parameters, the gain can be increased.
  HARQ shows better performance even if we consider preamble detection error
  Further study is necessary to improve the performance of IR in BCC
  It is desirable to use frequency diversity scheme in HARQ
  The number of retransmissions should be carefully considered

## Slide 13: References
[1] 11-19-0070-00-0eht-hybrid-arq-in-collision-free-and-collision-dominated-environments
[2] 11-18-1955-00-0eht-harq-for-eht-further-information
[3] 11-18-2031-00-0eht-harq-gain-studies

## Slide 14: Appendix 1
Comparison CC & IR performance
  PHY&MAC overhead is not considered
Simulation parameter
BCC CC/IR for HARQ
Up to 4 (re)TXs
Overhead is not considered
Sub-optimal MCS

## Slide 15: Appendix 2-1
Comparison between 2TXs and 4TXs in sub-optimal MCS selection case
Performance is almost the same except specific region
Simulation parameter
BCC IR for HARQ
Up to 2/4 (re)TXs
Overhead is considered
Sub-optimal MCS

## Slide 16: Appendix 2-2
In iid channel scenario, the IR up to 4 TXs show slightly better performance in both optimal & sub-optimal MCS selection case
Simulation parameter
BCC IR for HARQ
Up to 2/4 (re)TXs
Overhead is considered
Optimal MCS
Simulation parameter
BCC IR for HARQ
Up to 2/4 (re)TXs
Overhead is considered
Sub-optimal MCS