## Slide 1: MAC Architectures for EHT Multi-band Operation
Date: 2019-03-12
Authors:

## Slide 2: Introduction
Multi-band Operation
  One of candidate features discussed in EHT TIG/SG
  Traffic steering, single association/authentication state, multi-band aggregation, etc. (Appendix)
In this presentation,
  We classify the potential architectures : Independent MAC, Distributed MAC, Unified MAC
  Review operations that can be supported by these architectures

## Slide 3: Independent MAC
Independent MAC-SAP, association state, MLME, data plane
Asynchronous transmission
Upper layer link aggregation (e.g. 802.1AX-2014) for load balancing and traffic steering
Non-transparent FST [7]

## Slide 4: Distributed MAC
Single MAC-SAP, authentication
Shared management info, sequence counter, PN counter, etc.
Independent per-band queueing
Single association state, Data/MGMT split (e.g. idle mode in band A/active mode in band B, update system information in band A only, etc.)
Transparent FST [7]

## Slide 5: Unified MAC
Single MLME and MAC Sublayer
Unified queueing
Synchronous transmission, MAC retransmissions on other bands, buffer status/ CCA status indications of band A on band B

## Slide 6: Summary
Independent MAC, Distributed MAC, Unified MAC
  Multi-band operation features supported varies among the architectures
Encourage discussion:
  EHT multi-band device reference model to assist technical contributions on multi-band operation

## Slide 7: References
[1] 11-18/1184r1, “Follow up discussions on Throughput Enhancement”
[2] 11-18/1518r0, “EHT Multi-Channel Operation”
[3] 11-18/1525r1, “EHT features for Multi-Band Operation”
[4] 11-18/1155r1, “Multi-AP Enhancement and Multi-Band Operations”
[5] 11-18/1908r0, “Overview of Full Duplex over Multi-Band for EHT”
[6] 11-19/108r1, “Discussion on Multi-Band for EHT”
[7] IEEE Standard 802.11™-2016

## Slide 8: Appendix
EHT multi-band operation discussed features [1,2,3,4,5,6]
  Asynchronous transmission
  Traffic steering (e.g. AC_VO on band A and AC_BE on band B)
  FDD (e.g. DL MSDU on band A/ UL MSDU on band B)
  Single association state/authentication state across the bands
  Data/MGMT split (e.g. idle mode in band A, active mode in band B, update system information in band A only, etc.)
  Synchronous transmission
  MAC retransmissions on other bands
  Buffer Status/ CCA status reporting of band A on band B
  Dynamic MPDU duplication for real-time application robustness/latency