## Slide 1: 20MHz Channel Access in 11bd
Date: 2019-03-11
Authors:
Name | Affiliation | Address | Phone | Email
Insun Jang | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | insun.jang@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com

## Slide 2: Introduction
In the last meeting, we discussed the transmission of 10MHz / 20MHz PPDU for 11bd STAs to increase the throughput [1], [2]
To transmit 20MHz PPDU, 11bd STAs have to be able to access a 20MHz channel
At this point, the first thing we have to consider is how 11bd STAs should access the 20MHz channel (at the level of MAC), which is discussed in this contribution

## Slide 3: Supported Bandwidth Capability
11bd STAs may be capable of accessing a 10MHz channel or a 20MHz channel (i.e., 10MHz or 20MHz supported BW capability)
In case of 10MHz capability, 11bd STAs can just exchange 10MHz PPDUs by sensing and accessing a 10MHz channel (like 11p)
In case of 20MHz capability, 11bd STAs can have a primary channel with 10MHz that they operate in common
  In legacy system using wide bandwidth (e.g., 11n/ac/ax), the concept of primary channel has been introduced, e.g., 20MHz primary channel for 40MHz bandwidth in 11n
  Therefore, it would be proper to introduce a 10MHz primary channel for 20MHz bandwidth even in 11bd

## Slide 4: 10MHz Primary Channel in 11bd
11bd STAs first sense and access a 10MHz Primary Channel
  We can follow back-off rules for 10MHz of 11p without modifications
Transmission
  To extend to 20MHz and transmit 20MHz 11bd PPDU, we could follow the original dynamic bandwidth operation (used in 11n/ac/ax)
  Specifically, if the non-primary channel (called secondary channel) were idle during an interval PIFS when the back-off count becomes zero, 20MHz 11bd PPDU can be transmitted. If not (i.e., busy), 10MHz 11bd PPDU can be transmitted
Reception
  11bd STAs can receive 10MHz or 20MHz 11bd PPDU using the signaling information (e.g., BW, MCS) decoded through the 10MHz primary channel

## Slide 5: Discussion
  11p STAs can recognize and access a service channel instructed from higher layer (e.g., IEEE 1609.4). Likewise, 11bd STAs can identify the service channel
  However, 11bd STAs cannot identify which channel is the primary channel
  11p doesn’t have the concept of primary channel and any signaling for this
  In legacy system using wide bandwidth (e.g., 11n/ac), the primary channel index is indicated in Beacon frame but there is no concept of Beacon transmission in OCB mode
Therefore, we propose a rule that which channels should be a primary channel and a non-primary channel for 20MHz

## Slide 6: Selection Rule of Primary Channel
  Current DSRC spectrum has been providing available 20MHz channels (i.e., channel 175/181) consisting of two 10MHz channels
  Therefore, if 11bd STAs set the instructed 10MHz service channel to the primary channel, the adjacent 10MHz channel (in the common 20MHz channel) can be considered as the non-primary channel
  For example, for 20MHz channel 175, if an 11bd STA operates on channel 174 as the service channel, channel 174 and 176 are considered as the primary channel and non-primary channel, respectively

## Slide 7: Selection Rule of Primary Channel (Cont’d)
  Proposed rule for setting the primary channel:
  11bd STAs with 20MHz Bandwidth Capability sets the 10MHz primary channel by the 10MHz service channel (e.g., dot11CurrentFrequency in baseline spec) instructed from higher layer
  The rule doesn’t require any signaling overhead between 11bd STAs for setting the primary channel
  The rule enables to communicate between 11bd STAs that receives a common service without any problems

## Slide 8: Summary
In this contribution, we have discussed the 20MHz channel access in 11bd and observed that 10MHz primary channel is needed to transmit 20MHz 11bd PPDU
Since 11bd applies the concept of primary channel which does not exist in 11p, we proposed a rule for setting the primary channel

## Slide 9: SP #1
Do you agree to introduce the concept of 10MHz primary channel for 20MHz channel access in 11bd
Y/N/A

## Slide 10: SP #2
Do you agree to define the following rule for setting the primary channel
  Rule: 11bd STAs with 20MHz Bandwidth Capability sets the 10MHz primary channel by the 10MHz service channel (e.g., dot11CurrentFrequency in baseline spec) instructed from higher layer
Y/N/A

## Slide 11: References
[1] 802.11-19/0009r0 Consideration on Features for 11bd
[2] 802.11-19/0016r0 Potential PHY Designs for NGV