## Slide 1: Low latency streaming capability for game applications
Date: 2019-03-12
Name | Affiliation | Address | Phone | Email
Kazuyuki Sakoda | Sony | 1730 N. First Street, San Jose CA 95112 |  | kazuyuki.sakoda(at)sony.com
William Carney | Sony |  |  | William.Carney(at)sony.com

## Slide 2: Introduction
RTA TIG walked through low latency applications
Game is a primary application of RTA
At this point in time, most of the game application focus on command transmission between game client and game server [1][2]
However there are growing interest in “Video streaming for games” in the game industry [3]
This presentation explains what the “Video streaming for games” is and expected KPI for the application

## Slide 3: Recap: Real-time mobile gaming [1], [4]
Abstract model of the Real-time Mobile Gaming is as follows:
Game server generate commands to Game Client
Game Client renders picture based on the commands from the Game Server
Game Client sends back commands from the game user to the Game Sever
Game Server
AP
Internet
Game Client

## Slide 4: Recap: Real-time mobile gaming [1], [3]
Abstract model of the Real-time Mobile Gaming is as follows:
Game Server
AP
Internet
Game Client
Latency: < 10msec
Latency: < 10msec
Total Bandwidth: 100kbps~1Mbps
E2E latency: < 100msec

## Slide 5: Cloud stream gaming
This is a variant of the cloud gaming
Game console itself is located on the cloud (Game Server), and the video pictures are streamed to Game Clients
Currently requires >5Mbps @720p HD with compression
Requirements for 802.11 should consider higher quality video and eventual migration to UHD
Required forward link bandwidth > 160Mbps [4]
Game Server
AP
Internet
Game Client

## Slide 6: Cloud stream gaming
This is a variant of the cloud gaming
Game console itself is located on the cloud (Game Server), and the video pictures are streamed to Game Clients
Currently requires >5Mbps @720p HD with compression
Requirements for 802.11 should consider higher quality video and eventual migration to UHD
Required forward link bandwidth > 160Mbps [4]
Game Server
AP
Internet
Game Client
Bandwidth: >160Mbps
E2E latency: < 100msec
Latency: < 10msec
Latency: < 10msec

## Slide 7: Remote play gaming
This is another type of wireless gaming, variant of the cloud streaming leveraging video streaming
Remote game console hosts the game and contents are streamed to Game Clients
Currently requires >5Mbps @720p HD
Requirements for 802.11 should consider higher quality video and eventual migration to UHD
Game Console
AP
Internet
Game Client
AP

## Slide 8: Remote play gaming
This is another type of wireless gaming, variant of the cloud streaming leveraging video streaming
Remote game console hosts the game and contents are streamed to Game Clients
Currently requires >5Mbps @720p HD
Requirements for 802.11 should consider higher quality video and eventual migration to UHD
Game Console
AP
Internet
Game Client
Latency: < 10msec
Latency: < 10msec
AP
Latency: < 10msec
Latency: < 10msec
Bandwidth: >160Mbps
E2E Latency: < 100msec
Bandwidth: ~100kbps
E2E Latency: < 100msec

## Slide 9: Summary
Some gaming application uses video streaming when delivering picture to the client
These gaming application have similar requirement to what are described in [1] and [2], in terms of latency, data flow rate, and frame loss ratio on reverse link
These gaming application requires higher bandwidth on forward link reaching several hundreds of Mbps, as it uses streaming which also requires low latency capability

## Slide 10: Strawpoll (1)
Do you think it is reasonable for EHT to consider streaming game as a part of the target use case?
  Yes:
  No:
  Abstain:

## Slide 11: References
[1] 11-18/1234r0, “Real-time Mobile Game vs Wi-Fi,” Kate Meng
[2] 11-18/1449r0, “Real-time Console Game Network Profile,” Karthik Iyer, et. al.
[3] 11-19/111r0, “Additional game use case over WLAN,” Kazuyuki Sakoda, et.al.
[4] 11-18/2009rx, “IEEE 802.11 Real Time Applications TIG Report,” Kate Meng