## Slide 1
Authors:
EHT Feature Discussion
Date: 2019-03-11
Name | Affiliation | Address | Phone | Email
Yonggang Fang | ZTE (TX) |  |  | yfang@ztetx.com
Bo Sun | ZTE |  |  | 
Kaiying Lv | ZTE |  |  | 
Ning Wei | ZTE |  |  | 
Nan Li | ZTE |  |  | 
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page 1

## Slide 2: Abstract
This contribution discusses a potential feature using EHT Multi-AP support to improve the efficiency of station geo-positioning procedure.

## Slide 3: Background
Potential Features
  EHT PAR lists some main features under the discussion for support indoor and outdoor operation in the 2.4 GHz, 5 GHz and 6 GHz frequency bands.
    320MHz bandwidth and more efficient utilization of non-contiguous spectrum,
    Multi-band/multi-channel aggregation and operation,
    16 spatial streams and MIMO protocols enhancements,
    Multi-AP Coordination (e.g. coordinated and joint transmission),
    Enhanced link adaptation and retransmission protocol (e.g. HARQ),
    If needed, adaptation to regulatory rules specific to 6 GHz spectrum,
    Refinements of 802.11ax features.
  With multi-AP support, EHT may leverage this advantages to further improve the efficiency of fine timing measurement procedure for station’s geo-positioning.

## Slide 4: 802.11az Positioning
Non-Trigger based Sounding Exchange for Ranging
  It is iSTA initiated the geo-positioning procedure
  In order to improve the accuracy of fine timing measurement, the iSTA may need to repeat this procedure with the same AP.
  To get the geo-position, the STA needs to repeat the same procedure with different APs.

## Slide 5: 802.11az Positioning
Trigger based Sounding Exchange for Ranging
  It is RSTA initiated sounding exchange for ranging based on 802.11ax triggering procedure.
  An AP may send a trigger frame to initiate the ranging exchange procedure with the STA.
  To get the station geo-position, multiple APs are required coordinately to perform the ranging procedure sequentially.

## Slide 6: Analysis of Positioning
Some Issues or Concerns
  IEEE 802.11 uses fine timing measurement to get the station’s geo location.
  In order to get the position of the station, it requires to perform the fine timing measurement with at least 3 APs, which may take longer time when individually requesting the timing measurement with multiple APs.
  For the trigger-based sounding exchange procedure, it may need a coordinator to coordinate multiple APs to send trigger frames for the sounding exchanges. But how to efficiently coordinate multiple APs for sounding exchanges to reduce the measurement time might be a concern.
  In typical scenario, a STA may need to know its location at any time to trigger its location based services for the application software installed in the STA. Therefore non-trigger based geo-positioning would be more useful to applications running on the station.
  With Multi-AP support in EHT, a station may get the geo-position measured with multi-APs at anytime using the non-trigger based geo-positioning, and improve the efficiency of positioning.

## Slide 7: Potential Positioning with Multi-AP
Timing Measurement with Multi-AP support
  A STA may send a timing measurement message to multi-AP to start the ranging exchanges with those APs.
AP1
STA
AP2
MAP-Coordinator
TM-Request
TM Response
AP3
DS

## Slide 8: Enhancement Analysis
FTM enhancement
  As 802.11 supports FTM and 802.11az is to enhance the FTM, EHT may leverage those FTM features, and further enhance FTM based on with multi-AP feature supported in EHT.
    Reuse or define new sounding exchange messages and/or procedure with Multi-AP.
  Suggestion
  Suggest to consider this positioning enhancement as it can further improve efficiency of FTM with Multi-AP support.

## Slide 9: References
11-18-1231-04-0eht-eht-draft-proposed-par
11-18-1233-04-0eht-eht-draft-proposed-csd
IEEE P802.11az D1.0

## Slide 10
Thank you!