## Slide 1: eBCS Frame Authentication Proposal
Date: 2019-05-13
Authors:

## Slide 2: Abstract
This presentation describes a proposal for eBCS frame authentication that addresses TGbc R3 in 11-19-151r1.

## Slide 3: TGbc R3
The 802.11bc amendment shall provide origin authenticity protection for broadcast data frames.

## Slide 4: Architecture Assumption
AP broadcasts the eBCS frames that include the received multicast/broadcast frames.
AP
STA
STA
STA
STA
STA
STA
Multicast/Broadcast Frames
eBCS Frames

## Slide 5: Problem in Current GTKSA
Current GTKSA uses symmetric algorithm.
  Both AP and STAs use the same key.
If a user who has malicious intention can join the GTKSA, the user can easily make a rogue AP.
  Current GTKSA is not suitable for public use, untrusted user may join.
AP
STA
STA
STA
STA
STA
STA
Rogue
AP

## Slide 6: Requirements for the algorithm
Only the correct AP can sign the frames.
STAs can verify the signature.
AP
STA
STA
STA
STA
STA
STA
Rogue
AP

## Slide 7: Digital Signature (Public Key Algorithm)
AP has a “private key” and “public key” pair.
The “private key” is never disclosed.
The AP distributes “public key” to STAs.
Signature signed by the “private key” can be verified only by the “public key”
Remaining issue: How to verify that the “public key” is correct?
AP
STA
STA
STA
STA
STA
STA
Data
Sign
Data
Sign
Sign
Verify
Private Key
Public Key

## Slide 8: Public Key Infrastructure
CA(Certification Authority) has a “private key” and “public key” pair.
The CA’s public key is pre-installed in STAs. (e.g. included in application software)
The AP’s public key is signed by the CA’s private key.
The AP distributes its public key with signature to STAs.
STAs verify the signature of the AP’s public key by the CA’s public key.
AP
STA
STA
STA
STA
STA
STA
Data
Sign
Data
Sign
Sign
Verify
CA
Trusted way
Sign
Sign
Sign
Sign
Verify

## Slide 9: Performance of Digital Signature
Digital signature needs high computational cost.
It takes more than 2 msec to verify each frame on low-end devices.
Other low-weight algorithm should be combined with digital signature.
 | Intel Core i7 3.1GHz Linux |  | Intel Core i5 3.2GHz MacOS |  | AMD Turion II 2.2GHz FreeBSD |  | ARM Cortex-A7 1.1GHz Android | 
 | Sign | Verify | Sign | Verify | Sign | Verify | Sign | Verify
RSA 2048 | 2,651 | 77 | 2,502 | 72 | 6,580 | 188 | 94,073 | 2,460
RSA 4096 | 14,514 | 214 | 13,267 | 201 | 40,000 | 643 | 627,607 | 7,553
DSA L1024N160 | 225 | 426 | 206 | 390 | 599 | 1,098 | 7,274 | 13,942
DSA L2048N224 | 874 | 1,694 | 809 | 1,584 | 2,360 | 4,874 | 34,655 | 68,362
DSA L2048N256 | 873 | 1,695 | 799 | 1,548 | 2,436 | 4,702 | 39,672 | 77,262
DSA L3072N256 | 1746 | 3,496 | 1,605 | 3,173 | 4,896 | 9,674 | 84,727 | 169,804
ECDSA P256 | 37 | 91 | 33 | 87 | 138 | 247 | 5,027 | 14,792
ECDSA P384 | 4,459 | 8,588 | 4,324 | 8,560 | 17,160 | 35,719 | 94,448 | 184,409
ECDSA P521 | 8,321 | 16,538 | 8,147 | 16,479 | 35,759 | 49,511 | 190,014 | 360,304
usec / 1,500 byte message

## Slide 10: Timed Efficient Stream Loss-Tolerant Authentication (TESLA)
TESLA is a kind of one-way key chain algorithm published as IETF RFC4082.
It allows to check the integrity and authenticate the source of each packet in multicast or broadcast data streams by low-cost operations.

## Slide 11: Assumption for TESLA
Loose time synchronization between the sender (AP) and receivers (STAs)

## Slide 12: Generate One-way Key Chain
Sender(AP) generates 2*N keys.
K0
K1
Hash
K2
Hash
Hash
KN-1
Hash
KN
Hash
Random Seed
K’0
K’1
K’2
K’N-1
K’N
Hash’
Hash’
Hash’
Hash’
Hash’

## Slide 13: Authenticator
Sender add an authenticator to each frame by using key K’n
Key for authenticator is changed in TK
Kn is disclosed at TD = d * TK delay (d >= 2)
K’N
K’N-1
K’N-2
K’N-3
K’N-4
K’N-5
KN
KN-1
KN-2
KN-3
time
Key for authenticator
Disclosed Key
TK
TD

## Slide 14: Authentication
Receiver buffers frames until the key is disclosed.
The buffered frames are authenticated by the disclosed key.
The key integrity is verified as following:
  If Kn = Hash(Kn-1) and Kn is already verified, Kn-1 is correct.
K’N
K’N-1
K’N-2
K’N-3
K’N-4
K’N-5
KN
KN-1
KN-2
KN-3
time
Key for authenticator
Disclosed Key
Verify
Verify
Verify
K’N
Hash’
Authenticate frames
signed by K’N

## Slide 15: Problem on TESLA
KN has to be verified by other method.

## Slide 16: Combination of Digital Signature and TESLA
Digital signature is used to authenticate
  KN
  Timestamp
TESLA is used to authenticate Data frames

## Slide 17: Frame Sequence
eBCS Info frame
Transmitted in TI interval
TK
TI
eBCS Data frames
  eBCS Info frame includes
  Kc,N (where c is the seq num of eBCS Info)
  Kc-1,L (where L is the last used key index)
  Kc-1,L+1 (if d = 2)
  Timestamp
  TI
  TK
  d
  eBCS Info sequence number
  Public key with CA signature
  Signature by the sender’s private key
Sender generates one-way key chain before
generating each eBCS Info frame
(Kc,N, Kc,N-1, Kc,N-2, …, Kc,0)
  eBCS Data frame includes
  Kc,n+2 (where c is the seq num of eBCS Info, d=2)
  Ac,n (Authenticator generated by the key K’c,n)
  Key index: n
  eBCS Info seq num: c

## Slide 18: Key Disclosure and Authenticator Example
Cycle C
AC,0
KC,2
Cycle C+1
KC,0
KC,1
KC+1,8
AC,1
KC,3
AC,2
KC,4
AC,3
KC,5
AC,4
KC,6
AC,5
KC,7
KC-1,0
KC-1,1
KC,8
In case of d=2 and TI / TK=6
Kc,n: Key to be disclosed where c is the Cycle index and n is the Key index
Ac,n: Authenticator that is generated by K’c,n

## Slide 19: Receiver Procedure (1)
Wait for receiving eBCS Info frame
When a receiver receives an eBCS Info frame:
  Verify the sender’s public key by CA signature
  Verify the frame integrity by the sender’s public key
  Verify the timestamp is in the allowable range
  Remember Kc,N, TI, TK, d and eBCS Info Sequence Number
Now the receiver is ready to process eBCS Data frames

## Slide 20: Receiver Procedure (2)
When the receiver receives an eBCS Data frame:
  Verify the disclosed key (K)
  If the frames with authenticator generated by the key K are buffered, authenticate the frames.
    If the authentication succeeds, forward the frames to upper layer.
    If the authentication fails, discard the frames and the key K.
When the receiver receives the next eBCS Info frame:
  Verify eBCS Info frame as previously described
  Extract the keys to be disclosed (Ks)
  If the frames with authenticator generated by the key Ks are buffered, authenticate the frames.
    If the authentication succeeds, forward the frames to upper layer.
    If the authentication fails, discard the frames.

## Slide 21: Recovery from Missing Frames
Cycle C
AC,0
KC,2
Cycle C+1
KC,0
KC,1
KC+1,8
AC,1
KC,3
AC,2
KC,4
AC,3
KC,5
AC,4
KC,6
AC,5
KC,7
KC-1,0
KC-1,1
KC,8
In case of missing KC,5 and KC,4:
KC,5 and KC,4 can be generated from KC,3
KC,4 = Hash(KC,3)
KC,5 = Hash(KC,4)
In this case, the receiver has to buffer the frames
that have the authenticator generated by KC,5 and KC,4
until receiving KC,3.

## Slide 22: Dummy Data Frame
Cycle C
AC,0
KC,2
Cycle C+1
KC,0
KC,1
KC+1,8
AC,1
KC,3
AC,2
KC,4
AC,3
KC,5
AC,4
KC,6
AC,5
KC,7
KC-1,0
KC-1,1
KC,8
TESLA key is usually piggybacked in eBCS frames.
In case of no no data to be sent in a TESLA key period, the sender transmits a dummy data frame which
includes the key to be disclosed at the end of the TESLA key period.
Dummy Data Frame

## Slide 23: Latency and Memory Requirements
eBCS Data frames are buffered at least TD
Receivers have to buffer the frames transmitted in d * Tk.
  Even in case of missing frames, this restriction does not change.

## Slide 24: Allowable Time Difference
TESLA requires loose time synchronization between sender and receiver.
  To prevent replay attack
  Time Difference < TD

## Slide 25: Multiple eBCS APs Environment
In case of multiple APs transmit the same contents, each AP uses its own public/private key and TESLA keys.
Keys are independent from contents.
Server
AP1
AP2
STA
Contents
Contents
Use KAP2
Use KAP1

## Slide 26: Option for Latency Sensitive Application
In TESLA, at least TD latency is produced.
For latency sensitive applications, an option that all frames are signed by digital signature should be considered.
This option requires more computational resources for both sender and receiver.
Latency and computational cost are trade-off.

## Slide 27: References
IETF RFC4082 Timed Efficient Stream Loss-Tolerant Authentication (TESLA): Multicast Source Authentication Transform Introduction

## Slide 28: Comments & Questions