## Slide 1: eBCS Frame Authentication Proposal
Date: 2019-09-19
Authors:

## Slide 2: Abstract
This presentation describes a proposal for eBCS frame authentication that addresses TGbc R3.3.1 in 11-19-151r5.

## Slide 3: TGbc R3.3.1
The 802.11bc amendment shall provide origin authenticity protection for broadcast data frames.

## Slide 4: Architecture Assumption
AP broadcasts the eBCS frames that include the received multicast/broadcast frames.
AP
STA
STA
STA
STA
STA
STA
Multicast/Broadcast Frames
eBCS Frames

## Slide 5: Problem in Current GTKSA
Current GTKSA uses symmetric algorithm.
  Both AP and STAs use the same key.
If a user who has malicious intention can join the GTKSA, the user can easily make a rogue AP.
  Current GTKSA is not suitable for public use, untrusted user may join.
AP
STA
STA
STA
STA
STA
STA
Rogue
AP

## Slide 6: Requirements for the algorithm
Only the correct AP can sign the frames.
STAs can verify the signature.
AP
STA
STA
STA
STA
STA
STA
Rogue
AP

## Slide 7: Digital Signature (Public Key Algorithm)
AP has a “private key” and “public key” pair.
The “private key” is never disclosed.
The AP distributes “public key” to STAs.
Signature signed by the “private key” can be verified only by the “public key”
Remaining issue: How to verify that the “public key” is correct?
AP
STA
STA
STA
STA
STA
STA
Data
Sign
Data
Sign
Sign
Verify
Private Key
Public Key

## Slide 8: Public Key Infrastructure
CA(Certification Authority) has a “private key” and “public key” pair.
The CA’s public key is pre-installed in STAs. (e.g. included in application software)
The AP’s public key is signed by the CA’s private key.
The AP distributes its public key with signature to STAs.
STAs verify the signature of the AP’s public key by the CA’s public key.
AP
STA
STA
STA
STA
STA
STA
Data
Sign
Data
Sign
Sign
Verify
CA
Trusted way
Sign
Sign
Sign
Sign
Verify

## Slide 9: Performance of Digital Signature
Digital signature needs high computational cost.
It takes more than 2 msec to verify each frame on low-end devices.
  500 frames/sec = 750kB/sec = 6Mbps (when 1 core is fully used for verification)
Other low-weight algorithm should be combined with digital signature.
 | Intel Core i7 3.1GHz Linux |  | Intel Core i5 3.2GHz MacOS |  | AMD Turion II 2.2GHz FreeBSD |  | ARM Cortex-A7 1.1GHz Android | 
 | Sign | Verify | Sign | Verify | Sign | Verify | Sign | Verify
RSA 2048 | 2,651 | 77 | 2,502 | 72 | 6,580 | 188 | 94,073 | 2,460
RSA 4096 | 14,514 | 214 | 13,267 | 201 | 40,000 | 643 | 627,607 | 7,553
DSA L1024N160 | 225 | 426 | 206 | 390 | 599 | 1,098 | 7,274 | 13,942
DSA L2048N224 | 874 | 1,694 | 809 | 1,584 | 2,360 | 4,874 | 34,655 | 68,362
DSA L2048N256 | 873 | 1,695 | 799 | 1,548 | 2,436 | 4,702 | 39,672 | 77,262
DSA L3072N256 | 1746 | 3,496 | 1,605 | 3,173 | 4,896 | 9,674 | 84,727 | 169,804
ECDSA P256 | 37 | 91 | 33 | 87 | 138 | 247 | 5,027 | 14,792
ECDSA P384 | 4,459 | 8,588 | 4,324 | 8,560 | 17,160 | 35,719 | 94,448 | 184,409
ECDSA P521 | 8,321 | 16,538 | 8,147 | 16,479 | 35,759 | 49,511 | 190,014 | 360,304
usec / 1,500 byte message

## Slide 10: Timed Efficient Stream Loss-Tolerant Authentication (TESLA)
TESLA is a kind of one-way key chain algorithm published as IETF RFC4082.
It allows to check the integrity and authenticate the source of each packet in multicast or broadcast data streams by low-cost operations.
One-way key chain is based on the nature of one-way hash function.
  In case of Vi+1 = Hash(Vi)
    Calculating Vi+1 from Vi is easy.
    Calculating Vi from Vi+1 is difficult. (practically impossible)
Vi
Vi+1
easy
difficult

## Slide 11: Assumption for TESLA
Loose time synchronization between the sender (AP) and receivers (STAs)

## Slide 12: Generate One-way Key Chain
A transmitter generates a series of keys by using hash function.
K0
K1
Hash
K2
Hash
Hash
KN-1
Hash
KN
Hash
Random Seed
K’0
K’1
K’2
K’N-1
K’N
Hash’
Hash’
Hash’
Hash’
Hash’

## Slide 13: Authenticator Generation
The transmitter generates authenticator by HMAC hash function with the generated key.
The key to generate the authenticator is changed in a fixed duration Tk in reverse sequence of the key chain.
Data
HMAC-Hash(Key = K’i)
Authenticator
time
TK
K’N-1
TK
K’N-2
TK
K’N-3
TK
K’N-4
TK
K’N-5
TK
K’0

## Slide 14: Key Disclosure
The transmitter discloses the keys after d * Tk (d >= 2)
time
TK
K’N-1
TK
K’N-2
TK
K’N-3
TK
K’N-4
TK
K’N-5
TK
K’0
KN-1
KN-2
KN-3
Disclosed Key
(d = 2)
K2
Authenticator Key
Data
Auth (K’N-1)
Data
Auth (K’N-2)
Data
Auth (K’N-3)
KN-1
Data
Auth (K’N-4)
KN-2
Data
Auth (K’N-4)
KN-3
Data
Auth (K’0)
K2

## Slide 15: Frame Authentication
Receiver buffers frames until the key is disclosed.
The key integrity is verified as following:
  If Hash(Ki-1) = Ki and Ki is already verified, Ki-1 is correct.
The buffered frames are authenticated by the key calculated from the disclosed key.
K’N
K’N-1
K’N-2
K’N-3
K’N-4
K’N-5
KN
KN-1
KN-2
KN-3
time
Key for authenticator
Disclosed Key
Verify
Verify
Verify
K’N
Hash’
Authenticate frames
signed by K’N

## Slide 16: The First Key Verification
The first key, KN, has to be verified by other method.
KN should be verified by public key algorithm
KN
Signature

## Slide 17: The Last d keys Disclosure
The last d keys, K1 and K0 when d = 2, should be disclosed after the key sequence finished.
time
K’0
K2
Data
Auth (K’0)
K2
K1
K0
Tk

## Slide 18: Frame Sequence
eBCS Info frame
Transmitted in TI interval
TK
TI
eBCS Data frames
  eBCS Info frame includes
  Ks,N (where s is the seq num of eBCS Info)
  Ks-1,L (where L is the last used key index)
  Ks-1,L+1 (if d = 2)
  Timestamp
  TI
  TK
  d
  eBCS Info sequence number
  Public key with CA signature
  Signature by the sender’s private key
Sender generates one-way key chain before
generating each eBCS Info frame
(Ks,N, Ks,N-1, Ks,N-2, …, Ks,0)
  eBCS Data frame includes
  Ks,i+2 (where s is the seq num of eBCS Info, d=2)
  As,i (Authenticator generated by the key K’s,i)
  Key index: i
  eBCS Info seq num: s

## Slide 19: Receiver Procedure (1)
Wait for receiving eBCS Info frame
When a receiver receives an eBCS Info frame:
  Verify the sender’s public key by CA signature
  Verify the frame integrity by the sender’s public key
  Verify the timestamp is in the allowable range
  Remember Kc,N, TI, TK, d and eBCS Info Sequence Number
Now the receiver is ready to process eBCS Data frames

## Slide 20: Receiver Procedure (2)
When the receiver receives an eBCS Data frame:
  Verify the disclosed key (K)
  If the frames with authenticator generated by the key K are buffered, authenticate the frames.
    If the authentication succeeds, forward the frames to upper layer.
    If the authentication fails, discard the frames and the key K.
When the receiver receives the next eBCS Info frame:
  Verify eBCS Info frame as previously described
  Extract the keys to be disclosed (Ks)
  If the frames with authenticator generated by the key Ks are buffered, authenticate the frames.
    If the authentication succeeds, forward the frames to upper layer.
    If the authentication fails, discard the frames.

## Slide 21: Recovery from Missing eBCS Data Frames
Sequence S
AS,0
KS,2
Sequence S+1
KS,0
KS,1
KS+1,8
AS,1
KS,3
AS,2
KS,4
AS,3
KS,5
AS,4
KS,6
AS,5
KS,7
KS-1,0
KS-1,1
KS,8
In case of missing KS,5 and KS,4:
KS,5 and KS,4 can be calculated from KS,3
KS,4 = Hash(KS,3)
KS,5 = Hash(KS,4)
In this case, the receiver has to buffer the frames
that have the authenticator generated by KS,5 and KS,4
until receiving KS,3.

## Slide 22: Recovery from Missing eBCS Info Frames
Sequence S
AS+1,0
KS+1,2
Sequence S+2
KS,0
KS,1
KS+1,5
AS+1,1
KS+1,3
AS+1,2
KS+1,4
AS,0
KS,2
AS,1
KS,3
AS,2
KS,4
KS-1,0
KS-1,1
KS,5
In case of missing eBCS Info frame for the sequence S+1, the receiver discards all frames that are authenticated by KS,1 and KS,0, and
Option 1: Discards all frames in the sequence S+1.
Option 2: Buffer all frames in the sequence S+1.
When the receiver receives the eBCS Info frame for the sequence S+2,
the receiver authenticates the buffered frames by the keys KS+1,1 and KS+1,0.
KS+1,0
KS+1,1
KS+2,5
Sequence S+1
Discard

## Slide 23: Prevent Missing eBCS Info Frame
As described in the previous slide, missing an eBCS Info frame causes large data losses.
To prevent missing eBCS Info frames,
  eBCS Info frames should be transmitted in lower rate (e.g. MCS 0).
  eBCS Info frames should be transmitted multiple times.

## Slide 24: Irregular Sequence Reset
Sequence S
Sequence S+1
KS,5
KS,4
KS+1,8
AS+2,5
KS+2,7
AS,4
KS,6
AS,5
KS,7
KS-1,0
KS-1,1
KS,8
TESLA key is usually piggybacked in eBCS frames.
In case of no data to be sent in a TK, the transmitter resets the sequence and transmits eBCS Info frame of the next sequence S+1 to disclose the keys.
In case of no data to be sent in the sequence S+1, the transmitter stop transmission until the data to be sent comes. When the transmitter (re)starts a sequence, the first eBCS Info frame does not include the keys to be disclosed.
KS+2,8
Sequence S+2

## Slide 25: Parameters
d: Fixed to 2 is reasonable
TK: Longer TK requires receivers’ memory to buffer received frames. The clock of the transmitter and the receivers have to be roughly synchronized with the accuracy of TK to prevent from replay attack.
TI: Longer TI requires the transmitter’s memory to store a sequence of key chain.

## Slide 26: Multiple eBCS APs Environment
In case of multiple APs transmit the same contents, each AP uses its own public/private key and TESLA keys.
Keys are independent from contents.
Server
AP1
AP2
STA
Contents
Contents
Use KAP2
Use KAP1

## Slide 27: Option for Latency Sensitive Application
In TESLA, at least d * TK latency is produced.
For latency sensitive applications, an option that all frames are signed by digital signature should be considered.
This option requires more computational resources for both sender and receiver.
Latency and computational cost are trade-off.

## Slide 28: Summary
eBCS should support 2 types of frame authentication mechanism.
  TESLA with Public Key
  Public Key only

## Slide 29: Comparison
 | TESLA w/Public key | Public key only
Computational cost | Low | High
Authenticator size | 16 bytes (SHA-256, SHA3-256) 32 bytes (SHA3-512) | 256 bytes (RSA2048)
Public key (> 1,000 bytes) | Included only in eBCS Info frame | Included in every frame
Buffering / Delay | Receivers have to buffer frames until the key is disclosed e.g. 200ms (TK = 100ms) | No buffering required
Fault tolerance | Missing eBCS Info frame causes loss of data in TI, or require buffering frames during TI | Missing frame does not affect other frames
Adequacy | Good for high throughput, continuous data | Good for small, time sensitive data

## Slide 30: Considerations for the Use Cases
Consider the performances and requirements for the TGbc use cases in 11-19/268r5.

## Slide 31: Categorization of the Use Cases
Use Case |  | Data Type | Stream
1 | Stadium Video Distribution | Video | Yes
2 | Low Power Sensor UL Broadcast | Small data | No
3a | Railroad Crossing | Small data | No
3b | Traveler Information | Static data | Yes
4 | Broadcast Services for Event Production | Video | Yes
5 | Multi-lingual and Emergency Broadcast | Audio | Yes
6 | VR eSports Video Distribution | Video | Yes
7 | Multi-Channel Data Distribution | Static data | Yes
8 | Lecture room slide distribution | Static data / Video | Yes
9 | Regional based broadcast TV service | Video | Yes
10 | AP tagged UL forwarding | Small data | No

## Slide 32: Video
High bit rate and continuous.
TESLA w/public key is better for this use case.
Assumption
  Payload size of a frame: 1,500 B/frame
  TK: 100ms
  d: 2
Full HD (1920x1080@30fps)
  12Mbps (AV1 level 4.0) = 1.5MB/s = 1,000 frames/s
  Delay: 200ms
  Buffer size: 300kB
4K (3840x2160@30fps)
  30Mbps (AV1 level 5.0) = 3.75MB/s = 2,500 frames/s
  Delay: 200ms
  Buffer size: 750kB

## Slide 33: Audio
Small but frequent and continuous data transmission.
TESLA w/public key is better for this use case.
128kbps/channel = 16kB/s/channel = 11 frames/s/channel
Delay: 200ms
Buffer size: 4.5kB

## Slide 34: Static data
Not frequently changed contents
Broadcast serialized files repeatedly (e.g. HLML/CSS/JS/image files)
Continuous transmission, not time sensitive
TESLA w/Public key is better for this use case.
Expect 15MB of contents transferred in
  1s: 15MB/s = 10,000 frames/s
    Buffer: 3MB
  5s: 3MB/s = 2,000 frames/s
    Buffer: 600kB
  10s: 1.5MB/s = 1,000 frames/s
    Buffer: 300kB

## Slide 35: Small data
Small and irregular data transmission
Public key only mechanism is better for this use case
No delay / No buffer required

## Slide 36: References
IETF RFC4082 Timed Efficient Stream Loss-Tolerant Authentication (TESLA): Multicast Source Authentication Transform Introduction

## Slide 37: Comments & Questions