## Slide 1: FTM TOA measurement on non-HT duplicate PPDUs
Date: 2019-03-12
Authors:

## Slide 2: Background
All non-HT duplicate PPDUs may not be transmitted in a standards compliant manner.
As a result, the responders that want to interoperate with all REVmc initiators cannot do their TOA estimations on the non-HT duplicate PPDUs using the full BW in a coherent manner.
The outcome is reduced ranging accuracy in all REVmc ranging using non-HT duplicate PPDU ACKs.
If the initiator can let the responder know that it is transmitting its non-HT PPDUs in a standards compliant, then we can mitigate this problem.

## Slide 3: Add FTM TOA estimation BW negotiation
Don’t touch the standard for how a PPDU is transmitted
Negotiate the BW used for FTM TOA estimation on non-HT duplicate PPDU ACKs
  20 MHz or full BW
  Initiator request – Responder respond
Use bit in the FTM Parameters element

## Slide 4: Fine Timing Measurement Parameters Field (REVmd)
Planned use for ‘Secure ToF Measurement’ negotiation in 802.11az
Planned use in ‘EDMG Ranging Priority’ negotiation in 802.11az
Probably the use of at least one of these bits can be moved to the Ranging Parameters field in the Ranging Parameters element that is included in the initial Fine Timing Measurement Request frame and the initial Fine Timing Measurement frame, or to one of the Ranging subelements.

## Slide 5: Straw Poll
Do you support using a bit, assuming one can be freed up, to negotiate the FTM TOA estimation BW to 20 MHz or full BW on non-HT duplicate PPDU ACKs:
Y: N: A:

## Slide 6
Thank You!

## Slide 7: Ranging Parameters field in the Ranging Parameters element used in the FTM negotiation
We have several reserved bits we can use here, or we can add new bits here.