## Slide 1: Phase Shift Based TOA Reporting in Passive Location Ranging
Date: 2019-03-12
Authors:

## Slide 2: CIDs addressed
This submission addresses the TGaz LB 240 CIDs 1515, 1557 and 1563.

## Slide 3: Background
We now have the option to use phase shift based TOA reporting in TB Ranging.
There is no reason why we should not also enable this for the Passive Location Ranging case.
What is needed is some enabling in the time-stamp reporting.

## Slide 4
Proposed Protocol Addition:
1 bit

## Slide 5: Passive Location ISTA to RSTA LMR
‘ISTA Passive Location Measurement Report Element’:
Dialog Token, CFO to Responder, N Time Stamps, etc.
Per time-stamp – ‘Time Stamp Measurement Report field’:
  Type
    TOD
    TOA
    PS-TOA
    Correction to peer STA PS-TOA
  Valid
  Time-Stamp
  Time-Stamp Error
  RID (of transmitter)
Add a bit to add two new types.
Notes:   Report circle also enables to increase the MCS and reduce the broadcast time, since the chances of the client being close to at least one ASTA in the NW is much higher.

## Slide 6: Primus RSTA Broadcast Frame
LCI table, optional
RSTA Passive Location LMR:
  Dialog Token, CFO to Responder, N Time Stamps, etc.
  Per time-stamp – ‘Time Stamp Measurement Report field’:
    Type
      TOD
      TOA
      PS-TOA
      Correction to peer STA PS-TOA
    Valid
    Time-Stamp
    Time-Stamp Error
    RID (of transmitter)
Add a bit to add two new types.
Notes:   Report circle also enables to increase the MCS and reduce the broadcast time, since the chances of the client being close to at least one ASTA in the NW is much higher.

## Slide 7: Secundus RSTA Broadcast Frame
Per ISTA - ‘ISTA Passive Location Measurement Report Element’:
  Dialog Token, CFO to Responder, N Time Stamps, etc.
  Per time-stamp – ‘Time Stamp Measurement Report field’:
    Type
      TOD
      TOA
      PS-TOA
      Correction to peer STA PS-TOA
    Valid
    Time-Stamp
    Time-Stamp Error
    RID (of transmitter)
Copy of the LMR report from each ISTA
Add a bit to add two new types.
Notes:   Report circle also enables to increase the MCS and reduce the broadcast time, since the chances of the client being close to at least one ASTA in the NW is much higher.

## Slide 8
Range and DTOA Calculations

## Slide 9: ISTA to RSTA Range Calculations
RSTA
ISTA
t2
t1
t4
t3
DL NDP
UL NDP
Ranging NDP transmissions and time stamps
The differential distance from the ISTA to the RSTA can then be calculated as [1]:
,where the time stamps are as shown above and c is the speed of light.
D_IR = [(t2 - t1) + (t4 – t3)]/2 * c

## Slide 10: Propagation paths and time stamps
RSTA
ISTA
PSTA
Ranging NDP transmissions and time stamps
t2
t1
t4
t3
DL NDP
UL MU NDP
t5
t6
The differential distance between the PSTA and the RSTA vs. the ISTA can now be calculated as [2]:
  DD_PIR = [t6 – t3 – (t5 – t1)]*c = [t6 – t3 – (t5 – (t2-T_IR))]*c = [t6 – t5 – t3 + t2 - T_IR] * c
  Using T_IR = [(t4 – t1) – (t3 – t2)]/2
  We get: DD_PIR = [t6 – t5 – t3 + t2 - 0.5*t4 + 0.5*t1 + 0.5*t3 - 0.5*t2)]*c
  Or:
DD_PIR = [t6 – t5 – 0.5*t3 + 0.5*t2 – 0.5*t4 + 0.5*t1]*c

## Slide 11: Distance Calculations - ISTA, i.e. t4, PS-TOA
Distance calculations:
Assume t4 is measured with PS-TOA. According to our earlier calculations, the distance between ISTA and RSTA is:
D_IR = [(t2 - t1) + (t4 – t3)]/2 * c
When using PS-TOA for t4, t4 will be too large. To make the above calculation work out the responder can compensate by can either decrease t2 or increase t3.
Likewise the differential distance from PSTA to ISTA-RSTA pair is:
DD_PIR = [t6-t5_1-0.5*t3+0.5*t2-0.5*t4_1+0.5*t1_1]*c
Again, when using PS-TOA for t4, t4 will be too large. Here to make this calculation work out, the responder can compensate by either increase t2 or decrease t3.
Thus, the RSTA cannot adjust its reported time stamps, t2 and t3, such as to make both the D_IR and the DD_PIR calculations work out. If t2 is measured with PS-TOA by the RSTA, then the corresponding problem occurs. => Need to report the correction to the PS-TOA separately!

## Slide 12
ISTAs Reporting PS-TOAs

## Slide 13
Passive Location with Phase Shift Based TOA Reporting
- ISTA reporting PS-TOA
RSTA
Measures PS-TOA
ISTA
Correction to PS-TOA calculated
PS-TOA reported
Passive Station (PSTA)
PS-TOA and correction broadcasted

## Slide 14: Passive Location Ranging with PS-TOA – ISTA reporting PS-TOA
ISTA 1
ISTA 2
DL
NDP
UL
NDP
TF
RSTA
UL
NDP
UL
NDP
DL
NDPA
Poll
TF
PR
PR
iSTA to rSTA
LMR
TF
rSTA to
iSTA
LMR
UL
NDP
TF
iSTA to rSTA
LMR
LCI, DL LMR
UL LMR
iSTA to rSTA
LMR
ISTA reports
PR-TOAs
- Indicates PR-TOA feedback
RSTA starts computing the PS-TOA correction for the last ISTA
Calculation of (last) ISTA’s PS-TOA correction and reporting in the Primus broadcast frame.
RSTA reports corrections to the ISTAs’ PS-TOAs
ISTAs measures
PS-TOAs
Primus and Secundus LCI/LMR broadcasting frames
Re-broad-casting ISTA LMR reports

## Slide 15
PS-TOA Reporting in ISTA to ISTA Ranging
If an ISTA is reporting PS-TOAs, then it can still range with other ISTAs in the Passive Location Ranging exchange, as long as these other ISTAs are able to calculate the correction.
Measures PS-TOA
PS-TOA correction reported
PS-TOA reported
PS-TOA and correction broadcasted
RSTA
ISTA 2
Passive Station (PSTA)
ISTA 1
PS-TOA correction calculated

## Slide 16: ISTA PS-TOA Reporting Benefits in Passive Location Ranging
Enables simple design of passive location ISTAs
Simplifies immediate feedback for ISTAs
  The PS-TOA more or less already calculated in the PHY - Immediate ISTA feedback greatly simplified.
A ‘powerful enough’ RSTA would be capable to immediately turn around and broadcast the corrections to the ISTAs’ PS-TOAs – Enables immediate feedback of all time-stamps.
Also enables ISTA to ISTA ranging with PS-TOA reporting.

## Slide 17
RSTA Reporting PS-TOAs

## Slide 18
Passive Location with Phase Shift Based TOA Reporting
- RSTA reporting PS-TOA
RSTA
Measures PS-TOA
ISTA
PS-TOA reported
Passive Station (PSTA)
PS-TOA and correction broadcasted
Correction PS-TOA reported
Correction to PS-TOA calculated

## Slide 19: Passive Location Ranging with PS-TOA – RSTA reporting PS-TOA
DL
NDP
UL
NDP
TF
RSTA
ISTA 1
ISTA 2
UL
NDP
UL
NDP
DL
NDPA
Poll
TF
PR
PR
iSTA to rSTA
LMR
TF
rSTA to
iSTA
LMR
UL
NDP
TF
iSTA to rSTA
LMR
LCI, DL LMR
UL LMR
iSTA to rSTA
LMR
Primus and Secundus LCI/LMR broadcasting frames
ISTAs calculates the corrections to the RSTA’s s PS-TOAs
RSTA
PS-TOAs
- Indicate PS-TOA feedback
Broad-cast of RSTA TODs and PS-TOAs
Re-broad-casting ISTA the LMR reports
PS-TOA corrections reported

## Slide 20: RSTA PS-TOA Reporting Benefits in Passive Location Ranging
Offloads RSTA processing
Makes use of possibly available processing resources at the ISTAs

## Slide 21
Straw Poll

## Slide 22: Straw Poll
Do you support to add a bit to ‘Passive Location Ranging’ time-stamp stamp type to get two new time-stamp types:
PS-TOA
Correction to peer PS-TOA time stamp
as shown in slides 5-7, and use it to report PS-TOAs and corrections to peer PS-TOAs?
Y: N: A:

## Slide 23: References
[1] “Passive Location”, IEEE 802.11-17/0417r0.
[2] “CIDs 46,47,48 Regarding Fine Timing Measurement”, 11-12/1249r4, Carlos Aldana (Qualcomm) et al.

## Slide 24
Thank You!