## Slide 1: Phase Shift Based TOA Reporting in Passive Location Ranging
Date: 2019-09-16
Authors:

## Slide 2: Background
We now have the option to use phase shift based TOA reporting in TB Ranging.
There is no reason why we should not also enable this for the Passive Location Ranging case.
What is needed is some enabling in the time-stamp reporting protocol.

## Slide 3
Range and DTOA Calculations

## Slide 4: ISTA to RSTA Range Calculations
RSTA
ISTA
t2
t1
t4
t3
DL NDP
UL NDP
Ranging NDP transmissions and time stamps
The differential distance from the ISTA to the RSTA can then be calculated as [1]:
,where the time stamps are as shown above and c is the speed of light.
D_IR = [(t2 - t1) + (t4 – t3)]/2 * c

## Slide 5: Passive Location Differential Distance Calculations
RSTA
ISTA
PSTA
Ranging NDP transmissions and time stamps
t2
t1
t4
t3
DL NDP
UL MU NDP
t5
t6
The differential distance between the PSTA and the RSTA vs. the ISTA can now be calculated as [2]:
  DD_PIR = [t6 – t3 – (t5 – t1)]*c = [t6 – t3 – (t5 – (t2-T_IR))]*c = [t6 – t5 – t3 + t2 - T_IR] * c
  Using T_IR = [(t4 – t1) – (t3 – t2)]/2
  We get: DD_PIR = [t6 – t5 – t3 + t2 - 0.5*t4 + 0.5*t1 + 0.5*t3 - 0.5*t2)]*c
  Or:
DD_PIR = [t6 – t5 – 0.5*t3 + 0.5*t2 – 0.5*t4 + 0.5*t1]*c

## Slide 6: Passive Location Differential Distance Calculations – PS-TOA reporting case
RSTA
ISTA
PSTA
Ranging NDP transmissions and time stamps for phase shift reporting case
tp2
t1
tp4
t3
DL NDP
UL MU NDP
t5
t6
For the phase shift TOA reporting case, the differential distance between the PSTA and the RSTA vs. the ISTA can now be calculated as:
  DD_PIR = [t6 – t5 – 0.5*t3 + 0.5*t2 – 0.5*t4 + 0.5*t1]*c, and using e.g. t4 = tp4+(t2-tp2) we get
  DD_PIR = [t6 – t5 – 0.5*t3 + 0.5*t2 – 0.5*(tp4+(t2-tp2)) + 0.5*t1]*c, i.e.
  DD_PIR = [t6 – t5 – 0.5*t3 + 0.5*tp2 - 0.5*tp4 + 0.5*t1]*c Note: No RSTA or ISTA TOAs needed!!!
where tp2 and tp4 are phase shift TOAs.

## Slide 7
PS-TOA Reporting in Passive Location Ranging

## Slide 8
Passive Location with Phase Shift Based TOA Reporting
RSTA
PS-TOA measured and reported
ISTA
PS-TOA measured and reported
PS-TOAs and TODs reported
Passive Station (PSTA)
PS-TOAs and TODs broadcasted

## Slide 9
PS-TOA Reporting in ISTA to ISTA Ranging
If an ISTA is reporting PS-TOAs, then it can still range with other ISTAs in the Passive Location Ranging exchange, as long as these other ISTAs are measure and report PS-TOAs .
Measures PS-TOA
PS-TOA reported
PS-TOA reported
PS-TOAs (and TODs) broadcasted
RSTA
ISTA 2
Passive Station (PSTA)
ISTA 1
PS-TOA measured

## Slide 10: Passive Location Ranging with PS-TOA reporting
ISTA 1
ISTA 2
DL
NDP
UL
NDP
TF
RSTA
UL
NDP
UL
NDP
DL
NDPA
Poll
TF
PR
PR
iSTA to rSTA
LMR
TF
rSTA to
iSTA
LMR
UL
NDP
TF
iSTA to rSTA
LMR
LCI, DL LMR
UL LMR
iSTA to rSTA
LMR
ISTA reports
PS-TOAs
RSTA starts computing the PS-TOA for the last ISTA
Measurement of (last) ISTA’s PS-TOA and reporting in the rSTA to iSTA LMR and Primus broadcast frame.
RSTA reports ISTAs’ PS-TOA
ISTAs measures
PS-TOAs
Primus and Secundus LCI/LMR broadcasting frames
Re-broad-casting ISTA LMR reports
Basically the only change is to measure and report PS-TOAs!
RSTA reports
PS-TOA
ISTAs measures
PS-TOAs

## Slide 11: PS-TOA Reporting Benefits in Passive Location Ranging
Enables simple design of both RSTAs and ISTAs
  As they don’t have to measure TOAs (quickly)
Simplifies immediate feedback for ISTAs and RSTAs
  The PS-TOA more or less already calculated in the PHY
Enables simpler immediate feedback of all time-stamps.
Also enables ISTA to ISTA ranging with PS-TOA reporting.

## Slide 12
Proposed Protocol Addition:
1 bit

## Slide 13: Passive Location ISTA to RSTA LMR
‘ISTA Passive Location Measurement Report Element’:
Dialog Token, CFO to Responder, N Time Stamps, etc.
Per time-stamp – ‘Time Stamp Measurement Report field’:
  Type
    TOD
    TOA
    PS-TOA
    Reserved
  Valid
  Time-Stamp
  Time-Stamp Error
  RID (of transmitter)
Add a bit to add one new type.
Notes:   Report circle also enables to increase the MCS and reduce the broadcast time, since the chances of the client being close to at least one ASTA in the NW is much higher.

## Slide 14: Primus RSTA Broadcast Frame
LCI table, optional
RSTA Passive Location LMR:
  Dialog Token, CFO to Responder, N Time Stamps, etc.
  Per time-stamp – ‘Time Stamp Measurement Report field’:
    Type
      TOD
      TOA
      PS-TOA
      Reserved
    Valid
    Time-Stamp
    Time-Stamp Error
    RID (of transmitter)
Add a bit to add one new type.
Notes:   Report circle also enables to increase the MCS and reduce the broadcast time, since the chances of the client being close to at least one ASTA in the NW is much higher.

## Slide 15: Secundus RSTA Broadcast Frame
Per ISTA - ‘ISTA Passive Location Measurement Report Element’:
  Dialog Token, CFO to Responder, N Time Stamps, etc.
  Per time-stamp – ‘Time Stamp Measurement Report field’:
    Type
      TOD
      TOA
      PS-TOA
      Reserved
    Valid
    Time-Stamp
    Time-Stamp Error
    RID (of transmitter)
Copy of the LMR report from each ISTA
Add a bit to add one new type.
Notes:   Report circle also enables to increase the MCS and reduce the broadcast time, since the chances of the client being close to at least one ASTA in the NW is much higher.

## Slide 16: References
[1] “Passive Location”, IEEE 802.11-17/0417r0.
[2] “CIDs 46,47,48 Regarding Fine Timing Measurement”, 11-12/1249r4, Carlos Aldana (Qualcomm) et al.

## Slide 17
Thank You!