## Slide 1: RSTA Requires ISTA-to-RSTA LMR bit in the Extended Capabilities element
Date: 2019-03-12
Authors:

## Slide 2: Motivation/Background
The criteria for a bit to be added to the Extended Capabilities element is “does the ISTA need this information in order to determine if a .11az negotiation should be initiated with the corresponding RSTA?”
Propose that RSTA advertise its expectation that it expects the ISTA to share the Location Measurement Report with the RSTA by indicating the expectation in the ISTA-to-RSTA LMR, in the Extended Capabilities element

## Slide 3: Bit(s) in Extended Capabilities element (included in 2.4/5GHz Beacons)
RSTA Policy:
Bit <ANA>: RSTA requires ISTA to support ISTA-to-RSTA LMR exchange (applies to both TB and nTB)
If the ISTA does not set the ISTA-to-RSTA LMR Feedback subfield of the Ranging Parameters field in the Ranging Parameters element included in the initial FTM Request that the ISTA sends to the RSTA to initiate negotiation for a non-Trigger based or a Trigger based FTM session, the RSTA <tbd> reject the negotiation request
  <tbd> can be ‘may’ – not very useful
  <tbd> can be ‘shall’ – behavior is clear; if the ISTA does not support (or is no willing to send ISTA-to-RSTA LMR), then the proposed bit helps the ISTA avoid RSTAs that require ISTA-to-RSTA LMR, preventing wasteful transmissions.

## Slide 4: Opens
By setting the RSTA requires ISTA-to-RSTA LMR bit in the Extended Capabilities element to 1, the RSTA implicitly indicates that it is capable of obtaining the ISTA-to-RSTA LMR
Is it mandated that the RSTA should retrieve the ISTA-to-RSTA LMR?
  No
  The ISTA can discard the ISTA-to-RSTA LMR if the RSTA does not retrieve the LMR before MaxToAAvailableExp
  Should the ISTA-to-RSTA MaxToAAvailableExp be the same as that of the RSTA-to-ISTA MaxToAAvailableExp?

## Slide 5: Changes to the specification
Add the RSTA requires ISTA-to-RSTA LMR bit to the Extended Capabilities element
Add a MIB entry corresponding to this policy in Annex-C
In Clause 11.22.6.3.3 (Trigger-based and non-Trigger-based Ranging Measurement Negotiation) add a condition similar to the following:
  An RSTA shall reject a request if it has set the RSTA requires ISTA-to-RSTA LMR field in the Extended Capabilities element to 1, and the ISTA has sent an initial FTM request with a Ranging Parameters element in which the ISTA-to-RSTA LMR feedback subfield in the Ranging Parameters field is set to 0.
Other changes resulting from how the issues listed in the previous slide are resolved.

## Slide 6: Straw Poll
We support incorporating a RSTA requires ISTA-to-RSTA LMR bit in the Extended Capabilities element. The semantics of this bit is for the RSTA to reject a request for a Fine Timing Measurement session that does not indicate support for ISTA-to-RSTA LMR.
Y:
N:
Abstain:

## Slide 7: Backup

## Slide 8: EULA is between an App and a Cloud Service
When user consents to a prompt from an App, the EULA is executed with a peer Cloud Service
  ISTA and RSTA are out-of-the-loop
  However, ISTA may or may not execute a IFTMR/IFTM exchange with the RSTA based on what the RSTA requires (as advertised in the beacon based on what the cloud service requires) and what the User of the App has consented to
  How can an AP that services multiple Cloud Service and an ISTA that serves multiple Apps harmonize the Cloud Service/ISTA App requirements into a bit in the RSTA beacon/ISTA capability?
    Implementation dependent
    A potential policy: Enforce the most-constraining-requirement

## Slide 9: Potential Modifications -- Discussion
The RSTA require ISTA-to-RSTA LMR bit (enabled) is conditional on the RSTA requires PMF bit (enabled)
  Guarantees all management frames (IFTMR/IFTM/LMR) are protected
  Minimizes ISTA’s concern in sharing its location with the RSTA
The ISTA can constrain how the RSTA gets to use the ISTA-to-RSTA LMR
  Examples
    use it within the AP but not transmit it outside the AP
    Discard the ISTA-to-RSTA LMR after <seconds>
    Anonymize the ISTA-to-RSTA LMR before use
    others

## Slide 10: ISTA-to-RSTA LMR – a benefit
Can be used for the RSTA to provide feedback on the accuracy of the estimate
  RSTA can estimate relative position of the ISTA
  Validate the RSTA’s estimate of the ISTA’s relative position against what the ISTA-to-RSTA LMR estimate is; and provide feedback on how good it is

## Slide 11: Other Comments
Can the RSTA decide to abort/end the session if the session was established with the ISTA indicating support for ISTA-to-RSTA LMR but not reporting ISTA-to-RSTA LMR when requested by the RSTA?
  This behavior is already part of the current specification
  The RSTA can end/abort the session at any time (even without a reason)
Can the RSTA advertise the RSTA requires ISTA-to-RSTA LMR but not reject a request that does not indicate support for ISTA-to-RSTA LMR?
  This is possible but beats the purpose of the advertisement.
Can the RSTA not request ISTA-to-RSTA LMR?
  Yes. The ISTA discards measurements after the expiry of MaxToAAvailableExp