## Slide 1: TGbc additional use case scenario
Date: 2019-01-10
Authors:

## Slide 2: Abstract
This presentation provides TGbc additional use case scenario to incorporate TGbc use case slide.

## Slide 3: Scenario # VR eSports Video Distribution
Stakes holders
  Game makers/providers/players
  Game set makers
Topology/Architecture
Benefit of using TGbc
eBCS can distribute the video to thousands of audiences with less bandwidth consumption than unicast.
Service scene
  At the location of VR eSports games, such as arena, eBCS distributes the video that is the view of the player to the audiences.
Required function
  Video distribution latency should be less than 20ms.
  Distribute video to large number of audiences.
Server
AP
Player
Audiences

## Slide 4: Scenario # Multi-Channel Data Distribution
Stakes holders
  Museum/Concert Hall/Convention Hall/Sightseeing Venue/etc.
Topology/Architecture
Benefit of using TGbc
eBCS can be used for multi-lingual services to distribute the same information to people from multiple countries.
Service scene
  An AP broadcasts the same information in different languages each in a dedicated channel.
  A user can choose one of the channels
Required function
Distribution of different data
People can choose their preferred channel.
Audiences
Server
AP
Audiences
Ch#1: Japanese
Ch#2: English
Ch#3: Chinese
Ch#4: Korean
…

## Slide 5: Scenario # Lecture room slide distribution
Stakes holders
School / University /Conference room etc.
Teacher/ Professor / Speaker
Topology/Architecture
Benefit of using TGbc
Easy to distribution of slides to audiences
Service scene
Simultaneous distribution of slides on the screen to audience PC, Tablet, etc.
The audience no need to download visual aids and change pages
Synchronized slide distribution to all of students.
Required function
low latency
Capacity 1000STAs
Professor / Teacher/ Speaker
Student etc.
Screen
Projector with AP

## Slide 6: Scenario # Reginal based broadcast TV service
Stakes holders
Local TV services company
Residential people and home
Topology/Architecture
Benefit of using TGbc
Low CAPEX for TV company
Anytime, Anywhere receivable services for residential people
Easy installation to disaster shelter etc,.
Service scene
  Local news , TV contents can be distributed to consumer BYOD devices (not TV receiver) by small local TV company.
  In case of disaster, evacuation information will be distributed without any complex customer operation.
Required function
Middle range services
Audiences
Local TV services
Disaster shelter
Home
Evacuation
Information
Disaster side
Reginal
services
Inhouse
services
Wi-Fi

## Slide 7: Straw poll
Do you conditionally agree to incorporate additional TGbc use case scenario to TGbc Use Case document?
required condition: Precise more about functional requirement.
Yes
No
Abstain