## Slide 1: Motion Booklet for IEEE 802.11 TGbd
Date: 2019-03-14
Authors:

## Slide 2: Abstract
Booklet for the TGbd motions related to FRD and SFD.
Motions are consecutively numbered since the formation of the task group.

## Slide 3: March 2019 FRD & SFD Motions
Motion #1 -- #7
Vancouver, BC, USA

## Slide 4: Motion #1
Move to update the 11bd FRD according to the changes captured in document 11-19/0511r1.
Mover: Bahar Sadeghi
Second:
Approved by unanimous consent
Y/N/A

## Slide 5: Motion #2
Move to add the following text to section 3 in 11bd SFD.
  “ 11bd PPDU format includes L-STF, L-LTF, and L-SIG fields as shown in Figure 3.x
    L-STF means short training field of 11p.
    L-LTF means long training field of 11p.
    L-SIG means signal field of 11p.”
Mover: Dongguk Lim
Second:
Approved by unanimous consent
Y/N/A
L-LTF
L-STF
L-SIG
11bd PPDU
Figure 3.x 11bd PPDU format

## Slide 6: Motion #3
Move to add the following text to section 3 in 11bd SFD.
  “11bd supports the 10MHz bandwidth PPDUs.
  11bd supports the 20MHz bandwidth PPDUs. ”
Mover: Dongguk Lim
Second:
Approved by unanimous consent
Y/N/A

## Slide 7: Motion #4
Move to add the following text to section 3 in 11bd SFD.
  “In 20MHz bandwidth, L-STF, L-LTF, and L-SIG for 10MHz PPDU are duplicated as shown in the figure below.”
Mover: Dongguk Lim
Second:
Approved by unanimous consent
Y/N/A
10MHz
10MHz
L-LTF
L-STF
L-SIG
L-LTF
L-STF
L-SIG
11bd PPDU

## Slide 8: Motion #5
Move to add the following text into Section 3 of SFD
  “11bd amendment shall support LDPC.”
Mover: Prashant Sharma
Second:
Approved by unanimous consent
Y/N/A:

## Slide 9: Motion #6
Move to add the following text into Section 3 of SFD
  “An NGV STA shall be capable of the following operations:
    To decode 11p PPDUs with TBD receive sensitivity threshold (TBD value is -85dBm or lower).
    To transmit PPDU format up on request from upper layer, the PPDU format can be either 11p PPDU or 11bd PPDU.”
Mover: Rui Cao
Second:
Approved by unanimous consent
Y/N/A:

## Slide 10: Motion #7
Move to add the following text into Section 3 of SFD
  “An NGV STA shall indicate the NGV capability in MAC level, when transmitting an 11p PPDU”
Mover: Rui Cao
Second:
Approved by unanimous consent
Y/N/A: