## Slide 1: EVM Specification for OOK Waveform
Date: 2019-04-12
Authors:

## Slide 2: Introduction
EVM (Error Vector Magnitude) is a typical metric for measuring transmit modulation accuracy
For OFDM signal in 11a/n/ac/ad/ax, the EVM is measured for QAM symbols in frequency domain [1][2]
For .11ba, a new formulation may be needed to measure the EVM for OOK symbols in time domain

## Slide 3: EVM for OFDM Signal
Typically assuming certain capabilities and accuracies for the testing instrument:
Capable of converting the transmitted signal into a stream of complex samples
I/Q amplitude and phase balance
DC offset
Phase noise mitigation
Synchronization in time
Need to consider
Power normalization
Ideal symbol values
(Copied from [1])

## Slide 4: EVM for OOK Signal
Assumptions
  Measured signal is normalized with average power
  The testing equipment is capable of converting the transmitted signal into a stream of complex samples and measuring the magnitude of samples and accumulate them over On and Off durations
“Off”
“On”
0
Envelope
Measured Samples
On
Off
Time
Normalized “Constellation” of OOK modulation
Envelope
EVM
Measurement

## Slide 5: EVM for OOK Signal (cont.)
L-preamble
WUR Sync
WUR Data
Test Frame 1
L-preamble
WUR Sync
WUR Data
Test Frame
. . . . . . .
Testing Requirements
  Sampling rate:
  During the test, a bandpass filter of which the 3dB-bandwidth is equal to [50.5] MHz shall be used to obtain the signal on the channel under the test.
  The test shall be performed over at least [20] frames ().
  Perfect synchronization
  The frame under test, which includes both Sync and HDR/LDR data fields, shall be at least [256] s long.

## Slide 6: Some Notations
: Number of tested frames in a measurement duration
: Number of On symbols in k-th test frame
: Number of Off symbols in k-th test frame
: Number of samples in On or Off symbol duration (assuming it is the same for both On and Off symbol durations), which is different for 2ms and 4ms symbols
is the i-th observed sample of signal envelope on the j-th On symbol and the k-th test frame;
is the i-th observed sample of signal envelope on the j-th Off symbol and the k-th test frame

## Slide 7: Some Notations (cont.)
: the normalization factor of the received signal in a measurement duration
Note:
Assuming the testing instrument can obtain the real (I) and imaginary (Q) components of the WUR signal, the envelope functions in On symbol and in Off symbol may respectively be expressed as
and
where
, are the -th observed real and imaginary values in the -th On symbol and the -th test frame, respectively;
, are the -th observed real and imaginary values in the -th Off symbol and the -th test frame, respectively;

## Slide 8: Some Notations (cont.)
Some options to define the “envelope”:
(the ones for “Off” symbols can be defined in the same way)
Which one should be used in the spec is TBD

## Slide 9: EVM Expression
Defined normalized sample average for On and Off Symbols:
Then, the averaged RMS of WUR portion of all test frames is
Normalized Eye Diagram
|I|+|Q|
Time

## Slide 10: Simulation
Settings
  Fs: 80 MHz
  Nonlinear PA: Rapp model, 9dB back-off
  ADC model: Kaiser filter where beta = 0.5
  RX filter: 5th order 5 MHz Butterworth
Options for defining the “envelope”

## Slide 11: Simulation Results
HDR |  |  |  |  | 
Example 1 [3] | -26.81 | -23.92 | -23.05 | -16.84 | -16.18
Example 2 [3] | -33.85 | -25.24 | -24.32 | -21.10 | -20.39
Example 3 [3] | -24.19 | -23.06 | -17.36 | -12.90 | -13.02
Example 4 [4] | -24.23 | -22.87 | -21.43 | -12.73 | -12.77
HDR |  |  |  |  | 
Example 1 [3] | -26.81 | -23.92 | -23.05 | -16.84 | -16.18
Example 2 [3] | -33.85 | -25.24 | -24.32 | -21.10 | -20.39
Example 3 [3] | -24.19 | -23.06 | -17.36 | -12.90 | -13.02
Example 4 [4] | -24.23 | -22.87 | -21.43 | -12.73 | -12.77
LDR |  |  |  |  | 
Example 1 [3] | -32.32 | -30.04 | -27.30 | -22.20 | -22.01
Example 2 [3] | -37.66 | -31.18 | -27.33 | -20.44 | -22.98
Example 3 [3] | -32.41 | -30.56 | -22.69 | -18.68 | -21.03
Example 4 [4] | -27.75 | -27.42 | -25.89 | -16.73 | -16.17
LDR |  |  |  |  | 
Example 1 [3] | -32.32 | -30.04 | -27.30 | -22.20 | -22.01
Example 2 [3] | -37.66 | -31.18 | -27.33 | -20.44 | -22.98
Example 3 [3] | -32.41 | -30.56 | -22.69 | -18.68 | -21.03
Example 4 [4] | -27.75 | -27.42 | -25.89 | -16.73 | -16.17
Propose using as the reference
Propose requirement: EVM(HDR)= -20 dB, EVM(LDR) = -15 dB

## Slide 12: References
[1] IEEE P802.11REMmd “Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications”, 2019
[2] “IEEE P802.11ax™/D3.0, Amendment 6: Enhancements for High Efficiency WLAN”, 2018
[3] IEEE P802.11ba/D2.0, 2019
[4] Alphan Sahin, et al., “OOK Waveform for FDMA”, IEEE 11-18/0682r2, 2018