## Slide 1: CR for CID 1115
Date: 2019-05-01
Authors:

## Slide 2: Abstract
This submission addresses CID 1115 concerning Multi-BSSID capability in 11az ranging:
Clause | Page | Line | Comment | Proposed Change
9.3.1.23.9 | 27 | 30 | The text "The TA field for the Ranging Trigger frame is address of the RSTA transmitting the Trigger frame" needs to be modified to include the case when RSTA supports MultiBSSID and intends to include STAs from different BSSes in its TB sequence/measurement window. | Add support for reception of control frames (i.e. TA/NDPA) from transmitted BSSID for the case of Multi-BSSID.

## Slide 3: Introduction
Multiple virtual co-located APs can be used to efficiently manage traffic for different sets of users.
  E.g., in an airport, use one VAP to provide unsecured connectivity for “guest” users and one VAP to provide secured connectivity for airline employees/ premium customers.
802.11 uses Multiple BSSID concept to lower Mgt frame transmissions by collocated VAPs.
This presentation discusses issues for 11az ranging with 11ax Multiple BSSID mechanism as part of the resolution to CID 1115.

## Slide 4: Recap: Multiple BSSID terminologies
Co-located BSSID set: “A collection of access points (APs) operating on the same physical device”.
Co-hosted BSSID set: “A type of co-located BSSID set such that the access points (APs) use a common operating class, channel, and antenna connectors and advertise information using multiple Beacon or Probe Response frames each corresponding to a single BSSID.”
Multiple BSSID set: A type of co-located BSSID set such that the APs use a common operating class, channel, and antenna connectors and advertise information using single Beacon or Probe Response frames by one particular BSSID (transmitted BSSID).

## Slide 5: Multiple BSSID issues for 11az
How to allow ISTAs that have associated with a nontransmitted BSSID to perform ranging with transmitted BSSID?
  Handling rx of management frames: “The STA, when associated with a BSS corresponding to a nontransmitted BSSID, shall discard all Data and Management frames that use the transmitted BSSID as the transmit address, except for Beacon, (#114)FILS Discovery, Probe Response, and TIM broadcast frames.”
  Handling Control frames (e.g., TF): is the STA able to receive and respond to TFs sent from a co-located RSTA it did not negotiate with ?
How to advertise the different ranging services for nontransmitted BSSIDs inside a Beacon or Probe Response ?
  Motivation: preserve the MultiBSSID principle of supporting different types of services at different co-located BSSIDs.

## Slide 6: Handling of Control frames
ISTAs can be either associated to some collocated BSSID as the RSTA it negotiated with or it is not.
Proposal:
  Same behavior as in 11ax for associated ISTAs => they can receive 11az Ctrl frames from transmitted BSSID if that capability was negotiated during association.
  Unassociated ISTAs can only be triggered by the BSSID they negotiated with.

## Slide 7: Handling rx of Management frames
Two possible options to handle rx of ranging related Mgt frames (i.e., LMR and FTM) at an ISTA that is associated to a non-transmitted BSSID while performing ranging with the transmitted BSSID.
Option 1: add LMR and FTM to the list of frames that ISTA shall not discard when sent from transmitted BSSID.
  Prefer this option because it preserves separation of functionalities at different BSSIDs.
Option 2: LMR and FTM frames to the ISTA transmitted with Address 2 field as the non-transmitted BSSID.
Notes: In other words, the non-transmitted BSSID support the same ranging profile as transmitted BSSID as far as this ISTA is concerned.

## Slide 8: Advertisement of ranging profiles
In 11az the Extended Capabilities element contains ranging capability information (Table 9-153 in spec).
In 11ax the Multiple BSSID element contains information about nontransmitted BSSIDs.
  Note: Some elements (e.g., HE Operation, HE Capabilities) are common to transmitted BSSID and not included.
How to signal different 11az flavors at different BSSIDs ?
  Option 1: Different Extended Capabilities element for different BSSID profiles.
    High overhead.
  Option 2: Define a new low overhead IE to contain just Ranging capabilities information of non-transmitted BSSID profiles; bit in Beacon or Probe Response to signal support for different Ranging capabilities at different BSSIDs.
    Prefer this option.

## Slide 9: Example signaling with Option 2 in slide 8
Example of new IE included within each Nontransmitted BSSID Profile subelement.
Bits | Information | Notes
<ANA> | Multiple BSSID Ranging Support | A STA sets this field to 1 to indicate support of ranging profiles at different co-located BSSIDs; set to 0 otherwise.
Extended Capabilities element
Element ID | Length | Bitmap of Nontransmitted BSSID Ranging Capabilities | Reserved
Bits: 8 8 14 2

## Slide 10: Summary
Proposed following mechanisms to support Multiple BSSID with 11az ranging:
  Add exception to an 11ax rule so as to support reception of 11az Mgt frames.
  Allow ISTAs to receive TF from transmitted BSSIDs.
  Advertise different ranging capabilities at collocated APs via a new IE included in beacon/ Probe Response frames.