## Slide 1: CR for CID 1115
Date: 2019-05-01
Authors:

## Slide 2: Abstract
This submission addresses CID 1115 concerning Multi-BSSID capability in 11az ranging:
Clause | Page | Line | Comment | Proposed Change
9.3.1.23.9 | 27 | 30 | The text "The TA field for the Ranging Trigger frame is address of the RSTA transmitting the Trigger frame" needs to be modified to include the case when RSTA supports MultiBSSID and intends to include STAs from different BSSes in its TB sequence/measurement window. | Add support for reception of control frames (i.e. TA/NDPA) from transmitted BSSID for the case of Multi-BSSID.

## Slide 3: Introduction
Multiple virtual co-located APs can be used to efficiently manage traffic for different sets of users.
  E.g., in an airport, use one VAP to provide unsecured connectivity for “guest” users and one VAP to provide secured connectivity for airline employees/ premium customers.
802.11 uses Multiple BSSID concept to lower Mgt frame transmissions by collocated VAPs.
This presentation discusses issues for 11az ranging with 11ax Multiple BSSID mechanism as part of the resolution to CID 1115.

## Slide 4: Recap: Multiple BSSID terminologies
Co-located BSSID set: “A collection of access points (APs) operating on the same physical device”.
Co-hosted BSSID set: “A type of co-located BSSID set such that the access points (APs) use a common operating class, channel, and antenna connectors and advertise information using multiple Beacon or Probe Response frames each corresponding to a single BSSID.”
Multiple BSSID set: A type of co-located BSSID set such that the APs use a common operating class, channel, and antenna connectors and advertise information using single Beacon or Probe Response frames by one particular BSSID (transmitted BSSID).

## Slide 5: Multiple BSSID issues for 11az
Handling Control frames (e.g., TF): is the ISTA able to receive and respond to TFs sent from a co-located RSTA it did not negotiate with ?
  In 11ax this support is optional and signaled to AP during association.
Handling rx of management frames: “The STA, when associated with a BSS corresponding to a nontransmitted BSSID, shall discard all Data and Management frames that use the transmitted BSSID as the transmit address, except for Beacon, (#114)FILS Discovery, Probe Response, and TIM broadcast frames.”
  Note: no LMR and FTM frames.

## Slide 6: Handling Rx of Control frames
Note: For a given pair of an ISTA and a RSTA it negotiated with, the ISTA is either associated to some collocated BSSID in the same Multiple BSSID set as the RSTA or it is not.
We list the following options.
Option 1 :
  Same behavior as in 11ax for associated ISTAs => they can receive 11az Ctrl frames from transmitted BSSID if that capability was negotiated during association.
  for Unassociated ISTAs can only be triggered by the BSSID they negotiated with.
Option 2:
  ISTAs are mandated to respond to Ranging TFs sent from transmitted BSSID for both associated and unassociated case.

## Slide 7: Handling rx of Management frames
Two possible options to handle rx of ranging related Mgt frames (i.e., LMR and FTM) at an ISTA that is associated to a non-transmitted BSSID while performing ranging with the transmitted BSSID.
Option 1: add LMR and FTM to the list of frames that ISTA shall not discard when sent from transmitted BSSID.
  Prefer this option because it preserves separation of functionalities at different BSSIDs.
Option 2: LMR and FTM frames to the ISTA transmitted with Address 2 field as the non-transmitted BSSID.
Notes: In other words, the non-transmitted BSSID support the same ranging profile as transmitted BSSID as far as this ISTA is concerned.

## Slide 8: Summary
Proposed following mechanisms to support Multiple BSSID with 11az ranging:
  Allow ISTAs to receive Ranging TF from transmitted BSSIDs.
  Add exception to an 11ax rule so as to support reception of 11az Mgt frames.

## Slide 9: Straw Poll
Do you support 11az ISTAs can always respond to TF sent from a transmitted BSSID if the ISTA has negotiated TB Ranging with some RSTA in the same Multiple BSSID set?
Y: N: Abstain:

## Slide 10: Straw Poll 2
Which Option do you support regarding handing Rx of management frames ?
Option 1:
Option 2:
None of the above:
Abstain: