## Slide 1: MCS and PPDU Format of Responding Frame
Date: 2019-05-01
Authors:

## Slide 2: Recap: Responding MCS and PPDU Format in 11baseline
Different PPDUs are allowed in one BSS:
  The legacy (duplicated) PPDU is used to carry the responding control frame if other PPDU format is not absolutely necessary, e.g.
    HT/VHT/HE PPDU when STBC is used.
    The control frame include HT/VHT variant HT Control field.
    The HE PPDU for extended range when the legacy PPDU can’t reach the TXOP holder.
The MCS, data rate of the responding frame is decided by the MCS/rate of the soliciting frame.
  Primary Rate/MCS is selected from the Basic Rate/MCS Set or the Mandatory Rate/MCS if Basic Rate/MCS Set is not known.
  Primary Rate/MCS is the maximal rate/MCS that is no more than the soliciting MCS/rate.

## Slide 3: NGV Assumption
Different PPDUs are allowed between NGV STAs:
  NGV PPDU.
  11p PPDU.
No Basic Rate/MCS Set exists.
All MCSs are mandatory.

## Slide 4: BW, PPDU Format for Responding Frame
If the TXOP responder can only reach the TXOP holder by using the NGV PPDU, the NGV PPDU is used for the responding frame. Otherwise the 11p PPDU is used for the responding frame.
The responding PPDU has the same BW as the soliciting PPDU.
  20MHz responding PPDU will be duplicated if legacy PPDU is used.
QoS Data frame
11p STA1
NVG STA2
NGV STA1
NGV STA2
Ack
10MHz NGV PPDU
10MHz 11p PPDU
11p STA3
QoS Data frame
Ack
20MHz NGV PPDU
Duplicate 11p PPDU
Ack

## Slide 5: MCS/Rate of Responding Frame
Primary rate/MCS is decided first.
  The primary MCS/Rate of the responding frame will be the maximal rate/MCS that is not higher than the MCS/Rate of the soliciting frame.
If an alternate MCS/rate exists, the alternate MCS/rate can be used instead.
  An alternate MCS/rate creates the same length of the responding PPDU as the primary rate/MCS.
  An alternate MCS/rate is more reliable than the primary rate/MCS.

## Slide 6: Straw Poll
Do you support that
  If the TXOP responder can only reach the TXOP holder by using the NGV PPDU, the NGV PPDU is used for the responding frame. Otherwise the 11p PPDU is used for the responding frame.
  The responding PPDU has the same BW as the soliciting PPDU.
    20MHz responding PPDU will be duplicated if legacy PPDU is used.
  Yes
  No
  Abstain

## Slide 7: Reference
[1]11-18/1249r1