## Slide 1: Midamble Periodicity
Date: 2019-05-13
Authors:

## Slide 2: Introduction
Midamble has been investigated as an important feature to address channel Doppler for 11bd [1, 2].
The appropriate Midmable period will depend on channel Doppler, MCS etc.
In this contribution, we present the PER and goodput results for different Midmable periods and discuss the choice of Midamble period.

## Slide 3: Midamble Periodicity
Midamble is inserted in-between data symbols to help receiver re-estimate the channel.
Periodic Midamble insertion is a straightforward design.
  Midamble symbol(s) are added after every M data symbols.
Denser Midamble can support higher Doppler and MCS. However, the Midamble overhead will offset goodput gain.
The optimal Midamble period can be chosen for each MCS and/or Doppler to achieve the highest goodput.

## Slide 4: Simulation Settings
10MHz DSRC channel @5.9GHz
CFO: uniform [-10 10]ppm on both Tx and Rx side.
Channel model: C2C channel with pure Doppler
11ac 20MHz DC2
Ideal Timing
1x1, 1ss, LDPC, 300 bytes
Midamble
  one VHT-LTF
  Periods: 2, 4, 6, 8, 10
Goodput is the maximum achievable effective data rate.
Goodput (SNR) = maxMCS,M{Rate(MCS) * (1-PER(MCS, SNR))* M/(M+1)}
    M is the midamble period

## Slide 5: Rural LOS
Low MCS can tolerate sparse Midamble, and high MCS requires denser Midamble

## Slide 6: Urban Approaching LOS
Low MCS can tolerate sparse Midamble, and high MCS requires denser Midamble

## Slide 7: Urban Crossing NLOS
Low MCS can tolerate sparse Midamble, and high MCS requires denser Midamble

## Slide 8: Highway LOS
Low MCS can tolerate sparse Midamble, and high MCS requires denser Midamble

## Slide 9: Highway NLOS
Low MCS can tolerate sparse Midamble, and high MCS requires Midamble period of 2 or 4..

## Slide 10: Rural LOS

## Slide 11: Urban Approaching LOS

## Slide 12: Urban Crossing NLOS

## Slide 13: Highway LOS

## Slide 14: Highway NLOS

## Slide 15: Discussions
Simulations confirms that the optimal Midamble period is dependent on both MCS and channel.
The choice of Midamble period may need to consider:
  In OCB communications, transmitters may not have accurate Tx-Rx relative Doppler information.
  For high-Doppler environments (Highway), highest MCS may not be used in practice.
  Fix Midamble period can simplify Midamble design and limit PHY signal overhead.

## Slide 16: Reference
[1] Rui Cao and etc., “Potential PHY Designs for NGV”, IEEE 802.11-19/0016r0.
[2] Dongguk Lim and etc., “Consideration on Features for 11bd”, 802.11-19/0009r0.

## Slide 17: Straw Poll 1
Do you agree that 11bd PPDU shall define single Midamble period value for all MCS?
Y:
N:
A: