## Slide 1: 11bd MCS Discussions
Date: 2019-05-13
Authors:

## Slide 2: Introduction
In previous meetings, various PHY features have been discussed in several contributions [1, 2, 3].
In the context of BSS (OCB) networks, all PHY features/modes will be mandatory for each STA.
It is beneficial to limit the PHY features/mode possibilities for 11bd products.
In this contribution, we will discuss the support of MCS-related PHY features for 11bd.

## Slide 3: 11bd Modulation Choice
11p supports up to 64QAM with rate ¾.
Higher modulation order is a simple way to boost PHY throughput.
Simulations [1, 4] show that 256QAM rate ¾ provide prominent goodput gain under C2C Doppler channel.
Propose for 11bd to support 256QAM rate 3/4, using the same constellation mapping as 802.11ac.
Suggest to remove support of 4.5Mbps (BPSK ¾) for 11bd 10MHz.

## Slide 4: 11bd LDPC Design
In March meeting, LDPC became the mandatory coding scheme in 11bd for sensitivity and throughput improvements [1].
802.11n LDPC codes have been implemented in WiFi products and show good performance.
Adopting 802.11n LDPC code can facilitate fast 11bd product roll-out by leveraging existing WiFi products.
Since there are NO optional features, 11bd may consider supporting only LDPC for data encoding.

## Slide 5: Number of Spatial Streams
In OCB networks, STA can NOT claim its capability of maximum supported number of streams.
Support of multi-stream can be challenging in vehicular environments.
Explicit beamforming may also not be practical
  CSI @ Tx needs a sounding-feedback exchange

## Slide 6: Straw Poll 1
Do you agree to add the following text into Section 3 of SFD?
  “NGV PPDUs shall support 256 QAM with coding rate ¾. The 256 QAM constellation mapping is the same as in 21.3.10.9 (Constellation mapping)”
Y:
N:
A:

## Slide 7: Straw Poll 2
Do you agree to add the following text into Section 3 of SFD?
  “NGV PPDUs shall support LDPC code, with the same coding method as defined in 19.3.11.7 (LDPC Codes)”
Y:
N:
A:

## Slide 8: Straw Poll 3
Do you agree that 11bd PPDU data encoding only supports LDPC?
Y:
N:
A:

## Slide 9: Straw Poll 4
Do you agree that 11bd only supports single spatial stream?
Y:
N:
A:

## Slide 10: Reference
[1] Rui Cao and etc., “Potential PHY Designs for NGV”, IEEE 802.11-19/0016.
[2] Dongguk Lim and etc., “Consideration on Features for 11bd”, IEEE 802.11-19/0009.
[3] Yujin Noh and etc., “PHY Designs for NGV”, IEEE 802.11-19/0293.
[4] Prashant Sharma and etc., “PHY Numerology Discussions”, IEEE 802.11-19/0686.