## Slide 1: Investigating the Compliance of Wireless Units with regulatory and normative requirements
Date: 2019-05-14
Authors:
Name | Affiliation | address | Phone | email
Dr. Ammar Alhosainy | Carleton University | Department of Systems and Computer Engineering, Carleton University, Ottawa, Ontario, K1S 5B6, Canada | +1(613)400-8824 | amammar@sce.carleton.ca
Kareem Attiah |  |  |  | kareemattiah@sce.carleton.ca
Shady Alkamhawy |  |  |  | shadyelkamhawy@cmail.carleton.ca
Dr. Ahmad Altalabi |  |  |  | ahmadaltalabi@cmail.carleton.ca
Dr. Mohamed Aslan |  |  |  | maslan@sce.carleton.ca
Trevor Gamblin |  |  |  | tvgamblin@gmail.com
Prof. Ramy Gohary |  |  |  | gohary@sce.carleton.ca
Prof. Ioannis Lambadaris |  |  |  | ioannis@sce.carleton.ca

## Slide 2: Goal
Investigate the compliance of the IEEE 802.11 units according to
ETSI EN 301 893 v2.1.1 and proposing a novel Compliance Metric
Agenda
  Hardware Setup
  IEEE 802.11 medium access standard
  ETSI EN 301 893 based Compliance Check
  Proposed Compliance Metric (MC)
  Hardware and Software evolution
  Available resources and Test requirements
  Demo

## Slide 3: Guidance
Throughout the experiment steps, procedures, and comparisons we follow:
  European Telecommunications Standards document [1]
  The IEEE standards 802.11-2016 [2] and 802.11-2012 [3]

## Slide 4: Hardware Setup
UUT
SU/CD
USRP
PC/Laptop
RF Splitter/ Combiner
Client
Server
RF Splitter/ Combiner
Universal Software Radio Peripheral (USRP)
Unit Under Test (UUT)
Signaling Unit/Companion Device (SU/CD)

## Slide 5: Hardware Setup
Universal Software Radio Peripheral (USRP)
Unit Under Test (UUT)
Signaling Unit/Companion Device (SU/CD)
USRP (NI-B200):
  Sampling Rate: 20 × 106 samples/s (Reading error < 50 ns)
IEEE 802.11 Channel 36 (20 MHz)
  Center frequency is 5.18 GHz
Testing Traffic
  iperf, 100 Mb/s (Full buffer condition)
  UDP (Unidirectional traffic)
  iperf -c [IP] -u -b100M -S 0x00
  (Type Of Service TOS, or DSCP)
UUT
SU/CD
USRP
PC/Laptop
RF Splitter/ Combiner
Client
Server
RF Splitter/ Combiner

## Slide 6: USRP
Coverage frequency of 70 MHz to 6 GHz
56 MHz bandwidth
Up to 61.44 MSample/s quadrature (IQ components)
USB 3.0 connection
USRP B200 SDR Kit

## Slide 7: USRP output
Data
ACK/BA
Time (ms)
IQ signal magnitude

## Slide 8: Interframe spaces

## Slide 9: The X duration histogram
16 𝜇𝑠
4
34 𝜇𝑠
9𝜇𝑠
16
43 𝜇𝑠
9 𝜇𝑠

## Slide 10: IEEE 802.11 Interframe Spaces
Source: Next Generation Wireless LANs, 802.11n and 802.11ac, Cambridge University Press 2008, 2013
Short Interframe Space (SIFS)
  Associated with ACK, BA, and CTS
  For legacy, HT, and VHT IEEE 802.11
    SIFS = 16 μs
DCF Interframe Space (DIFS)
  Associated with Data and RTS
  DIFS = SIFS + 2 × slotTime
  For Legacy, HT, and VHT IEEE 802.11
    slotTime = 9 μs, DIFS = 34 μs

## Slide 11: Distributed Coordination Function (DCF)
Source: Next Generation Wireless LANs, 802.11n and 802.11ac, Cambridge University Press 2008, 2013
Data Transmission Mechanism (CSMA/CA)
  Sense the medium for a DIFS duration
  Backoff for (n × slotTime), n is a uniform RV ~ [0, CW], initial CW = 15

## Slide 12: Enhanced Distributed Channel Access (EDCA)
Extension of DCF, introduced in 802.11e
Support prioritized QoS
  Transmission Opportunity (TXOP)
  Arbitration Interframe Space (AIFS)

## Slide 13: Enhanced Distributed Channel Access (EDCA)
Transmission Opportunity (TXOP)
Access Category (AC) | CWmin | CWmax | AIFSN | TXOP/2012 | TXOP/2016
Background (AC_BK) | 15 | 1023 | 7 | 0 | 2.528 ms
Best Effort (AC_BE) | 15 | 1023 | 3 | 0 | 2.528 ms
Video (AC_VI) | 7 | 15 | 2 | 3.008 ms | 4.096 ms
Voice (AC_VO) | 3 | 7 | 2 | 1.504 ms | 2.080 ms
Legacy DCF | 15 | 1023 | 2 | 0 | 0
Source: Next Generation Wireless LANs, 802.11n and 802.11ac, Cambridge University Press 2008, 2013
Table 9-137 in [2] and Table 8-105 in [3]
SIFS = 16 𝜇𝑠
n = 0 to 3
TXOP

## Slide 14: Enhanced Distributed Channel Access (EDCA)
  Arbitration Interframe Space (AIFS)
  AIFS = SIFS + AIFSN × slotTime
Source: Next Generation Wireless LANs, 802.11n and 802.11ac, Cambridge University Press 2008, 2013
Access Category (AC) | CWmin | CWmax | AIFSN | TXOP/2012 | TXOP/2016
Background (AC_BK) | 15 | 1023 | 7 | 0 | 2.528 ms
Best Effort (AC_BE) | 15 | 1023 | 3 | 0 | 2.528 ms
Video (AC_VI) | 7 | 15 | 2 | 3.008 ms | 4.096 ms
Voice (AC_VO) | 3 | 7 | 2 | 1.504 ms | 2.080 ms
Legacy DCF | 15 | 1023 | 2 | 0 | 0
Table 9-137 in [2] and Table 8-105 in [3]
AIFS[AC_VO] = 34 µs
AIFS[AC_VI] = 34 µs
AIFS[AC_BE] = 43 µs
AIFS[AC_BK] = 79 µs

## Slide 15: Reading the X histogram (Voice and Best Effort traffic)
16 𝜇𝑠
n ∊ [0 … 3]
34 𝜇𝑠
9𝜇𝑠
AIFS[BE] = 43 𝜇𝑠
9𝜇𝑠
TXOP > 0
Access Category (AC) | CWmin | CWmax | AIFSN | TXOP/2012 | TXOP/2016
Background (AC_BK) | 15 | 1023 | 7 | 0 | 2.528 ms
Best Effort (AC_BE) | 15 | 1023 | 3 | 0 | 2.528 ms
Video (AC_VI) | 7 | 15 | 2 | 3.008 ms | 4.096 ms
Voice (AC_VO) | 3 | 7 | 2 | 1.504 ms | 2.080 ms
Legacy DCF | 15 | 1023 | 2 | 0 | 0
Voice
Best Effort
n ∊ [0 … 15]

## Slide 16: Reading the X histogram (Video & Background traffic)
n ∊ [0 … 7]
AIFS[BK] = 79 𝜇𝑠
9 𝜇𝑠
TXOP > 0
Access Category (AC) | CWmin | CWmax | AIFSN | TXOP/2012 | TXOP/2016
Background (AC_BK) | 15 | 1023 | 7 | 0 | 2.528 ms
Best Effort (AC_BE) | 15 | 1023 | 3 | 0 | 2.528 ms
Video (AC_VI) | 7 | 15 | 2 | 3.008 ms | 4.096 ms
Voice (AC_VO) | 3 | 7 | 2 | 1.504 ms | 2.080 ms
Legacy DCF | 15 | 1023 | 2 | 0 | 0
Video
Background
n ∊ [0 … 15]

## Slide 17: Analyzing compliance with Harmonized Standard (HS) ETSI EN 301 893
According to ETSI EN 301 893 [1]:
  Classify the silent periods and sort them into a set of bins
    Example: Access category (Video)

## Slide 18: Standard Compliance Check 1, steps
According to ETSI EN 301 893 [1]:
  Convert periods count in each bin into a probability
  Accumulate bin probabilities, compare with the upper threshold
Compliant
so far

## Slide 19: Standard Compliance Check 2, steps
According to ETSI EN 301 893 [1]:
  4. Measure the Channel Occupancy Time (COT) = TXOP:
Access Category (AC) | Max COT
Class 1, Background (AC_BK) | 6.00 ms
Class 2, Best Effort (AC_BE) | 6.00 ms
Class 3, Video (AC_VI) | 4.00 ms
Class 4, Voice (AC_VO) | 2.00 ms
Source: Next Generation Wireless LANs, 802.11n and 802.11ac, Cambridge University Press 2008, 2013

## Slide 21: Example product 1: Ericsson AP6321
UUT: Ericsson AP (AP6321), IEEE 802.11n, 5 GHz
Configurations:
All default configurations except:
Channel number 153
Channel bandwidth 20 MHz

## Slide 22: Example product 1: Ericsson AP6321
Priority Class:
Video
Priority Class:
Voice
COT (TXOP) Result (Limit) =
1.638 ms (2.0 ms)
COT (TXOP) Result (Limit) =
3.035 ms (4.0 ms)

## Slide 23: Example product 1: Ericsson AP6321
Priority Class:
Best Effort
Priority Class:
Background
COT (TXOP) Result (Limit) =
3.875 ms (6.0 ms)
COT (TXOP) Result (Limit) =
3.875 ms (6.0 ms)

## Slide 24: Example product 2: D-Link DIR-822
UUT: D-Link AP (DIR-822), 802.11n, 5 GHz
Configurations:
All default configurations except:
Channel number 153
Channel bandwidth 20 MHz

## Slide 25: Example product 2: D-Link DIR-822
Priority Class:
Voice
COT (TXOP) Result (Limit) =
2.0751 ms (2.0 ms)
Priority Class:
Video
COT (TXOP) Result (Limit) =
5.8287 ms (4.0 ms)

## Slide 26: Example product 2: D-Link DIR-822
Priority Class:
Background
Priority Class:
Best Effort
COT (TXOP) Result (Limit) =
3.316 ms (6.0 ms)
COT (TXOP) Result (Limit) =
0.9421 ms (6.0 ms)

## Slide 27: Maximum TXOP duration of various products compared to limits permitted in EN 301 893

## Slide 28: Summary of the Results
 | Voice |  | Video |  | Best Effort |  | Background | 
 | COT/TXOP [ms] | Bin Prob. | COT/TXOP [ms] | Bin Prob. | COT/TXOP [ms] | Bin Prob. | COT/TXOP [ms] | Bin Prob.
EN 301 893 COT/TXOP max limit | 2.0 |  | 4.0 |  | 6.0 |  | 6.0 | 
Ericsson AP (AP6321) | 1.4103 | passed | 3.0344 | passed | 0.3361 | passed | 3.8752 | passed
BelAir AP (20E-11R) | 3.9053 | passed | 3.9071 | passed | 3.9072 | passed | 3.9072 | passed
Asus AP (RT-AC68U) | 1.7486 | passed | 15.794 | passed | 15.079 | failed | 15.551 | failed
D-Link AP (DIR-822) | 2.0751 | passed | 5.8287 | passed | 3.316 | failed | 0.94215 | passed
TP-Link AP (Archer C50) | 23.697 | passed | 21.552 | passed | 20.23 | failed | 19.41 | failed
Asus USB client (USB-N53) | 2.9589 | passed | 4.2743 | passed | 1.6221 | passed | 0.2791 | passed
Cisco USB client (WUSB600N) | 2.8468 | passed | 4.4709 | passed | 1.6971 | passed | 0.3685 | passed
D-Link USB client (DWA-160) | 2.8933 | passed | 4.4271 | passed | 1.4715 | passed | 0.3006 | passed
EDIMAX USB client (EW-7822UAC) | 2.9308 | passed | 4.4579 | passed | 1.6079 | passed | 0.9454 | passed

## Slide 29: Compliance Metric
Geometric mean of three sub-factors
Backoff Random Number Distribution Factor
Kullback-Leibler divergence (0 to 1)
TXOP Factor
Ratio of TXOP violation (0 to 1)
Aggressiveness/Submissiveness Factor
Tendency of violation (-1 to 1)
Compliance Metric is a percentage (0 % to 100 %)
100 % = fully compliant

## Slide 30: Compliance Metric

## Slide 31: Hardware Evolution (First version: RF shielding box)
UUT
SU/CD
USRP
Server 1
Server 2
RF Shielding Box
RF shielding box
2 servers

## Slide 32
Server 1
Server 2
UUT
SU/CD
USRP
RF Splitter/ Combiner
RF Cables
2 servers
Hardware Evolution (Second version)

## Slide 33
UUT
SU/CD
USRP
PC/Laptop
Client
Server
RF cables
One Laptop
Hardware Evolution (Current version: Single Machine)

## Slide 34: Results Comparisons
Measurements in RF Shielding box
Cabled measurements

## Slide 35: Software Evolution—1st ver.: MATLAB & Python script

## Slide 36: Software Evolution—Reimplementation in Python Introducing a GUI, no need for MATLAB license

## Slide 37: Results Comparisons
MATLAB based evaluation code
Python based evaluation code

## Slide 38: Open Source code stored on GitHub: CarletonWirelessLab/ANTS, available under MIT license
https://github.com/CarletonWirelessLab/ANTS
https://github.com/CarletonWirelessLab

## Slide 39: Example requirements
Standard PC
  CPU of Intel Core i5 class
    >1.7 GHz recommended
  USB3 support needed
  8 GB RAM, better 16 GB RAM
  Disk space > 20 GB
  1.5 GB / measurement
Ubuntu Linux 16.04
  Python 3 environment
  GNUradio
USRP B200
IEEE 802.11 client
  Companion device
RF cables and splitter
  Attenuators might be helpful
Detailed requirements and Software installation steps are found on GitHub
https://github.com/CarletonWirelessLab/ANTS

## Slide 40: Outlook
Further simplification of tests
  “One-button solution”
  Automatic generation of PDF files containing evaluation reports
Public database containing measurement reports
Testing of device compliance with IEEE 802.11a preamble
  IEEE 802.11a RATE and LENGTH in SIGNAL field indicating deferral duration
  Sensitivity at related power threshold
  To become mandatory with next revision of EN 301 893

## Slide 41: Published Papers
Journal Paper:
  “Statistical Evaluation of the Behavior of 5 GHz Radio LAN Devices”
    IEEE Transactions on Instrumentation and Measurement, Early access on IEEE explore
Conference Papers:
  “Compliance Evaluation of Wi-Fi Devices”
    The 20th IEEE International Workshop on Signal Processing Advances in Wireless Communications (SPAWC 2019), (SPAWC 2019), Cannes, France, July 2-5, 2019
  “A Soft Metric for Assessing the Compliance of WLAN Devices”
    16th Canadian Workshop on Information Theory (CWIT 2019), Hamilton, ON, Canada, June 2-5, 2019

## Slide 42: Demo!

## Slide 43
Thank you

## Slide 44: References
[1] ETSI EN 301 893 (V2.1.1), “5 GHz RLAN; Harmonised Standard covering the essential requirements of article 3.2 of Directive 2014/53/EU,” European Telecommunications Standards Institute, ETSI EN 301 893 V2.1.1, May 2017.
[2] “IEEE Approved Draft Standard for Information technology—Telecommunications and information exchange between systems - Local and metropolitan area networks—Specific requirements Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications,” in IEEE P802.11-REVmc/D8.0, August 2016, pp.1-3774, Jan. 1 2016.
[3] “IEEE Standard for Information technology—Telecommunications and information exchange between systems Local and metropolitan area networks—Specific requirements Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications,” in IEEE Std 802.11-2012 (Revision of IEEE Std 802.11-2007), pp.1-2793, March 29 2012.
[4] Eldad Perahia and Robert Stacey (2013), “Next Generation Wireless LANs 802.11n and 802.11ac,” Cambridge, Cambridge University.