## Slide 1: LMR Immediate and Delayed Feedback
Date: 2019-05-01
Authors:

## Slide 2: Background
LRM Timestamp Feedback
  Immediate (from this measurement phase)
  Delayed (from the preceding measurement phase)
ToA Feedback Type
  Phase shift feedback (average linear phase based)
  Firstpath feedback (based on the first path ToA)
LMR Direction
  RSTA-to-ISTA
  ISTA-to-RSTA

## Slide 3: Current Draft
Ranging Parameters
  One indication immediate/delayed
  If ISTA-to-RSTA present assumed same as RSTA-to-ISTA
  ToA feedback type (always immediate -> overwrites other indication)
Example
  “Delayed” feedback
  RSTA-to-ISTA feedback type “phase shift” -> immediate
  ISTA-to-RSTA present, feedback type “Firstpath” -> delayed

## Slide 4: Options
Allow for delayed phase shift feedback?
  If yes -> need two bits
Allow for RSTA-to-ISTA LMR be different from ISTA-to-RSTA?
  If yes -> needs two bits
Otherwise fine as is

## Slide 5: Strawpoll I
Allow for delayed phase shift feedback?
  Yes
  No
  Abstain

## Slide 6: Strawpoll II
Allow for RSTA-to-ISTA LMR be different from ISTA-to-RSTA?
  Yes
  No
  Abstain