## Slide 1: 20MHz Channel Usage in 11bd
Date: 2019-05-14
Authors:
Onn Haran, Autotalks

## Slide 2: Primary channel transmission is subject to adjacent channel interferences of non-primary channel
Communication ranges of both primary and non-primary channels are degraded when originated from different devices
  The energy of non-primary channel is strong (> -72dBm) otherwise it wouldn’t have been detected
  Communication range in presence of such strong adjacent channel is decreased (based on [3])
  Interference can be mitigated by deferring transmission till adjacent channel is idle ([3])
Scenario of primary channel transmission
From [1]

## Slide 3: Primary and Secondary channel selection
Assumption: The 10MHz channels, part of 20MHz channel, are barely used
  In other words, usage of CH 174 and CH 176 is rare, and so is usage of CH 180 and CH 182
  In most cases, 20MHz service can be activated without observing any activity in sub 10MHz channels
  The usage of those 10MHz channels (174/176/180/182) is likely be regional without clear nationwide guidance
  No way to know in advance which of the channels is primary and which is secondary
  All stations should maintain consistent Primary and Secondary channel definition

## Slide 4: Secondary Channel service is not as fair as Primary Channel service in presence of 20MHz
  Secondary Channel detection level is higher (-72dBm) than primary channel (-82dBm)
  It should be remembered that Secondary Channel detection was tested only on non-V2V channels
  Detection scheme might still work with long delay spread but it has to be retested with V2V channels

## Slide 5: Suggestion: Sub-channel transmission should not be allowed
20MHz channel transmission should be deferred when either primary or secondary channel are not idle
  20MHz channel shall not transmit in 10MHz sub-channels, and shall not receive packets in 10MHz sub-channels
  20MHz co-exists with both 10MHz sub-channels
  Service in 20MHz channel doesn’t interoperate with services in 10MHz sub-channels
Busy
Sub-channel 10 MHz
Sub-channel 10 MHz
Busy
20MHz TX

## Slide 6: Possible 10MHz Roles
Primary / Secondary roles | Implementation | Pros | Cons
Pre-configured roles | NAV in primary channel and energy detection in secondary channel | Simple and legacy implementation | Since it is not possible to know which channels would be active, primary or secondary, sharing with 10MHz channel, in case existing, would be problematic
Dynamic roles | NAV in first detected channel, and energy detection in both channels | Relatively low complexity Works well when one of the channels is used | Lower fairness in case the two channels are used
No roles | NAV in both channels | Highest fairness and robustness | High complexity design, duplicating most of the receiver

## Slide 7: Straw Poll #1
Do you agree to add the following text into Section 3 of SFD?
802.11bd 20MHz channel shall have an option to be used as a whole, without transmitting or receiving in single 10MHz sub-channel
Y: 2
N: 14
A: 17
May 2019
Onn Haran, Autotalks

## Slide 8: Straw Poll #2
Which of the scheme is preferred for 10MHz channel roles definition?
1. Pre-configured roles: 1
2. Dynamic roles: 11
3. No roles: 6
A: 18
May 2019
Onn Haran, Autotalks

## Slide 9: References
  [1] 20MHz Channel Access in 11bd (IEEE802.11-19-366/r2)
  [2] Enhanced CCA for Non-Primary Channels Using Guard Interval (IEEE802.11-10-12/r0)
  [3] Simulation of Multi-channel Interference (IEEE802.11-19-320/r2)
May 2019
Onn Haran, Autotalks