## Slide 1: 11ax Evaluation Mobility
Date: 2019-07-15
Authors:

## Slide 2: Abstract
In this contribution, we present the preliminary results of 11ax simulations on mobility in Dense Urban eMBB scenario.
The simulations adhere to the methodology specified by ITU-R for self-evaluating a RAT for IMT-2020 [1].
The preliminary results show that 11ax can meet the ITU requirements on mobility in Dense Urban eMBB scenario[2].
Notes: Here is the abstract.

## Slide 3: Abbreviation
RIT ( Radio Interface Technology)
URLLC（Ultra-Reliable and Low Latency Communications）
eMBB（enhanced Mobile Broadband）
mMTC (massive Machine Type Communication)
NSA（Non-Standalone ）

## Slide 4: Outline
Objective
Simulation Configuration
Simulation Assumption
Mobility Simulation Results
Mobility Interruption Time Analysis
Control Plane Latency Analysis
Conclusion
Next Step
References

## Slide 5: Simulation Configuration
Simulation bandwidth : 20 MHz
Carrier Frequency: 4GHz
BS Tx power : 49 dBm, UE Tx power: 23 dBm
BS Antenna gain: 8 dBi, UE antenna gain: 0 dBi
BS noise figure: 5 dB, UE noise figure : 7 dB
BS antenna configuration : dual polarization 8Rx with 8 dBi gain in intended direction.
UE antenna configuration : 1Tx with with 0 dBi gain.
The complete configuration is specified in the ITU-R guidelines for self-evaluating a RAT ([2]).

## Slide 6: Simulation Assumptions
TCH Payload : 1500 Byte
BPSK, QPSK, 16QAM, 64QAM
LDPC, 1/2, 2/3, 3/4, 5/6 code rate
single spatial stream
Midamble periodicity in number of OFDM symbols is 10/20
Channel estimation based on L-MMSE channel estimation
Maximum Ratio Combining
LDPC decoding

## Slide 7: Minimum Requirements
The minimum requirements of mobility in [3] are quoted as follows

## Slide 8: Simulation Procedure (1)
The mobility simulation procedure is quoted as follows [2]
Step 1: Run uplink system-level simulations, identical to those for average spectral efficiency, and 5th percentile user spectral efficiency except for speeds taken from Table 4 of Report ITU-R M.2410-0, using link-level simulations and a link-to-system interface appropriate for these speed values, for the set of selected test environment(s) associated with the candidate RITs/SRITs and collect overall statistics for uplink SINR values, and construct CDF over these values for each test environment.
Step 2: Use the CDF for the test environment(s) to save the respective 50th-percentile SINR value.

## Slide 9: Simulation Procedure (2)
Step 3: Run new uplink link-level simulations for the selected test environment(s) for either NLOS or LOS channel conditions using the associated speeds in Table 4 of Report ITU‑R M.2410‑0, as input parameters, to obtain link data rate and residual packet error ratio as a function of SINR. The link-level simulation shall use air interface configuration(s) supported by the proposal and take into account retransmission, channel estimation and phase noise impact.
Step 4: Compare the uplink spectral efficiency values (link data rate normalized by channel bandwidth) obtained from Step 3 using the associated SINR value obtained from Step 2 for selected test environments, with the corresponding threshold values in the Table 4 of Report ITU-R M.2410-0.
Step 5: The proposal fulfils the mobility requirement if the spectral efficiency value is larger than or equal to the corresponding threshold value and if also the residual decoded packet error ratio is less than 1%, for all selected test environments. For the selected test environment it is sufficient if one of the spectral efficiency values (using either NLOS or LOS channel conditions) fulfils the threshold.

## Slide 10: Simulation Results – channel estimation
MCS1: QPSK,1/2 code rate
Midamble periodicity:20
channel estimation: L-MMSE VS linear interpolation

## Slide 11: Simulation Results – 30 km/h
Midamble periodicity: 10/20
Median SINR: 5.65dB@30km/h
Spectral Efficiency at 2.9dB is 1.71/1.92 bit/s/Hz > 1.12 bit/s/Hz

## Slide 12: Simulation Results – 120 km/h
Midamble periodicity: 10/20
Median SINR: 4.6dB@120km/h
Spectral Efficiency at 2.9dB is 1.17/1.35 bit/s/Hz > 0.8 bit/s/Hz

## Slide 13: Conclusion
The evaluation results show that 11ax can meet the requirements of mobility in Dense Urban eMBB scenario of IMT-2020

## Slide 14: Reference
[1] Report ITU-R M.2412-0 (10/2017), Guidelines for evaluation of radio interface technologies for IMT-2020
[2] Report ITU-R M.2410-0 (11/2017), Minimum requirements related to technical performance for IMT-2020 radio interface(s)
[3] Report ITU-R M.2411-0 (11/2017) , Requirements, evaluation criteria and submission templates for the development of IMT-2020