## Slide 1: IEEE 1609 / 802.11 Joint Session
Date: 2019-05-07
Authors:
Name | Affiliation | Address | Phone | Email
Justin McNew | JMC Rota Inc., IEEE 1609 Vice Chair | STE 705 PMB 154 3830 Valley Centre Dr. San Diego, CA 92130 | 310 922 4923 | justinm@jmcrota.com

## Slide 2: IEEE 1609 / SAE Standards Overview
Applications / higher layers interface to IEEE 1609

## Slide 3: 1609-Compliant Protocol Stack
802.11 is used in “OCB mode”
  Bypasses traditional 802.11 association to reduce latency
    What PHY features from 802.11ac/ax are available without association?
  Security is implemented on MSDUs above the MAC
    Layer 2 security is not used (addressed by IEEE 1609.2)
Note: 1609.2 security services do not
interface with the 802.11 MLME or PLME

## Slide 4: 1609.4: Historical Purpose
Develop the channel coordination features required by industry to utilize the complete frequency band (5.850 GHz to 5.925 GHz)
  Control channel / service channel approach, with dedicated safety channels
Hide the complexity of channel switching from application developers
Avoid modifying the MA-UNITDATA.request
  At the time of 802.11p, modifying this primitive was not considered an option

## Slide 5: 1609.4 Management and Data SAPs / Primitives
Conceptually…
MLMEX – management SAP used to manage the MLME in the context of channel switching
MA-UNITDATAX – data SAP used to abstract the power, rate and channel controls from the existing MAC SAP and route them through the MLMEX to the MLME

## Slide 6: 1609.4 and 802.11-2012 Primitives Comparison
IEEE 1609.4
MA-UNITDATAX.request (
source address,
destination address,
routing information,
data,
priority,
service class,
Channel Identifier,
Time Slot,
Data Rate,
TxPwr_Level,
ExpiryTime
)
IEEE 802.11
MA-UNITDATA.request (
source address,
destination address,
routing information,
data,
priority,
service class
)
The channel switching features are “out of band” from the MAC data SAP and abstracted by the MLMEX

## Slide 7: How we did it…
Implementers generally modified MAC firmware to combine the 1609.4 multi-channel operation with traditional 802.11 functionality
Examples: broadcast or data collection applications
  WAVE Short Message used for broadcast messages
  WAVE Service Advertisement (WSA) used to announce a service
    Just another MSDU from the MAC’s perspective
DSRC
(802.11p + 1609)
DSRC
(802.11p + 1609)

## Slide 8: Next Generation V2X “Desirements”
IEEE 1609 supports the V2X direction of 802.11 TGbd
Packet-by-packet features of interest for the MA-UNITDATA.request
  Selectable data rate and power
  Selectable mode(s)
    E.g. legacy and “NGV” mode (other modes?)
Operating mode(s) features of interest
  Upper layers choose legacy or NGV mode (pre-configured through MLME)
  Let MAC / PHY choose which mode based on observed preambles / SIGNAL
Other potential features improvements
  MAC address change feature extensions might be useful
    MLME-RESET was originally used for MAC address randomization (with a 2-TU time limit for a reset in 802.11p)
    Locally administered random MAC address is currently used
  Others?