## Slide 1: LC MAC submission
Date: 2019-05-13
Authors:
Name | Affiliation | Address | Phone | Email
Suhwook Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | suhwook.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com

## Slide 2: Abstract
This submission is response of call for proposal [1]
We will address a number of issues for designing the LC MAC
Detail MAC proposal will be submitted in July meeting

## Slide 3: 11bb MAC
When we design MAC layer for LC, there are two most important documents we should consider
  PAR document [2]
  Usage model document [3]
So, we will focus on these two documents and address possible MAC features which are related with two documents

## Slide 4: PAR document
5.2.b Scope of the project: This amendment specifies a new PHY layer and modifications to the IEEE 802.11 MAC that enable operation of wireless light communications (LC)
  (PHY description)
  This amendment specifies changes to the IEEE 802.11 MAC that are limited to the following:
    1) Hybrid coordination function (HCF) channel access,
    2) Overlapping basic service set (OBSS) detection and coexistence,
    3) Existing power management modes of operation (excluding new modes), and modifications to other clauses necessary to support these changes.

## Slide 5: 1st MAC item in PAR: HCF channel access
Before we design channel access for LC, followings are needed to be addressed
  Light waves have a strong straightness so that carrier sensing sometimes may not work well
  STAs cannot be heard from each other, which can lead to collision at UL transmission
So we can consider contention-free access scheme which is managed by the AP
  IEEE 802.11ad/ay defines contention-free access scheme (SP access) which is allocated by AP
  IEEE 802.15.7/13 defines contention-free period

## Slide 6: HCF channel access
However, EDCA is also required for non-AP STA to support some operations which may not be fully managed by the AP
  Scanning/discovery
  BSS initial access
  UL urgent transmission
  Handover
  Etc..
Besides, all legacy 802.11 AP/STA are implemented with EDCA, so we can reuse easily

## Slide 7: 2nd MAC item in PAR: OBSS detection and coexistence
IEEE 802.11 standard family defines followings to handle OBSS
  Fast BSS transition defined by 11r
  OBSS management defined by 11aa
  BSS color defined by 11ah
  Fast initial link setup defined by 11ai
  Spatial reuse by defined 11ax

## Slide 8: LC OBSS
BSS color can be easily adopted in LC
However, the others seem complicate that they may be unlikely to be adopted in LC MAC
Also we may need a LC oriented handover operation for supporting mobility in LC networks

## Slide 9: 3rd MAC item in PAR: Power Management
We have several existing power saving features in baseline spec as follows
  PSM, PSP, U-APSD [4]
  TWT [5]
TWT which is firstly defined in 11ah has been enhanced by 11ax and considered as main feature of power save
  TWT consists individual TWT and broadcast TWT
  Individual TWT is mandatory in Wi-Fi 6

## Slide 10: Power Management
It would be reasonable that we adopt TWT as a main power management in LC
Even though TWT is main feature of power save, we have to investigate whether TWT is appropriate for LC because it is quite complicate
  We may revise TWT or adopt some parts of TWT if needed
  We may consider individual TWT first, and then move to broadcast TWT

## Slide 11: Additional items for Usage model
In addition to the PAR document, there are several other items that we should consider regarding the Usage document
  Interference management
  Mobility
  Transmit power control
  QoS support

## Slide 12: Interference management & Mobility
Interference management
  Usage model 1, 3, and 4 assume high levels of LC-OBSS interference
  Non-LC interference (from sunlight, artificial-light, etc.) and LC-P2P interference shall also be considered
Mobility
  STAs can move in Usage model 1 and 3
So we may needs cooperation between APs to handle OBSS interference and support mobility

## Slide 13: Transmit power control & QoS support
Transmit power control
  Both AP and STA need to support variety of illuminance levels
  Recommended illuminance varies from 50 to 160k lux
  Distance between AP and STA ranges from 3 ~ 20 meters
QoS support
  LC has to support QoS traffic such as Video, Audio, Teleconference, etc.
  Each traffic type has different maximum throughput, latency, reliability requirement
We may reuse TPC and QoS support feature which are defined in the latest 802.11 spec

## Slide 14: IEEE 802.11ax
11ax is a state-of-the-art system in 802.11 standard family and it defines following new features
  OFDMA
  Spatial Reuse
  UL MU-MIMO
  Trigger based access

## Slide 15: IEEE 802.11ax MAC adaptation
Most of the 11ax MAC features are based on multi-user operation
  Even though we don’t take MU operation into account, OFDMA and trigger based access can be useful to allocate TXOP to STA by AP
  Also we may revise OFDMA for single user
  SR and UL MU-MIMO do not seem to fit LC

## Slide 16: Summary
We addressed and reviewed several MAC features for designing LC MAC
  Channel access, OBSS, Power management (PAR document)
  Interference management, Mobility, Transmit power control, QoS support (Usage document)
  OFDMA, Spatial Reuse, UL MU-MIMO, Trigger based access (11ax)
We may reuse the mentioned features as much as possible
  However, we may have to revise them according to the characteristic of light communication
It will be proposed in July meeting what features will be modified and incorporated into the LC

## Slide 17: References
[1] 11-18-2039-03-00bb-tgbb-call-for-proposals.doc
[2] 11-17-1604-10-00lc-a-par-proposal-for-light-communications.pdf
[3] 11-18-1109-05-00bb-lc-usage-model-document.pptx
[4] 11-14-1161-03-00ax-parameters-for-power-save-mechanisms.pptx
[5] IEEE 802.11ax D4.0