## Slide 1: Comparisons of HARQ transmission schemes for 11be
Date: 2019-6-24
Authors:
Name | Affiliations | Address | Phone | email
Yan Zhang Hongyuan Zhang Sudhir Srinivasa Liwen Chu Rui Cao Mao Yu | Marvell |  |  | yzhang@marvell.com

## Slide 2: HARQ Review
HARQ CC is studied in [1][2][3], and show some performance gain over ARQ. To realize the gain, frequency diversity across transmissions is needed to achieve the potential gain via BCC interleaver or LDPC tone mapper patterns varying across transmissions.
HARQ IR is shown to have larger performance gain over ARQ in [4][5]. However, this is done with BCC encoding, which is only applied to RU size less than or equal to 242 tones, and MCS up to 9. Hence the gain cannot be realized for the most use cases which utilize larger RU sizes and LDPC encoding.
A modified HARQ CC scheme and HARQ IR scheme for LDPC encoding are explored and evaluated along with ARQ and HARQ CC.

## Slide 3: HARQ Punctured CC outline
HARQ Punctured CC is improved upon regular HARQ CC to achieve higher throughput without adding much implementation complexities at both transmitter and receiver.
  All coded bits corresponding to an MPDU are transmitted in the first transmission as in regular HARQ CC.
  A portion of the coded bits are transmitted in the subsequent retransmissions for soft combining at receiver side.
  The percentage of the coded bits transmitted in the subsequent retransmissions can be determined based on the first transmission PER statistics.

## Slide 4: HARQ IR outline
The HARQ IR for LDPC encoding scheme can support all LDPC code rates and all codeword lengths employed in current WIFI standards.
Rate ½ code designs still use the ones in current standard specs. All code rates higher than ½ will be achieved by puncturing rate ½ code for a given LDPC codeword length.
All information bits and some parity bits are transmitted in the first transmission for the initial code rate. Additional parity bits are transmitted in the subsequent retransmissions to achieve a lower effective code rate if the initial code rate is higher than 1/2. The lower effective code rates for the subsequent retransmissions can be determined based on either CQI reports or relevant PER statistics.
For MCS values with rate ½ code, use the same retransmission schemes as HARQ Punctured CC.

## Slide 5: Simulation setup
20MHz 2x2 (2SS) and 80MHz 4x2 (2SS) DNLOS channel (channels are not normalized) without impairments
SU BF, LDPC encoder
4x HE-LTF, MCS0-11
1000 packets
Up to 3 (re)transmissions for each packet (2000 bytes) for 20MHz, 2x2 (2SS) channel, and up to 2 (re)transmissions for each packet (8000 bytes) for 80MHz, 4x2 (2SS) channel, same channel realization is applied across all (re)transmissions for each packet.
ARQ, HARQ CC, Punctured CC and IR are evaluated (excluding preambles) with both MPDU based retransmissions and codeword based retransmissions.

## Slide 6: HARQ vs ARQ Goodput Comparison, 20MHz 2x2 channel, 2SS, with Optimal MCS selection
For both MPDU based and codeword based retransmission schemes, HARQ Punctured CC and HARQ IR have a few dB gain over HARQ CC and ARQ even with optimal MCS selection. The median gain of HARQ schemes over ARQ are shown below.
Median gain(dB) | MPDU based | Codeword based
CC | 1.38 | 1.41
Punctured CC | 2.58 | 2.47
IR | 2.90 | 2.94
Table 1 Median SNR gain of HARQ schemes over ARQ with optimal MCS selection

## Slide 7: ARQ first transmission PER performance, 20MHz 2x2 channel, 2SS
First transmission PER varies from 10% to 40% within 2-3 dB range for all MCS levels. Hence MCS selection based on SNR measurements may result in PER varying from 10% to 40%. The MCS levels with the largest SNR ranges are shown below
Required SNR | 10% PER | 20% PER | 30% PER | 40% PER | SNR range
MCS 7 | 31.98dB | 30.65dB | 29.79dB | 29.17dB | 2.81dB
MCS 9 | 36.63dB | 35.35dB | 34.54dB | 33.88dB | 2.75dB
MCS 11 | 41.61dB | 40.31dB | 39.52dB | 38.87dB | 2.74dB
Table 2 Required SNR values to achieve packet first transmission PER 10%-40%

## Slide 8: HARQ vs ARQ Goodput Comparison, with first Tx PER varying 10-40%, MPDU based retransmission
HARQ Punctured CC and HARQ IR have comparable performances when first Tx PER varies from 10% to 40%. They provides larger throughput gain over ARQ than HARQ CC. The median throughput gains of HARQ schemes over ARQ with rate adaptation are shown in the table 3.

## Slide 9: HARQ vs ARQ Goodput Comparison, with first Tx PER varying 10-40%, Codeword based retransmission
With codeword based retransmission, goodput of all transmission schemes improved compared to MPDU based retransmission. However, the spectral efficiency gains of HARQ schemes over ARQ with rate adaptation are comparable to that of MPDU based schemes. The median throughput gains of HARQ schemes over ARQ with rate adaptation are shown in the table 4.

## Slide 10: HARQ vs ARQ Goodput Comparison, with first Tx PER varying 10-40%
Spectral efficiency gain of HARQ Punctured CC and HARQ IR over ARQ with rate adaptation is significant when first Tx PER is above 20% for both MPDU based and codeword based retransmissions.
Median SE gain | 10% PER | 20% PER | 30% PER | 40% PER
CC | 11.5% | 24.6% | 37.0% | 49.8%
Punctured CC | 18.4% | 37.9% | 57.8% | 78.5%
IR | 18.2% | 39.1% | 61.3% | 85.3%
Table 3. Spectral efficiency gain of HARQ schemes over ARQ with rate adaptation with MPDU based retransmission
Median SE gain | 10% PER | 20% PER | 30% PER | 40% PER
CC | 9.6% | 24.0% | 40.7% | 59.9%
Punctured CC | 12.4% | 32.0% | 53.7% | 79.1%
IR | 13.0% | 32.7% | 56.6% | 84.2%
Table 4. Spectral efficiency gain of HARQ schemes over ARQ with rate adaptation with Codeword based retransmission

## Slide 11: HARQ vs ARQ Goodput Comparison, 80MHz 4x2 channel, 2SS, with Optimal MCS selection
For both MPDU based and codeword based retransmission schemes, HARQ Punctured CC and HARQ IR have small gain over ARQ with optimal MCS selection due to large beamforming gain. The median gain of HARQ schemes over ARQ are shown below.
Median gain(dB) | MPDU based | Codeword based
Punctured CC | 0.80dB | 0.72dB
IR | 0.62dB | 0.48dB
Table 5 Median SNR gain of HARQ schemes over ARQ with optimal MCS selection

## Slide 12: ARQ first transmission PER performance, 80MHz 4x2 channel, 2SS
Due to large beamforming gain, PER varies from 10% to 40% within 1dB range for all MCS levels. Hence MCS selection based on SNR measurements may result in PER varying from 10% to 40%. SNR ranges for some MCS levels are shown below
Required SNR | 10% PER | 20% PER | 30% PER | 40% PER | SNR range
MCS 7 | 22.87dB | 22.52dB | 22.17dB | 21.88dB | 0.99dB
MCS 9 | 27.81dB | 27.47dB | 27.12dB | 26.87dB | 0.95dB
MCS 11 | 32.91dB | 32.61dB | 32.31dB | 32.01dB | 0.90dB
Table 6 Required SNR values to achieve packet first transmission PER 10%-40%

## Slide 13: HARQ vs ARQ Goodput Comparison, with first Tx PER varying 10-40%, MPDU based retransmission
HARQ Punctured CC and HARQ IR have comparable performances when first Tx PER varies from 30% to 40%, while the former has some gain over the latter when first Tx PER varies from 10% to 20%. The median throughput gains of HARQ schemes over ARQ with rate adaptation are shown in the table 7.

## Slide 14: HARQ vs ARQ Goodput Comparison, with first Tx PER varying 10-40%, Codeword based retransmission
With codeword based retransmission, goodput of all transmission schemes improved compared to MPDU based retransmission. The spectral efficiency gains of HARQ schemes over ARQ with rate adaptation are much smaller that of MPDU based schemes. The median throughput gains of HARQ schemes over ARQ with rate adaptation are shown in the table 8.

## Slide 15: HARQ vs ARQ Goodput Comparison, with first Tx PER varying 10-40%
Spectral efficiency gain of HARQ Punctured CC and HARQ IR over ARQ with rate adaptation is significant when first Tx PER is above 20% for MPDU based retransmissions, while it is much smaller for codeword based retransmissions.
Median SE gain | 10% PER | 20% PER | 30% PER | 40% PER
Punctured CC | 11% | 29% | 50% | 72%
IR | 7% | 25% | 47% | 70%
Table 7. Spectral efficiency gain of HARQ schemes over ARQ with rate adaptation with MPDU based retransmission
Table 8. Spectral efficiency gain of HARQ schemes over ARQ with rate adaptation with Codeword based retransmission
Median SE gain | 10% PER | 20% PER | 30% PER | 40% PER
Punctured CC | 1.5% | 6.5% | 17.7% | 33.6%
IR | 0.9% | 5.9% | 17.4% | 34.2%

## Slide 16: Discussions on HARQ Punctured CC Memory
Based on our simulations, buffer memory requirements will significantly reduced after two transmissions for SU BF 2x2, 2SS case, as shown in the Table 9. (SNR operating point corresponds to packet first transmission PER around 40% for each MCS level).
Table 9 PER statistics after each transmission with HARQ Punctured CC scheme for SU BF 2x2, 2SS
PER | 1st Transmission | 2nd Transmission | 3rd Transmission
MCS 0 | 39.8% | 31.5% | 0.5%
MCS 1 | 40.8% | 30.9% | 0.4%
MCS 3 | 40.8% | 9.8% | 0.3%
MCS 4 | 40.1% | 11.7% | 0.1%
MCS 5 | 39.8% | 6.9% | 0
MCS 6 | 40.2% | 9.7% | 0
MCS 7 | 40.1% | 13.9% | 0
MCS 8 | 39.3% | 8.7% | 0.1%
MCS 9 | 40.2% | 10.7% | 0
MCS 10 | 40.6% | 8.3% | 0.1
MCS 11 | 39.7% | 9.9% | 0

## Slide 17: Discussions on HARQ Punctured CC Memory
Similarly buffer memory requirements will significantly reduced after two transmissions for SU BF 4x2, 2SS case, as shown in the Table 10.
Table 10 PER statistics after each transmission with HARQ Punctured CC scheme for SU BF 4x2, 2SS
PER | 1st Transmission | 2nd Transmission
MCS 0 | 40.9% | 29.5%
MCS 1 | 39.5% | 32.6%
MCS 2 | 39.1% | 33%
MCS 3 | 39.9% | 15.8%
MCS 4 | 39.7% | 14%
MCS 5 | 40.4% | 4.6%
MCS 6 | 39.4% | 7.4%
MCS 7 | 39.7% | 15.4%
MCS 8 | 40% | 9%
MCS 9 | 40.2% | 2.5%
MCS 10 | 39.4% | 1.4%
MCS 11 | 39.7% | 1%

## Slide 18: Discussions on HARQ Punctured CC Memory
With codeword based retransmission, buffer size can be further reduced.
The following figures show the distribution of number of incorrectly decoded codewords after 1, 2 and 3 transmissions with HARQ Punctured CC when SNR operating points correspond to packet first transmission PER around 40% for SU BF 2x2, 2SS transmission.
A large percentage of failed first transmission have all codewords incorrectly received, but this is reduced by more than half for MCS 0 and MCS 1, and reduced by more than 85% for MCS 3 and MCS 4. There are very few errors after 3 transmissions.

## Slide 19
A large percentage of failed first transmission have all codewords incorrectly received, but this is reduced by more than 90% for MCS 5-11 after 2 transmissions. There are almost no errors after 3 transmissions except MCS 8 and MCS10 each have one instance of one codeword error.

## Slide 20: Discussions on HARQ Punctured Memory
The following figures show the number of incorrectly decoded codewords after 1 and 2 transmissions with HARQ Punctured CC when SNR operating points correspond to packet first transmission PER around 40% for SU BF 4x2, 2SS transmission.
Number of wrong codewords among most of the packets are greatly reduced to below 8 codewords after 2 transmission with HARQ Punctured CC for MCS0 – MCS3. Few packets have all codewords wrong after 2 transmissions.

## Slide 21
Number of wrong codewords of most packets are less than 10 for the first transmission, and the number of wrong codewords for all packets are greatly reduced below 5 for MCS5 and above, and most of the packets only have one wrong codewords.

## Slide 22: Discussions on HARQ Memory
If receiver cannot buffer the LLRs for certain MPDUs due to memory limitations, it can signal this information to the transmitter. Once transmitter receives the signaling, it will adjust the subsequent retransmissions accordingly, i.e., retransmit the same coded bits as those sent in the first transmission.
Alternatively, transmitter can estimate how many MPDUs receiver can buffer based on receiver buffer capacity exchanged at the HARQ request/response stage. Based on received Block Ack information, transmitter can roughly estimates how many retransmission MPDUs and new MPDUs can be aggregated in the next A-MPDU so that receiver has enough memory to buffer the MPDUs under normal circumstances.
In order to prevent the LLR buffer overflow, transmitter should give retransmission MPDUs higher priority, so that the receiver can flush out LLR buffer reserved for the retransmission MPDUs in time.

## Slide 23: Discussion and Conclusions
As shown in slides 7 and 12, first transmission PER can varies from 10% to 40% even when SNR operating point only varies within 2dB or smaller when beamforming gain is high. SNR measurements most likely varies around this range compared to the real channel. Hence it is very difficult to achieve optimal ARQ link adaptation, i.e., achieving 10% PER for selected MCS.
As shown in slides 9-10, and 13-14, both HARQ Punctured CC and HARQ IR can have significant throughput gain over ARQ with rate adaptation when first transmission PER is above 20%.
HARQ regular CC requires BCC interleaver or LDPC tone mapper varying over different transmission to get the frequency diversity gain, while HARQ punctured CC and HARQ IR have no such requirement. The throughput gain from HARQ regular CC is much smaller than the other two schemes, as shown in tables 3 and 4.
Although codeword based retransmission scheme can improve throughput for both HARQ and ARQ, and requires less buffer memory, it also requires more PHY and MAC changes.
  MAC MBA needs to be modified to codeword level, and the number of codewords could be more than thousand for a large data packet.
  PHY needs add signaling to indicate mapping between codewords and MPDUs
  Each codeword need extra CRC information to prevent false detection, such as FCS appending at the end of each codeword.

## Slide 24: Conclusions and Proposals
HARQ transmission should be adopted in 11be to compensate performance degradation due to inaccurate link adaptation, (e.g., avoid rate drop when PER reaches certain threshold), and reduce the number of retransmissions, thus improving STA throughput and network efficiency.
The proposed HARQ Punctured CC requires least changes based on the current PHY design, and provides higher throughput gain than HARQ CC.
The proposed HARQ IR requires larger buffer memory than HARQ punctured CC for most of the MCS transmission, and the throughput of two schemes are comparable for all simulated cases.
HARQ Punctured CC should be adopted as an mandatory feature for HARQ transmission due to its advantages over other schemes.

## Slide 25: Reference
[1] IEEE 802.11-18/1955r0 “HARQ for EHT – Further Information”
[2] IEEE 802.11-18/2029r1 “HARQ in EHT”
[3] IEEE 802.11-18/1992r1 “HARQ feasibility”
[4] IEEE 802.11-19/354r0 “Consideration on HARQ”
[5] IEEE 802.11-19/390r0 “Effect of Preamble Decoding on HARQ in 802.11be”

## Slide 26: Appendix
Wrong codewords statistics of each transmission for HARQ IR Codeword based retransmission, SU BF 2x2, 2SS
Wrong codewords statistics of each transmission for HARQ IR Codeword based retransmission, SU BF 4x2, 2SS

## Slide 27: Discussions on HARQ IR Memory
Based on our simulations, buffer memory requirements will significantly reduced after two transmissions for SU BF 2x2, 2SS case, as shown in the Appendix Table 1.
Appendix Table 1 PER statistics after each transmission with HARQ IR scheme for SU BF 2x2, 2SS
PER | 1st Transmission | 2nd Transmission | 3rd Transmission
MCS 0 | 39.8% | 31.5% | 0.5%
MCS 1 | 40.8% | 30.9% | 0.4%
MCS 3 | 40.8% | 9.8% | 0.3%
MCS 4 | 57.7% | 19.2% | 0.1%
MCS 5 | 47.5% | 0.5% | 0.2%
MCS 6 | 59.9% | 16.7% | 0
MCS 7 | 73.8% | 19.4% | 1.4%
MCS 8 | 55.6% | 11.4% | 0
MCS 9 | 71.6% | 15.6% | 1.1%
MCS 10 | 57.8% | 14.8% | 0
MCS 11 | 74.3% | 16.3% | 0.4%

## Slide 28: Discussions on HARQ IR Memory
Based on our simulations, buffer memory requirements will significantly reduced after two transmissions for SU BF 4x2, 2SS case, as shown in the Appendix Table 2.
Appendix Table 2 PER statistics after each transmission with HARQ IR scheme for SU BF 4x2, 2SS
PER | 1st Transmission | 2nd Transmission
MCS 0 | 40.9% | 29.5%
MCS 1 | 39.5% | 32.6%
MCS 2 | 68.6% | 24.2%
MCS 3 | 39.9% | 15.8%
MCS 4 | 80.5% | 28.6%
MCS 5 | 61% | 0%
MCS 6 | 83.3% | 16.8%
MCS 7 | 93.7% | 16.8%
MCS 8 | 85.5% | 17.1%
MCS 9 | 97.1 | 15.3%
MCS 10 | 92% | 9%
MCS 11 | 98% | 13.2%

## Slide 29: Discussions on HARQ IR Memory
A large percentage of failed first transmissions have all codewords incorrectly received, but this is reduced by more than 90% for MCS 4-11 after 2 transmissions. There are very few errors after 3 transmissions.

## Slide 30: Discussions on HARQ IR Memory
Number of wrong codewords are greatly reduced to less than 10 after 2 transmissions with HARQ IR for SU BF 4x2, 2SS case.