## Slide 1: Enabling Uplink Persistent Allocation for EHT
Date: 2019-07-31
Authors:
Name | Company | Address | Phone | Email
Lei Huang | Panasonic Corporation |  |  | lei.huang@sg.panasonic.com
Urabe Yoshio |  |  |  | 
Rojan Chitrakar |  |  |  | 
Yanyi Ding |  |  |  | 

## Slide 2
Background
Many candidate features for 11be has been discussed in EHT SG [1], e.g.
  320MHz bandwidth and more efficient utilization of non-contiguous spectrum
  Multi-band/multi-channel aggregation and operation
  16 spatial streams and MIMO protocols enhancements
A large amount of users can be supported in a single PPDU. For example,
  If all 26-tone RUs in 320 MHz are allocated to different STAs, about 150 users can be supported in a single PPDU.
It is expected that control signaling overhead required for EHT MU transmission will be increased significantly.
This contribution addresses one possibility of reducing control signaling overhead for EHT UL MU transmission.

## Slide 3
  Only dynamic allocation per PPDU is allowed for 11ax UL MU transmission.
    Resource allocation information (e.g. RU allocation, MCS, SS allocation, etc.) for an UL allocation need to be included in a Trigger frame for soliciting HE TB PPDU transmission.
  Example use case
    AP transmits a broadcast Trigger frame periodically to poll a group of STAs (e.g. 8 STAs) to send BSR (buffer status report) for periodic traffic such as voice or video
  Overhead analysis
    The typical airtime for the Trigger frame transmission is 113us
      Assume the Trigger frame has a size of 70 octets
        MAC header: 16 octets
        Common Info: 8 octets
        User Info List: 5 octets * 8
        Padding + FCS: 6 octets
      Assume the Trigger frame is carried in a non-HT PPDU with the data rate of 6 Mb/s
11ax UL MU Transmission
Time
TF for G1 STAs
TF for G2 STAs
G1 BSR
G2 BSR
G1 BSR
G2 BSR
TF for G1 STAs
TF for G2 STAs

## Slide 4
  For overhead reduction, uplink persistent allocation (UPA) across PPDUs can be considered for 11be UL MU transmission.
    For an UPA, resource allocation information is unchanged for a time period.
    Resource allocation information for the UPA may not be included in the Trigger frame for soliciting EHT TB PPDU transmission if it has been captured by the scheduled STA of the UPA.
      For example, the User Info field for an UPA may not be present in a Trigger frame for soliciting a transmission of the UPA.
    Consequently a shortened Trigger frame can be used to solicit EHT TB PPDU transmission including one or more UPA.
Uplink Persistent Allocation for Shortening Trigger Frame

## Slide 5
Uplink Persistent Allocation for Shortening Trigger Frame (cont.)
A Persistent Allocation Announcement frame advertises resource allocation information and persistent allocation identifier (PAID) for each UPA
  The PAID of an UPA uniquely identifies the UPA from a STA’s perspective.
A shortened Trigger frame is used to solicit EHT TB PPDU transmission.
  The shortened Trigger frame contains the PAID of each UPA only.

## Slide 6: Uplink Persistent Allocation for Shortening Trigger Frame (cont.)
Overhead analysis for example use case
  The typical airtime for the shortened Trigger frame transmission is 61us
      A group of STAs (e.g. 8 STAs) share a same PAID.
      The shortened Trigger frame has a size of 31 octets
        MAC header: 16 octets
        Common Info: 8 octets
        PAID: 1 octet
        Padding: 2 octets
        FCS: 4 octets
      The shortened Trigger frame is carried in a non-HT PPDU with the data rate of 6 Mb/s
  Compared with 11ax, overhead is reduced by 46%.
Time
Shortened TF for G1 STAs using PAID1
Shortened TF for G2 STAs using PAID2
G1 BSR
G2 BSR
G1 BSR
G2 BSR
Shortened TF for G1 STAs using PAID1
Shortened TF for G2 STAs using PAID2

## Slide 7: Summary
It is proposed to enable uplink persistent allocation for 11be to shorten Trigger frame for soliciting EHT TB PPDU transmission.

## Slide 8: Reference
11-18-1231-06-0eht-eht-draft-proposed-par, March 2019