## Slide 1
Consideration on
20MHz Channel Access in 11bd
Date: 2019-05-15
Authors:

## Slide 2: Introduction
In 11bd SFD [1],
  In 20MHz bandwidth, L-STF, L-LTF, and L-SIG for 10MHz PPDU are duplicated as shown in the figure below
However, the baseline channel access procedure for wideband cannot be applied directly
Since there may not be concept of primary channel in OCB, careful consideration is needed to utilize 20MHz
In this contribution, 20MHz channel access procedures are discussed

## Slide 3: Wide Bandwidth Channel Access
In the base specification in 11n, wide bandwidth channel access using PIFS is specified
In BSS, the primary channel is decided by AP
  STAs in AP shares the same primary channel
  The secondary channel usage is based on OBSS
    Low probability for traffic
    on secondary channel
    as a primary channel
Wideband signal
D
I
F
S
P
I
F
S
Primary
10
Secondary
10
TXOP

## Slide 4: Considerations on 802.11bd Channels
Channel usage in NGV: no AP exists
  OCB traffic
  No primary channel
The channel used in 5.9 GHz
  Each channel has its own purpose
  Each channel is equally important
In order to access a 20MHz channel in 802.11bd, contention channel shall be defined
Ch 172
Ch 174
Ch 176
Ch 178
Ch 180
Ch 182
Ch 184
SCH
safety
SCH
safety
CCH
SCH: may used in 20MHz
SCH: may used in 20MHz
5.855GHz 5.865GHz 5.875GHz 5.885GHz 5.895GHz 5.905GHz 5.915GHz 5.925GHz

## Slide 5: Terminologies
In order to describe 20MHz channel operation clearly, terminologies for different channel types need to be defined
  Service channel, Contention channel, Extension channel
Contention channel
  10MHz channel on which channel access procedure is performed
  Similar to a primary channel in BSS
Service channel
  10MHz channel on which a specific service, e.g., BSM is delivered without 20MHz wide channel operation
Extension channel
  10MHz channel to which 20MHz channel is extended

## Slide 6: Option 1: Service Channel as Contention Channel
Current 10MHz service channel is set as a contention channel
  Example: Ch 174 & Ch 176
    For the applications use Ch 174, Ch 174 is set as a contention channel
    For the applications use Ch 176, Ch 176 is set as a contention channel
Legacy wide channel access using PIFS can be reused
  Channel contention is performed on the contention channel and the availability of the extension10MHz channel is checked during PIFS
    Pros: Simple and reusing the existing procedure
    Cons: Fairness problem on the extending 10MHz channel

## Slide 7: Option 1: Service Channel as Contention Channel (Cont’d)
20MHz PPDU Transmission Failure
  Legacy Dynamic Bandwidth Operation
    If the extension channel is busy during PIFS, the STA just transmits 10MHz PPDU

## Slide 8: Option 2: Dual Contention Channels
Both channels are contention channels
Both 10MHz channels perform a channel access procedure independently
  20MHz Channel can only be used upon successful backoff on the both channels
    Pros: Highest fairness
    Cons: Performance degradation
Ch
174
Ch
176
10
MHz
10
MHz
Postpone
Access
Data

## Slide 9: Option 2: Dual Contention Channels (Cont’d)
Various channel access failure cases can happen depending on the selected parameters (e.g., backoff value)
  Further rigorous investigation is required
  Clear definition on the procedure shall be defined

## Slide 10: Option 3: Dynamic Contention Channel for Channel Access
Set the contention channel between two 10MHz channels at the time of channel access
  Contention channel can be selected at random or alternatively or by using some additional information
  Channel extension can be done
  when the extension channel is
  idle during TBD time
    Pros: Fairness & Flexibility
    Cons: Contention channel selection
      Random selection
      Additional information

## Slide 11: Option 3: Dynamic Contention Channel for Channel Access (Cont’d)
20MHz PPDU Transmission Failure
  If the contention channel is busy but the service channel is idle, the STA can transmit 10MHz PPDU through the service channel

## Slide 12: Conclusion
Option 1 is a legacy wide channel access procedure, and it has an advantage of easy implementation. However, there is a fairness issue on the extension channel.
Option 2 is dual contention channels, and it guarantees the highest fairness among three options. However, it may have a performance degradation problem.
Option 3 is a dynamic contention channel for a channel access, and it has fairness and flexibility. However, the contention channel selection needs to be defined.

## Slide 13: Straw Poll 1
Which option do you prefer for 20MHz channel access?
  Option 1: Service Channel as Contention Channel (11n like access)
  Option 2: Dual Contention Channels
  Option 3: Dynamic Contention Channel for Channel Access
  None of above

## Slide 14: Reference
[1] 19/0497r1 specification framework document