## Slide 1
Channel usage in NGV: follow-up
Date: 2019-05-15
Authors:
Notes: Good morning. I am Yougsu Gwak from Korea National University of Transportation. The contribution’s title is channel usage in NGV: follow-up. The document number is 809r1.

## Slide 2: Introduction
As in PAR document[1], the 11bd operation in V2X communication shares the channel with 11p devices, maintaining interoperability
  This amendment shall provide interoperability, coexistence, backward compatibility, and fairness with deployed OCB (Outside the Context of a BSS) devices.
When the number of nodes increases, the channel access mechanism cannot ensure the reliability of the communication because of the channel capacity limitation
In this contribution, the channel access performance for the case of periodic BSM message transmission is investigated, as the number of nodes increases.
Notes: First, I will briefly explain what was already presented in March. As in PAR document, the channel of the 11bd will be shared with 11p devices to provide interoperability, coexistence, backward compatibility, and fairness with deployed OCB devices. When the number of nodes increases, the reliability of the communication cannot be ensured due to the lack of the channel capacity. In this contribution, the channel access performance for the case of periodic BSM message transmission is investigated.

## Slide 3: Channel usage in DSRC
According to the FCC regulation[3], in the DSRC communication based on IEEE 802.11p, each channel in 5.9 GHz band assigned for V2X communication utilizes 10 MHz bandwidth
  The BSM message is sent in Ch 172, which is dedicated for safety message
In this contribution, it is assumed that 11bd devices also transmit BSM messages using the same channel as 11p devices.
Ch 172
Ch 174
Ch 176
Ch 178
Ch 180
Ch 182
Ch 184
SCH
safety
SCH
safety
CCH
SCH: may used in 20MHz
SCH: may used in 20MHz
Notes: According to the FCC regulation, in the DSRC communication based on 11p each channel in 5.9 GHz band assigned for V2X communication employs 10 MHz bandwidth like the proposed figure. The periodic BSM message is sent in CH 172, which is dedicated for safety message, and it is also assumed that 11be devices transmit BSM messages to the same channel.

## Slide 4: Channel capacity limitation in dense scenario
In case of the large number of cars, BSMs sent by each node may cause congestion in the single 10 MHz channel
  The dense environment includes traffic jam, intersection and tollgate scenarios
Notes: In this contribution, the channel access performance for the case of periodic BSM message transmission is investigated as the number of cars increases. So, the very dense scenario that a lot of cars are together is supposed. And all of them are sending BSMs.

## Slide 5: Contention-based MAC access for highly congested channel
When the channel is congested, the contention-based MAC channel access mechanism causes the large collision probability.
The transmission procedure of BSM messages, which is a broadcast message without retransmission, does not guarantee the reliability of the transmission.
Notes: The problem is that the contention-based MAC channel access increases the channel collision probability. Moreover, since BSM is a broadcast message without retransmission, it does not ensure the reliability of the transmission.

## Slide 6: Brief analysis of collision probability in contention-based channel access
In order to investigate how large number of nodes affects the reliability, brief simulation is performed.
Assumptions
  perfect channel
  channel access with legacy DCF parameters
  only BSM messages with 100ms period
Parameter | Values
BSM size (including Header) | 400 Bytes
Number of nodes | 10~200
AIFSN | 2
minCW | 15
MCS | 0/2
Notes: This is simulation parameters. Perfect channel without losses and only BSM message transmission with 100ms period are assumed. All BSM size including header is 400 bytes and the dense scenario with the number of cars 10 to 200 is set. You can find the other parameters at the proposed table.

## Slide 7: Collision probability of BSM messages in single 10 MHz channel
For 400 Bytes BSM message with MCS=0
  Collision probability of more than 0.1 occurs in case of more than 70 nodes
For 95% reliability, the number of nodes should be less than 60, for idle channel
For 99% reliability, the number of nodes should be less than 40, for idle channel
Notes: This is the simulation result when MCS is 0. X axis is the number of cars and Y axis is collision probability. As the number of cars increases, the collision probability also increase.

## Slide 8: Collision probability of BSM messages in single 10 MHz channel
For 400 Bytes BSM message with MCS=2
  Collision probability of more than 0.1 occurs in case of more than 120 nodes
For 95% reliability, the number of nodes should be less than 100, for idle channel
For 99% reliability, the number of nodes should be less than 60, for idle channel
Notes: This is the simulation result when MCS is 2. X axis is the number of cars and Y axis is collision probability. It shows better performance rather that the previous simulation results with MCS is 0 since higher MCS makes the channel less contend.

## Slide 9: Observation
Even with only BSM messages in the channel, the contention-based channel access in single channel does not guarantee the reliability required for safety operation
  Reliability cannot be achieved in dense environments, such as heavy traffic (e.g. traffic jam), platooning scenario, and highly populated places like intersection or tollgate.
For other environments, the number of nodes meeting the reliability requirements will be decreased
  When channel switching is applied, the collision probability will be increased, as described in [4]
  When the other messages sent in the channel(warning signal, etc), the collision probability will be increased
Notes: Even though we generated only BSM messages in the channel, the contention-based channel access does not guarantee the reliability in the dense environments such as heavy traffic and highly populated places. For other environments, the requirement to ensure the reliability will be decreased.

## Slide 10: Discussion
As the reliability issue arises in the dense scenario, the modification of the channel access procedure, as well as channel switching mechanism are needed
  Modification shall not affect backward compatibility and interoperability with legacy devices
  Modification shall work under OCB communication
Higher MCS or wider channel bandwidth may lower the collision probability, but the transmission range requirement may not be satisfied.
Distributed multi-user operation may be required to enhance the channel efficiency.
  Based on distributed 802.11ax OFDMA or Distributed PCF
Notes: Discussion. As the reliability issue arises in the dense scenario, the modification of the channel access procedure or channel switching mechanism are necessary. Of course, the modifications shall not affect backward compatibility. And higher MCS or wider channel bandwidth may lower the collision probability, but the transmission range requirement may not be satisfied. Otherwise, distributed multi-user operation may be adopted to enhance the channel efficiency. This is the end of presentation discussed at the Telecon in March, and we got a feedback.

## Slide 11: Regarding the congestion control
The upper layer congestion control may be applied to control the amount of traffic
  E.g. Congestion Control requirements as defined in SAE J2945.1, DCC, etc
However, the robust MAC will improve the channel utilization and reliability
  Lower collision and failure probability for same channel load
Notes: The feedback is that the upper layer congestion control may be applied to control the amount of traffic. So it can be a kind of wastes. However, in addition to the congestion control mechanism, it will be more beneficial to have the channel access mechanism in the MAC layer. In short, we should deal with them independently.

## Slide 12: Conclusion
In this presentation, we investigated the channel access performance used in 11p, especially for BSM messages in 10 MHz channel
Even though a dedicated 10MHz channel is allocated for BSM messages, the reliability of BSM transmissions cannot be achieved as the number of nodes increases.
The conventional channel access method is not enough to achieve the reliability requirements in dense environment
In 802.11bd, efficient distributed multi-user channel access methods are required to accommodate more vehicles.
Notes: Conclusion is that…

## Slide 13: Reference
[1] 18/861r9 IEEE 802.11 NGV SG Proposed PAR
[2] 17/651r2 Indication for WUR Duty Cycle
[3] Electronic Code of Federal Regulations
[4] L. Miao, et. al., “Performance Evaluation of IEEE 802.11p MAC Protocol in VANET Safety Applications,” 2013 IEEE Wireless Communications and Networking Conference (WCNC), Shanghai, 2013, pp. 1663-1668.
[5] J. B. Kenney, “Dedicated Short-Range Communication (DSRC) Standards in the United States,” in Proceedings of the IEEE, vol. 99, no. 7, pp. 1162-1182, July 2011.

## Slide 14: Straw poll
Do you agree to add the following text in Section 2.1 of Functional Requirements Document?
  The 802.11bd amendment shall provide at least one mode of channel access that provides improved transmission reliability under congested communication environment compared to IEEE Std 802.11™-2016 operating in 5.9 GHz band
Y: 6
N: 2
A: 6