## Slide 1: Multiple Band Operation Discussion
Date: 2019-05-14
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Manish Kumar Hongyuan Zhang Yan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | Marvell |  |  | 

## Slide 2: Recap: Multi-band Operation
Nowadays many APs are operating with dual/tri radios concurrently and independently, while STAs are typically with single radio.
For multi-band operation, EHT may allows:
  Multi Channel Aggregation at both AP and STA sides: Higher throughput (BW)
    160+20, 160+80, 160+160 etc.
  Flexible usage of multiple bands
  Multi-Channel Full Duplex (FDD): improves efficiency and reduce latency.
    Useful in applications such as gaming, video streaming etc.

## Slide 3: General Discussion of EHT Multi-band Operation
An EHT multi-band STA entity associates with an EHT multi-band AP entity through one association.
  Common capabilities (capability applying to all bands), per band capabilities.
  Common operation parameters, per band operation parameters.
  Operation Negotiation (BA, security, channel switch, BW update etc.)
    Common operation negotiation (single negotiation applying to all bands), per band operation negotiation.
  UP layer interface:
    No change to MAC data service specification,
    Common MLME SAP primitives, per band MLME SAP primitives

## Slide 4: Band Sharing
Option 1: dynamic band switch (band switch without negotiation)
  The frames for single TID can be transmitted in any band.
    The BA can transmitted in any band.
  Power save (mode change, state change), security (key negotiation, PN), Sequence Number, BA negotiation etc. in one band apply to all bands.
Option 2: band switch through negotiation
  Frames from single TID between a source and a destination are allocated to one band.
    The BA/Ack of the data frames is transmitted in the same band as the data frame Tx.
  Power save (state, mode change), security (key negotiation, PN), Sequence Number, BA negotiation etc. in one band apply to the band only.

## Slide 5: Unsynchronized and Synchronized PPDUs
For Unsynchronized PPDUs transmission, PPDU in one band can be transmitted after the backoff counter related to the band becomes 0.
  The PPDUs in different bands overlapped in time domain can be addressed to same STA.
    Method should be proposed to guarantee single reorder queue and single BA bitmaps
  A multi-band STA/AP entity can announce whether it supports the reception in one band while transmitting PPDU in another band (support of simultaneous Tx and Rx).
    The medium access should satisfy the restriction announced by the receiver.
Synchronized PPUD(s) in multiple bands can be transmitted after the backoff counter in one band is 0 and there are idle channels in other bands.
  Otherwise Fairness should be guaranteed.
Case1
Case1
Case2
Case3

## Slide 6: Backoff and Primary Channel
To support unsychronized operation, Each band has its own primary channel;
  A backoff procedure is associated with each primary channel:
    Each primary channel has its own EDCA parameters, CWmin, CWmax, AIFSN, CW, Retry counters etc.
  Beacon frames are transmitted in each primary channel with same TBTT or different TBTT.
    With same TBTT for two primary channels, Beacons can be transmitted in multiple PPDUs.

## Slide 7: Operation Mode Update with Multiple Primary Channels
The operation parameters in Multiple bands in an EHT BSS can be updated independently by EHT multi-band AP/STA
  One of the band can be disabled for power save.
BSS operating channel(160+80MHz)
240160
BSS operating channel(160MHz)
Primary channel for BW change
Primary channel not for BW change
BSS operating channel(160+80MHz)
16080 in Band 1
BSS operating channel(160MHz)
Band 1
Band 2