## Slide 1: Feedback Overhead Analysis for 16 Spatial Stream MIMO
Date: 2019-05-09
Authors:

## Slide 2
Abstract
In this contribution, we provide an overhead analysis for sounding/feedback for 16 spatial streams using 802.11ax protocols and discuss the need for feedback overhead reduction for 16 Spatial Stream MIMO and Multi-AP coordination in 802.11be.

## Slide 3: Introduction
  16 spatial stream MIMO has been discussed as a possible feature for 802.11be [1].
    Preliminary simulation results show performance benefits in increasing the number of spatial streams [2].
    However, this comes with an attendant increase of the required sounding and feedback.
  In 802.11ax sounding and feedback were modified to support the new numerology and OFDMA transmissions [9], compared to the TDM based feedback in VHT .
  Reduction of the overhead required for efficient channel acquisition at the transmitter for 16 Spatial Stream MIMO and Multi-AP coordination in 802.11be were discussed in [3].
    Questions were raised regarding if the sounding and feedback mechanisms defined in 802.11ax were adequate to support 16 spatial stream.
  In this contribution, we provide an overhead analysis of 16 SS training using 802.11ax sounding/feedback.

## Slide 4: Sounding and Feedback in 802.11ax (1/2)
  One-to-multiple sounding feedback is supported in 802.11ax. This enables multiple STAs to provide feedback at the same time and reduce the overhead relative to one-by-one sounding, as in 802.11ac. [9]

## Slide 5: Sounding and Feedback in 802.11ax (2/2)
  Feedback Segmentation:
    If HE compressed BF/CQI frame exceeds 11454 bytes, the report should be split into up to 8 feedback segments.
    All feedback segments shall be sent in a single A-MPDU contained in a PPDU and shall be included in the A-MPDU in the descending order of the Remaining Feedback Segments subfield values. [9]
  The length of feedback report is limited by the Length field in the L-SIG field (L_LENGTH).
    Length field has 12 bits, which can cover up to 4095 bytes
    Length is calculated from TXTIME using 6Mbps rate in legacy mode.
  TXOP signaled in HE SIG-A is up to 8448us.
    Though this duration of 8448 us is not the actual limit of TXOP, it serves as a good indication that a sounding sequence greater than this duration is not practical.

## Slide 6: Feedback Overhead Analysis for 16 SS (L_LENGTH constraint)
  The analysis is to evaluate:
    Are sounding and feedback defined in 802.11ax enough to support 16 spatial stream training?
  Analysis method:
    Evaluate the size of HE compressed beamforming report, that is carried in an HE TB PPDU.
      L_LENGTH is used as overhead measure.
    Settings in NDPA:
      Feedback type: [SU, MU].
      Ng: [4, 16].
      Quantize resolution : [(4,2) or (6,4)] for SU; [(7,5) or (9,7)] for MU
      # of RUs to be measured: [4, 9]
    HE TB PPDU setting:
      MCS4, nominal PE (8us), 2xHE-LTF + 1.6us GI, Nss=1.
      RU size to carry HE compressed BF report: [26-tone, 52-tone, 106-tone, 242-tone].

## Slide 7: SU-MIMO: 16 SS Cases, BW=20MHz
    11ax can’t support: feedback with L_LENGTH greater than 4095 Bytes
    SU report
    Nr x Nc is the V matrix size.
    TXOP duration = NDPA + NDP + BFRP + Feedback + 3SIFS
    Trade off for Feedback RU size and TXOP for training: To support the same number of concurrent STA sounding/feedback, the larger RU size allocated for each STA, the smaller the number of concurrent STAs supported for each BFRP, and thus the longer the TXOP duration for the sounding and training procedure.
Nr | Nc | Ng | phi | # 26-tone RUs | fdbk_RU | txop (us) | report AMPDU size (bytes) | report L_LENGTH
16 | 4 | 4 | 6 | 9 | 26 | 7626.4 | 4364 | 5266
16 | 8 | 4 | 4 | 9 | 26 | 7846.4 | 4504 | 5431
16 | 8 | 4 | 6 | 4 | 26 | 6244 | 3500 | 4228
16 | 8 | 4 | 6 | 9 | 26 | 12559.2 | 7448 | 8965
16 | 8 | 4 | 6 | 9 | 52 | 6533.6 | 7448 | 4495
16 | 16 | 4 | 4 | 9 | 26 | 10010.4 | 5856 | 7054
16 | 16 | 4 | 6 | 4 | 26 | 7928.8 | 4556 | 5494
16 | 16 | 4 | 6 | 9 | 26 | 16155.2 | 9696 | 11662
16 | 16 | 4 | 6 | 9 | 52 | 8333.6 | 9696 | 5845

## Slide 8: MU-MIMO: 16 SS Cases, BW=20MHz
    Current 11ax mechanism can’t support: feedback with L_LENGTH greater than 4095 Bytes
    MU report
    Nr x Nc is the V matrix size. TXOP duration = NDPA + NDP + BFRP + Feedback + 3SIFS
Nt | Nr | Ng | phi | # 26-tone Rus | fdbk_RU | txop (us) | report AMPDU size (bytes) | report L_LENGTH
8 | 8 | 4 | 9 | 9 | 26 | 6735.2 | 3888 | 4693
16 | 16 | 4 | 7 | 4 | 26 | 9757.6 | 5696 | 6865
16 | 16 | 4 | 7 | 9 | 26 | 20047.2 | 12128 | 14581
16 | 16 | 4 | 7 | 9 | 52 | 10277.6 | 12128 | 7303
16 | 16 | 4 | 9 | 2 | 26 | 7476 | 4272 | 5152
16 | 16 | 4 | 9 | 4 | 26 | 12637.6 | 7496 | 9025
16 | 16 | 4 | 9 | 4 | 52 | 6572.8 | 7496 | 4525
16 | 16 | 4 | 9 | 9 | 26 | 26188 | 15968 | 19186
16 | 16 | 4 | 9 | 9 | 52 | 13351.2 | 15968 | 9607
16 | 16 | 4 | 9 | 9 | 106 | 6559.2 | 15968 | 4534
16 | 16 | 16 | 9 | 9 | 26 | 8667.2 | 5016 | 6046
16 | 8 | 4 | 7 | 4 | 26 | 7533.6 | 4308 | 5197
16 | 8 | 4 | 7 | 9 | 26 | 15258.4 | 9136 | 10990
16 | 8 | 4 | 7 | 9 | 52 | 7883.2 | 9136 | 5506
16 | 8 | 4 | 9 | 4 | 26 | 9743.2 | 5688 | 6853
16 | 8 | 4 | 9 | 9 | 26 | 20032.8 | 12120 | 14572
16 | 8 | 4 | 9 | 9 | 52 | 10269.6 | 12120 | 7297
16 | 8 | 16 | 9 | 9 | 26 | 6733.6 | 3808 | 4597
16 | 4 | 4 | 7 | 9 | 26 | 9210.4 | 5356 | 6454
16 | 4 | 4 | 9 | 9 | 26 | 11975.2 | 7084 | 8527
16 | 4 | 4 | 9 | 9 | 52 | 6241.6 | 7084 | 4276
16 | 2 | 4 | 9 | 9 | 26 | 6752 | 3820 | 4609

## Slide 9: Analysis with TXOP+L_LENGTH constraint
The following slides calculate different tuples of (# of reporting STAs, feedback RU size) in a sounding sequence, and determine whether each tuple satisfies L_LENGTH limit and HE-SIG-A TXOP limit, with the assumptions:
  80MHz MU NDP sounding
  ={9,7}, Ng=4
  Report TB-PPDU (MCS=4, Nss=1) or (MCS=6, Nss=2)
  BFRP MCS0
  Nr=16, Nc=1/2/4
  Feedback RU size: 52/106/242 tones
  Number of non-AP STAs in a NDP sounding sequence: 4/8/16/32/64
  Multiple BFRPs are used in a TXOP if the # of feedback RUs < the # of STAs participating in the sounding
  No error in HE compressed BF/CQI frame (best case)

## Slide 10: BW=80MHz, Nr=16, Nc=1, fdbk MCS=4,nss=1
(<=L_LENGTH limit,<=Txop limit ) | # of fdbk STAs |  |  |  | 
fdbk RU size | 4 | 8 | 16 | 32 | 64
52 |  |  | (FALSE, TRUE) | (FALSE, FALSE) | (FALSE, FALSE)
106 |  | (TRUE, TRUE) | (TRUE, TRUE) | (TRUE, FALSE) | (TRUE, FALSE)
242 | (TRUE, TRUE) | (TRUE, TRUE) | (TRUE, TRUE) | (TRUE, FALSE) | (TRUE, FALSE)

## Slide 11: BW=80MHz, Nr=16, Nc=2, fdbk MCS=4,nss=1
(<=L_LENGTH limit,<=Txop limit ) | # of fdbk STAs |  |  |  | 
fdbk RU size | 4 | 8 | 16 | 32 | 64
52 |  |  | (FALSE, FALSE) | (FALSE, FALSE) | (FALSE, FALSE)
106 |  | (FALSE, TRUE) | (FALSE, FALSE) | (FALSE, FALSE) | (FALSE, FALSE)
242 | (TRUE, TRUE) | (TRUE, TRUE) | (TRUE, FALSE) | (TRUE, FALSE) | (TRUE, FALSE)

## Slide 12: BW=80MHz, Nr=16, Nc=4, fdbk MCS=4,nss=1
(<=L_LENGTH limit,<=Txop limit ) | # of fdbk STAs |  |  |  | 
fdbk RU size | 4 | 8 | 16 | 32 | 64
52 |  |  | (FALSE, FALSE) | (FALSE, FALSE) | (FALSE, FALSE)
106 |  | (FALSE, FALSE) | (FALSE, FALSE) | (FALSE, FALSE) | (FALSE, FALSE)
242 | (TRUE, TRUE) | (TRUE, FALSE) | (TRUE, FALSE) | (TRUE, FALSE) | (TRUE, FALSE)

## Slide 13: BW=80MHz, Nr=16, Nc=1, fdbk MCS=6,nss=2
(<=L_LENGTH limit,<=Txop limit ) | # of fdbk STAs |  |  |  | 
fdbk RU size | 4 | 8 | 16 | 32 | 64
52 |  |  | (TRUE, TRUE) | (TRUE, TRUE) | (TRUE, FALSE)
106 |  | (TRUE, TRUE) | (TRUE, TRUE) | (TRUE, TRUE) | (TRUE, FALSE)
242 | (TRUE, TRUE) | (TRUE, TRUE) | (TRUE, TRUE) | (TRUE, TRUE) | (TRUE, FALSE)

## Slide 14: BW=80MHz, Nr=16, Nc=2, fdbk MCS=6,nss=2
(<=L_LENGTH limit,<=Txop limit ) | # of fdbk STAs |  |  |  | 
fdbk RU size | 4 | 8 | 16 | 32 | 64
52 |  |  | (TRUE, TRUE) | (TRUE, FALSE) | (TRUE, FALSE)
106 |  | (TRUE, TRUE) | (TRUE, TRUE) | (TRUE, TRUE) | (TRUE, FALSE)
242 | (TRUE, TRUE) | (TRUE, TRUE) | (TRUE, TRUE) | (TRUE, TRUE) | (TRUE, FALSE)

## Slide 15: BW=80MHz, Nr=16, Nc=4, fdbk MCS=6,nss=2
(<=L_LENGTH limit,<=Txop limit ) | # of fdbk STAs |  |  |  | 
fdbk RU size | 4 | 8 | 16 | 32 | 64
52 |  |  | (FALSE, TRUE) | (FALSE, FALSE) | (FALSE, FALSE)
106 |  | (TRUE, TRUE) | (TRUE, TRUE) | (TRUE, FALSE) | (TRUE, FALSE)
242 | (TRUE, TRUE) | (TRUE, TRUE) | (TRUE, TRUE) | (TRUE, FALSE) | (TRUE, FALSE)

## Slide 16: Analysis with TXOP+L_LENGTH constraint: Observations
For report TB-PPDU (MCS=4, Nss=1): a single MU sounding sequence cannot support 16 STAs if Nc>1
For report TB-PPDU (MCS=6, Nss=2): a single MU sounding sequence can support 16 STAs even for Nc=4
All STAs may not be able to support high MCS and Nss. When multiplexed in a TB-PPDU, the padding to satisfy the worst STA will likely make the final PPDU length and TXOP longer
  Rx/Tx MCS/Nss and Nc are separate capabilities of an HE-STA

## Slide 17: 16 SS Feedback Overhead Reduction
    These analysis show that some new design may be needed to support 16 SS training
    Feedback overhead reduction techniques discussed in [3] include:
      ϕ only feedback as defined in 802.11ah
      Time domain channel feedback as defined in 802.11ad/ay
      Differential Givens rotation: Feed back time or frequency difference in Given’s Rotation angles
      Variable Angle Quantization: Use different quantization levels for different Given’s rotation angles (ϕi, ψi).
      Multi-component Feedback: splits feedback into multiple components [4][5]
      Codebook based Feedback: Feed back codeword from a well designed codebook [6]
      Two way channel training [7]
      Implicit Feedback: Bfer solicits packets suitable for channel estimation in the reverse direction [7]

## Slide 18: Overhead Reduction Techniques
 | Technique | Pros | Cons
1 | only feedback | exists in 802.11ah | single data stream only
2 | time domain channel | exists in 802.11ad/ay | may need additional signaling to identify tap positions and the extra matrix
3 | Differential Givens Rotation | Simple improvement from 802.11ax, variant in 11ay | Additional processing, Error Propagation
4 | Variable Angle Quantization | simple improvement from 802.11ax | additional processing
5 | Multi-component Feedback | Well understood, reduced feedback overhead | May need additional design
6 | Codebook based Feedback | Well understood, reduced feedback overhead | May need additional design
7 | Two way channel training | Do not need calibration, reduced feedback overhead | May need additional design
8 | Implicit Feedback | Simple improvement from 802.11n | Needs calibration
 | Technique | Pros | Cons
1 |  | exists in 802.11ah | single data stream only
2 | time domain channel | exists in 802.11ad/ay | may need additional signaling to identify tap positions and the extra matrix
3 | Differential Givens Rotation | Simple improvement from 802.11ax, variant in 11ay | Additional processing, Error Propagation
4 | Variable Angle Quantization | simple improvement from 802.11ax | additional processing
5 | Multi-component Feedback | Well understood, reduced feedback overhead | May need additional design
6 | Codebook based Feedback | Well understood, reduced feedback overhead | May need additional design
7 | Two way channel training | Do not need calibration, reduced feedback overhead | May need additional design
8 | Implicit Feedback | Simple improvement from 802.11n | Needs calibration

## Slide 19: Conclusions
In this contribution, we have performed an overhead analysis that extends 802.11ax sounding feedback to support up to 16 spatial stream training.
  We identified several cases where 11ax sounding and feedback can not support 16 spatial streams.
  A sounding sequence may not be able to support 16 STAs’ feedback with conservative MCS/Nss.
New designs may be needed to support 16 SS training in 802.11be
  Feedback overhead reduction methods [3] should be discussed

## Slide 20: References
11-19/244r0 EHT PAR document, Michael Montemurro (BlackBerry)
IEEE 802.11-18/0818r3, 16 Spatial Stream Support in Next Generation WLAN, Sameer Vermani (Qualcomm)
IEEE 802.11-19/0391r0, Feedback Overhead Reduction in 802.11be, Kome Oteri (InterDigital)
IEEE 802.11-18/1184r1, EHT discussions on throughput enhancement, Tianyu Wu (Samsung)
Chaiman Lim; Taesang Yoo; Clerckx, B.; Byungju Lee; Byonghyo Shim, "Recent trend of multiuser MIMO in LTE-advanced," in Communications Magazine, IEEE , vol.51, no.3, pp.127-135, March 2013
Love, D.J.; Heath, R.W.; Lau, V.K.N.; Gesbert, D.; Rao, B.D.; Andrews, M., "An overview of limited feedback in wireless communication systems," in Selected Areas in Communications, IEEE Journal on , vol.26, no.8, pp.1341-1365, October 2008.
L. P. Withers, R. M. Taylor and D. M. Warme, "Echo-MIMO: a two-way channel training method for matched cooperative beamforming," IEEE Trans. Signal Process., vol. 56, no. 9, pp. 4419-4432, Sep. 2008.
IEEE 802.11-18/1191r0, MU sounding improvements, Sigurd Schelstraete (Quantenna)
IEEE P802.11ax™/D4.0, February 2019, (amendment to IEEE P802.11REVmd/D2.0)

## Slide 21: Appendix: Givens Decomposition and 16 ss Support
Givens Rotation and extension to 16 SS. Assuming a Nr x Nc complex matrix V, then it can be compressed with D and G matrices
Exemplary extension to 16 ss:
Nr | Nc | # Phi | # Psi
8 | 1 | 7 | 7
8 | 2 | 13 | 13
8 | 4 | 22 | 22
8 | 8 | 28 | 28
16 | 1 | 15 | 15
16 | 2 | 29 | 29
16 | 4 | 54 | 54
16 | 8 | 92 | 92
16 | 16 | 120 | 120