## Slide 1: TGba Possible Architecture and Specification Issues
Date: 2019-05-12
Authors:

## Slide 2: Abstract
This presentation attempts to provide a discussion on some possible specification technical issues in 802.11ba D2.0 that are the result of changes made to the draft when the concept of WURx and PCR were removed and WUR functionality was defined as a mode of an AP and non-AP STA.

## Slide 3: There are 3 basic concepts that need review/draft edits
Multi-Channel operation of WUR AP and non-AP STA is not defined
  STA/AP pairs operate on a Single Channel
  DFS in the 5 GHz - precludes WUR PPDUs transmission
Now that WUR functionality is a mode of the STA, it must be defined:
  The allowed states of the STA need to be clearly specified
  How a STA goes into and out of these allowed states must be specified
  The properties of the STA in each defined state must be specified
  What the STA procedure for “waking up” must be specified
Now that the transmission of WUR PPDUs is a capability of an AP
  The type of WUR PPDUs that can be transmitted need to be clearly specified
  When a WUR PPDU shall/may be transmitted must be specified
  How the AP buffers STA PPDUs when a STA is assumed to be in WUR mode must be specified
  What the AP procedure is for “waking” a STA must be specified

## Slide 4: Multi-Channel operation

## Slide 5: In 802.11 a STA/AP operate on a Single Channel
The change in .11ba architecture from multiple devices (AP, STA, PCR, WURx) to simply an AP and non-AP STA with a WUR mode restricts multi-band operation, as:
A non-AP STA associated with a AP have a single defined band and channel of operation. Throughout the 802.11 spec all STA/AP transmission are assumed to be on the channel of the band used when the non-AP STA associates with the AP.
The only allowed multi-band operation is described in 11.32 [1], which allows for multi-band operation when a device contains multiple STAs.
A device can have multiple STAs, but a STA is a single logical entity.

## Slide 6: Therefore the 802.11ba Amendment Should
Either operate on a single band/channel as typical 802.11 STAs do or specify some of the following:
A means that an WUR AP can transmit a WUR PPDU on a different channel (different than the channel the non-AP STA associated with the AP on).
A means that an WUR AP can cause a WUR PPDU to be transmitted on a different channel/band and a means that the non-AP STA can receive it. (Note, for single band operation a STA can be told to move to a new channel for WUR PPDU reception.)
Add a WUR multi-band operation description (preferably in 11.32 [1]) for a multi-STA device.
Provide a description/requirements of how multi-band, multi-channel, and multi STA behavior work.

## Slide 7: Potential Issues of WUR in DFS 5GHz Band
Transmission of WUR PPDUs will confuse DFS receivers.
  The current 802.11ba draft does not allow for WUR operation in the DFS bands.
Since multiband operation is not defined in the specification and 5GHz STA can only receive and transmit in the 5 GHz band, all WUR PPDU transmissions can only use non-DFS 5GHz channels.
Therefore, WUR non-AP STAs associated with WUR a APs are restricted to operate only on non-DFS channels.
This will limit the usefulness or WUR in the 5GHz band.

## Slide 8: WUR Mode and the STATE of the STA must be define

## Slide 9: The STA and its State
A STA is a logical entity that has a state.
  “station (STA): A logical entity that is a singly addressable instance of a medium access control (MAC) and physical layer (PHY) interface to the wireless medium (WM).”[1]
  “state: condition or mode of existence that a system, component, or simulation can be in” [2]
Hence a STA is only in one state at any given time
  There are not two parts to a STA, hence a WUR non-AP STA is a single entity and has a single State.
e.g. when a non-AP WUR STA is in WUR awake state it:
  can only receive WUR PPDUs on the WUR channel configured by the frame exchange that defined the WUR mode for the STA.
  is not also in any other state, e.g. doze (a well defined PS state with different properties)

## Slide 10: State Changes
It is critical that the P802.11 and its amendments clearly define:
  The properties of the various states that 802.11 entities (AP or STA) can be in.
  The methods used to change the state of an 802.11 entity:
    Providing the sequence of events (frame exchanges, timers, measurements, etc.)
    When the changes in state occur or may occur
Possible issues with the current 802.11ba draft:
  There seems to be a mixing or nesting of PS and WUR states: e.g. “wake-up radio (WUR) mode: A negotiation status between a WUR AP and a WUR non-AP STA such that the WUR non-AP STA alternates between the WUR awake state and the WUR doze state when the WUR non-AP STA is in the doze state.” – this nesting is also present in other areas of the specification.
  The procedure for triggering the start of a WUR awake/doze schedule, does not seem to be defined.
    I have been told that the STA is assumed to start its WUR awake/doze schedule upon the competition of a WUR setup frame exchange defining the WUR mode (This seems to be buried in Table 30-1, assuming the phrase “enters WUR mode” means the STA is assumed to follow its WUR awake/doze schedule.)
    I have also been told that the STA with a defined WUR mode (one that has completed the WUR setup frame exchange) triggers the start of the WUR awake/doze schedule by sending a frame with the PS bit set to 1. (I can’t find this in the current draft, except for the use of “doze state” above.)

## Slide 11: State Changes (cont.)
If the STA is assumed to start its WUR awake/doze schedule upon the completion of a WUR setup frame exchange defining the WUR mode:
  The need for WUR mode suspend capability is probably no longer necessary. As procedure for triggering WUR mode would provide all the require configuration information to be exchanged by the WUR non-AP STA and WUR AP to trigger the mode. Therefore there is no need to remember the WUR parameters with WUR mode suspend.
  Note that if WUR mode is triggered by the setup frame exchange then it is independent of PS mode.
If the STA with a defined WUR mode is assumed to be trigger to start its WUR awake/doze schedule by sending a frame with the PS bit set to 1:
  This needs to be clearly specified
  I have a hard time understanding why WUR isn’t simply a new Power Save mode. As, any mode that uses the PS bit to trigger its behavior and saves power should be considered a Power Save mode.
  If WUR mode is activated by setting the PS bit, then the WUR mode suspend has purpose.
  If WUR is a Power Save mode, why does it need a MAC clause? Why isn’t it describe in the 11.2 the Power management clause
Please see the following two Mode/State diagram slides, one for each of these cases

## Slide 12: WUR STA Mode Active Triggered by WUR Frame Exchange
PS mode
Active mode
Doze State
Awake State
WUR mode
WUR Mode can be triggered from any mode, WUR wakeup would return to any mode (Active or PS).
WUR Doze State
WUR Awake State
STA completes WUR frame exchange
STA completes WUR fame exchange
STA send PPDU to the AP with PS bit set to 0
STA send PPDU with PS bit set to 1,

## Slide 13: WUR STA Mode Active Triggered by Setting PS Bit in a PPDU
PS mode
Active mode
Doze State
Awake State
WUR mode
WUR Mode can be triggered from any PS state, WUR wakeup would return to that PS state.
WUR Doze State
WUR Awake State
STA send PPDU with PS bit set to 1, WUR not configured
STA send PPDU with PS bit set to 1, WUR is configured
STA send PPDU with PS bit set to 1, WUR is configured
STA send PPDU with PS bit set to 0
STA send PPDU with PS bit set to 0, WUR is configured
STA send PPDU with PS bit set to 1, WUR is suspended

## Slide 14: Potential Issues with AP Behavior and transmission of WUR PPDUS

## Slide 15: WUR PPDU Transmission
Why is the requirements for the AP to maintain the non-AP STA’s WUR awake time not specified where the requirement to maintain the WUR status is specified? It is specified in a sub-bullet of the “If a WUR non-AP STA is in WUR mode, then:” requirements.
The specification says that the WUR non-AP STA is in the doze state when the AP transmits the WUR PPDU. The doze state is a power management state defined to be a state where the STA does not receive PPDUs. This is very confusing. Shouldn’t the specification say that the WUR PPDU is transmitted when the WUR non-AP STA is in WUR awake state?

## Slide 16: WUR AP Buffering Requirements
The draft seems to rely on the power management buffering of PPDUs for the WUR non-AP STAs. But, the draft does not state where the buffering is done nor which buffering rules are used. The draft only mentions what should be done with some buffered frames (Clause 29) and that frames are buffered (Clause 4). This should be clarified.

## Slide 17: WUR Wake-up Procedure (AP Behavior)
The specification does not provide guidelines for AP behavior regarding timeout intervals or WUR PPDU retries, stating:
“The methods by which a WUR AP determines the exact value of the timeout interval and determines the number of retries after the transmission of individually addressed WUR Wake-up frame fails are implementation specific and out of scope of this standard.”
This seem incomplete
Also there is no guidance for when an AP should disassociate a non-AP STA for being non-responsive and when is appropriate for an AP to disassociate it and clear the buffered PPDUs
The specification as written seems to require an AP to buffer data forever for non-responsive non-AP STAs.

## Slide 18: WUR Wake-up Procedure (STA Behavior)
The draft indicated that a non-AP STA which is woken up will “… follow existing operation, which is any PS operation the associated WUR AP and the WUR non-AP STA has agreed to use …”
This implies that a non-AP STA will always wake up in to a preconfigured PS mode. Therefore a non-AP STA must cycle through PS mode awake and doze states till it receives all the buffered PPDUs. This seems to undermine the ability of the STA to simply turn on is capability to receive/send PPDUs and send a PPDU to the AP indicating it is available to receive PPDUs. At which time the AP can then send all the buffered PPDUs and the STA can then send additional PPDUs or go back to WUR sleep.

## Slide 19: References
Draft P802.11REVmd_D2.0
24765-2017 - ISO/IEC/IEEE International Standard - Systems and software engineering—Vocabulary

## Slide 20: Appendix

## Slide 21
Figure 11-12
State Transition diagram of non-AP and non-PCP STAT in active and PS modes
From [1]

## Slide 22: WUR STA State Diagram Assuming WUR frame Exchange Trigger
Scheduled PS mode
Active mode
Unscheduled PS mode
Scheduled / Unscheduled PS mode
WUR mode
WUR Mode can be triggered from any PS state, WUR wakeup would return to that PS state.

## Slide 23: WUR STA State Diagram Assuming PS Bit Trigger
Scheduled PS mode
Active mode
Unscheduled PS mode
Scheduled / Unscheduled PS mode
WUR mode
WUR Mode is triggered by the PS bit – as PS modes are. WUR wakeup to Active mode.