## Slide 1: NGV PPDU with Hierarchical MCS
Date: 2019-09-11
Authors:

## Slide 2: Abstract
This contribution proposes a new NGV PPDU, compatible with the WAVE PPDU, which enables spectral efficient communications, by allowing WAVE and NGV capable devices to simultaneously transmit/receive using hierarchical modulation and coding scheme (MCS)
A different kind of NGV PPDU, where WAVE and NGV payloads were concatenated in time, was discussed in [1]

## Slide 3: Motivation
NGV use cases
  2. Sensor sharing,
  4. Infrastructure applications and
  6. Automated driving assistance
introduce new services demanding high throughput [3]
At the same time, legacy basic safety message (BSM) services need to continue to be supported
In dense scenarios, like high traffic areas, spectrum efficiency is thus important to meet both the high throughput and BSM requirements of different services
One method to increase spectrum efficiency is to enable simultaneous transmissions

## Slide 4: Multiplexing with Hierarchical MCS
Hierarchical MCS allows simulation transmission/ reception
The basic idea behind hierarchical MCS is to have two independent streams, called basic and additional layer, transmitted at the same time, each with a different MCS
Hierarchical MCS is a technology already in use, for instance, in various DVB standards [2]
  In DVB, an example of such transmission may include standard definition (SD) video encoded with 16QAM modulation and high definition (HD) video encoded with 256QAM

## Slide 5: WAVE and NGV layers
The WAVE receiver decodes only the basic (WAVE-) layer, while the NGV receiver decodes both layers, the basic (WAVE-) and the additional (NGV-) layers, depending on the SINR
We preferably need a mechanism to indicate NGV layer existence to NGV devices e.g. by reusing some WAVE header bit
If there is no reusable bits to spare for this purpose, NGV MCS can be derived from WAVE MCS (e.g. if WAVE layer is modulated with QPSK then NGV is with 64QAM)
WAVE stream bits
NGV stream bits
802.11bd
MAC
802.11bd
PHY
802.11bd
MAC
802.11bd
PHY
802.11p
MAC
802.11p
PHY
BSM-1 MCS-x
BSM-2 MCS-y
BSM-1
BSM-2
BSM-1
Hierarchical multiplexing
BSM-1 on WAVE layer
BSM-2 on NGV layer
Both layers
received
Only WAVE
Layer received
BSM: Basic Safety Message

## Slide 6: Proposal
We propose a new type of NGV PPDU that is compatible with WAVE PPDU
Comparing NGV PPDU multiplexing WAVE+NGV using hierarchical MCS with that concatenating payloads in time, the main advantage of the former is the simultaneous transmission of the payloads and the main disadvantage is the inter-layer interference, which demands for better SINR
We believe that both multiplexing methods (hierarchical MCS and time concatenation) would be beneficial to be specified in TGbd, allowing upper layers to trade spectral efficiency and reliability

## Slide 7: References
[1] https://mentor.ieee.org/802.11/dcn/19/11-19-0082-02-00bd-interoperable-approach-for-ngv-new-modulations.pptx
[2] https://www.etsi.org/deliver/etsi_tr/102300_102399/102377/01.04.01_60/tr_102377v010401p.pdf
[3] https://mentor.ieee.org/802.11/dcn/18/11-18-1323-02-0ngv-ngv-sg-use-cases.pptx