## Slide 1: Use Case Document: AP tagged UL forwarding
Date: 2019-05-14
Authors:

## Slide 2
Abstract
This presentation provides an additional use case scenario to be incorporated into TGbc use case document (11-19/0268) and updating the TGbc Functional Requirements document (11-19/0151).

## Slide 3: Use Case xx: AP tagged UL forwarding
Stakeholders
  IoT Users, IoT operators, tracking services, etc
  Manufactures of semiconductor, APs, networking and mobile devices
Topology/Architecture
Expected Benefits:
  Ability to broadcast information destined to the end server
  Ability to reduce cost and implementation complexity
  Ability to enable low power STA operations
Service scene
  An eBCS AP provides forwarding service to an end-servers for eBCS non-AP STAs that may not be associated with the AP
  An eBCS AP appends on additional information before forwarding the packet to the addressed server
Required function
Pre-configured low-cost low power tracker device automatically connects to an end server through eBCS APs in the neighborhood with zero setup action
Tracker device periodically reports to its server through eBCS APs without scanning and association
eBCS AP appends metadata (such as IP, date/time, location, RSSI etc) to the packets before forwarding to the destination server
Meta-data from an eBCS AP will be protected

## Slide 4: Additions to Functional Requirements document
3.4 Association state
  TGbc R6: The 802.11bc amendment shall support modes of operation:
  a) in an infrastructure BSS where there is an association between the transmitter and the receiver(s)
  b) in cases where there is no association between transmitter(s) and receiver(s). [Ref-1 5.2.b]
  TGbc R7: 802.11bc amendment shall have a mechanism to facilitate power-efficient broadcasting.
  TGbc R8: 802.11bc amendment assumes that there is no association and/or handshake required between STA and the AP.
  TGbc Rx: 802.11bc amendment shall provide a mechanism for an AP to append metadata (such as IP address, date, time, location, RSSI) to a packet before forwarding it to a remote server. Confidentiality and integrity of the appended meta-data shall be assured.