## Slide 1: 11az Ranging and Location Privacy
Date: 2019-05-12
Authors:
Name | Affiliations | Address | Phone | Email
Qi Wang | Apple, Inc. |  |  | qi_wang2@apple.com
Chris Hartman | Apple, Inc. |  |  | chartman@apple.com
Tomo Adachi | Toshiba |  |  | tomo.adachi@toshiba.co.jp
Saishankar Nandagopalan | Cypress |  |  | saishankar.nandagopalan@cypress.com
Prabodh Varshney | Nokia |  |  | prabodh.varshney@nokia.com
Michael Montemurro | Blackberry |  |  | mmontemurro@blackberry.com
William Carney | Sony |  |  | William.Carney@sony.com

## Slide 2: Motivation
802.11 has been working for years to develop mechanisms to improve and protect user privacy.
“Many words have been written about privacy over the past year, including in these pages. I believe it’s one of the most important topics of our time.” -- Sundar Pichar, Google CEO, in a New York Times article on May 7, 2019
The outcome of the ongoing 11az debate of ranging/location privacy has broad and important implications for the design of the 802.11 technology concerning user privacy and its potential adoption in the marketplace.

## Slide 3: Background on FTM
FTM procedure enables range measurement between two STAs
  Range = c/2 * [(t4 - t1)- (t3-t2)]
  ISTA derives its location from:
    Ranging with >= 3 RSTAs/APs
    Known locations of the RSTAs/APs
802.11az defines FTM enhancements to improve:
  Accuracy
  Scalability
  Security
Fig.2 Location determination using triangulation
Fig.1 FTM ranging principle

## Slide 4: Background on FTM – cont’d
Fig.3 Components of FTM procedure
Fig.4 FTM negotiation phase

## Slide 5: 11az Ranging/Location Privacy Debate
What should be the permitted behavior(s) of RSTA (i.e., RSTA’s “negotiation status” and “I2R LMR Feedback” setting in negotiation response frame)?

## Slide 6: Our Positions and Rationale (1)
ISTA, not RSTA, shall drive the negotiation concerning whether ISTA’s location is shared; RSTA shall only act in accordance with ISTA’s choice.
An ISTA can be a personal device.
Location sharing requires explicit user consent.
A user’s privacy choice shall not be dictated by a network.
Public policy and regulatory statutes increasingly driving user privacy expectations.

## Slide 7: Our Positions and Rationale (2)
RSTA shall not override ISTA’s ”I2R LMR Feedback” in RSTA’s negotiation responding frame.
Philosophically:
Due to the very nature of privacy, and the increasing regulatory oversight, ISTA’s privacy choice shall always be respected.
Technically:
Changing an ISTA’s ”I2R LMR Feedback” setting requires a specific action by an end user, which cannot be accomplished by receiving an RSTA’s negotiation response frame with an overridden value at the MAC layer. Allowing overriding by removing the user from this critical decision makes no technical sense.

## Slide 8: Our Positions and Rationale (3)
RSTA shall not reject a ranging request solely because ISTA has not explicitly granted permission to share its location.
802.11 protocol execution shall not rely on users’ surrender of privacy control.
Rejection (i.e., no ranging) because of ISTA’s not sharing location at the PHY/MAC layer precludes ISTA’s location sharing at a higher layer if desired.
Not providing ranging service to those ISTAs impairs 11az market adoption and success.

## Slide 9: Compromise under consideration
Compromise proposal in 11-19-0331r3 (not accepted by TGaz)
  RSTA should not reject an ISTA’s request solely because the ISTA is unwilling to share its location.
  RSTA sets a “Ranging Privacy” bit in the Extended Capabilities element in beacons
-- Differentiates between APs w.r.t. sharing policy
-- Improves negotiation efficiency
  RSTA with Ranging Privacy bit set to 1 shall not reject an ISTA’s request solely because the ISTA is unwilling to share its location.
Further compromise discussions are still ongoing.

## Slide 10: Serious Implications For 802.11
Should the execution of an 802.11 protocol be contingent on willingness of users to surrender their privacy?
  Or in other words: Should a technical specification require users to compromise their privacy, whether knowingly or not, in order to utilize some functionality therein?
Can a device declaring support of a feature refuse to execute the mandatory part of the feature solely because its communication peer doesn’t activate an optional part of the feature?

## Slide 11: 11az Status
No final agreement has been achieved.
TGaz has scheduled further discussion of this topic during the Atlanta May 2019 meeting.
  Wednesday PM1, Highland Ballroom IV/V – lobby level
  Thursday AM1, Highland Ballroom I/II – lobby level
  Thursday PM2, Highland Ballroom I/II – lobby level

## Slide 12: Straw Poll 1
Do you agree that the execution of an 802.11 protocol shall not be contingent on willingness of users to surrender their privacy?
Results:
Yes: No: Abstain:

## Slide 13: Straw Poll 2
Do you agree that a device declaring support of a feature shall not refuse to execute the mandatory part of the feature solely because its communication peer doesn’t activate an optional part of the feature?
Result:
Yes: No: Abstain:

## Slide 14: References
[1] IEEE Draft P802.11az_D1.0 - Draft Standard for Information Technology - Telecommunications and Information Exchange Between Systems Local and Metropolitan Area Networks - Specific Requirements Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications - Amendment 8: Enhancements for Positioning
[2] IEEE Std 802.11-2016 (Revision of IEEE Std 802.11-2012) - IEEE Standard for Information technology—Telecommunications and information exchange between systems Local and metropolitan area networks—Specific requirements - Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications
[3] IEEE 802.11-19-005r0, 802.11az Annex-C, G. Venkatesan, Intel, et al.
[4] IEEE 802.11-19-481, “RSTA requires ISTA-to-RSTA LMR”, A. Raissinia, Qualcomm, et al.
[5] IEEE 802.11-19-331, “Text clarification on ISTA-to-RSTA LMR”, Q. Wang, Apple, et al.