## Slide 1: Paths to 5G
Date: 2019-05-14
Authors:
Name | Affiliations | Address | Phone | email
Roger Marks | EthAirNet Associates | Denver, CO, USA | 1-802-capable | roger@ethair.net

## Slide 2: Abstract
This contribution provides a list of possible alternatives to advance the standing of IEEE 802.11 as a 5G technology.

## Slide 3: Background
A January 2016 contribution presented a preview of the nature and relevance of 5G and IMT-2020, putting forth six IMT propositions and also proposing several ways for IEEE 802 to participate [1]
Subsequently, IEEE 802 chartered the 5G/IMT-2020 Standing Committee [2], which met from March-July 2016 and issued a report covering:
  Costs and benefits of creating an IEEE 5G specification
  Costs and benefits of providing a proposal for IMT-2020, considering possible models of a proposal:
    as a single technology,
    as a set of technologies,
    or as one or more technologies within a proposal from external
    bodies (e.g., 3GPP)
See those documents for details, not reiterated here.
This document lists several alternatives that could be considered at the current time.

## Slide 4: Paths
The slides below list several possible paths.
These are not necessarily mutually exclusive.
This contribution does not fully analyze the paths.
In some cases, basic arguments pro and con are provided, but this contribution does not advocate in favor of any path and does not intend to suggest that the benefits of any path outweigh its negatives.

## Slide 5: Path 1: Inclusion in Initial IMT-2020 Recommendation
Development of Initial IMT-2020 Recommendation is underway in ITU-R Working Party 5D
  Proposal deadline July 2, with many hoops to jump through beforehand
Pro:
  strong 5G recognition value
  good IMT spectrum value; however,
    IMT identification is not mandatory for administrations
    could result in risk to RLAN spectrum
Con:
  late to develop a solid proposal
  Requires successful evaluation in all five test environments
  Partnership required, because 802.11 may not meet all five
  Partnerships are risky and troublesome
    ITU may expect coordination among partners on all future issues, including standards and ongoing maintenance (e.g. endorsement of documents, etc.)

## Slide 6: Path 2: Inclusion in Revised IMT-2020 Recommendation
Revision of IMT-2020 Recommendation will be ongoing and quasi-periodic
  Likely every two years
Each revision will provide an opportunity to submit a new proposal
Per Workplan, timeline, process and deliverables for the future development of IMT, ‘It has been agreed that the well-known process and deliverable formats utilized for both IMT-2000 and IMT-Advanced should be utilized also for IMT-2020 and considered as a “model” for the IMT-2020 deliverables to leverage on the prior work.’
Per Document IMT-ADV/25 (Rev.2 ), “WP 5D has adopted the following basic principles for developing draft revisions of Recommendation ITU-R M.2012:
  1) a recurring update within ITU-R for the formal revision of the Recommendation ITU-R M.2012 is appropriate in order to incorporate the latest and most up to date versions of the detailed specifications in Recommendation ITU-R M.2012;
  2) that new proposals for candidate terrestrial radio interface technologies will follow the process used for the initial IMT-Advanced technologies;

## Slide 7: Path 3: Inclusion in Revised IMT-Advanced Recommendation
IMT comprises IMT-2000, IMT-Advanced (2012), and IMT-2020
IMT-2000 Recommendation was originally updated annually
Now, IMT-2000 and IMT-Advanced are updated in alternate years
Each revision provides an opportunity to submit a new proposal.
IMT-Advanced does not require all four test environments
  RIT or SRIT will be accepted for inclusion in the standardization phase if, as the result of deliberation by ITU-R, it is determined that the RIT or SRIT meets the requirements... for three of the four test environments ...
Con:
  less marketing value than IMT-2020
Pro:
  from an ITU Radio Regulations perspective, offers the same spectrum value as IMT-2020, since spectrum is identified for IMT, not for IMT-2000, IMT-Advanced, or IMT-2020

## Slide 8: Path 4: IMT-2020 RIT
Submit one or more IMT-2020 RITs, not claiming all five test environments
  If the proposal is judged to be complete, it is forwarded to the registered external evaluation groups.
See Document IMT-2020/2 (“Submission, evaluation process and consensus building for IMT-2020”)
  Step 4 – Evaluation of candidate RITs or SRITs by independent evaluation groups
    Candidate RITs or SRITs will be evaluated. The ITU-R membership, standards organizations, and other organizations are invited to proceed with the evaluation.
Pro: prestigious support for self-evaluation if results are favorable
Could lead to:
  positive impression among customers
  favorable treatment by regulators

## Slide 9: Path 4/Note 1: Current independent evaluation groups
5G Infrastructure Association
ATIS WTSC IMT-2020 Evaluation Group
Canadian Evaluation Group
Wireless World Research Forum
Telecom Centres of Excellence, India
The Fifth Generation Mobile Communications Promotion Forum, Japan
TTA 5G Technology Evaluation Special Project Group
Trans-Pacific Evaluation Group
ETSI Evaluation Group
Egyptian Evaluation Group
5G India Forum

## Slide 10: Path 4/Note 2: Process Step Highlights
Step 4 – Evaluation of candidate RITs or SRITs by independent evaluation groups
Step 6 – Review to assess compliance with minimum requirements
  …evaluated proposal for an RIT/SRIT is assessed as a qualifying RIT/SRIT, if an RIT/SRIT fulfils the minimum requirements for the five test environments…
  Such a qualified RIT/SRIT will go forward for further consideration in Step 7.
  According to the decision of the proponents, earlier steps may be revisited to complement, revise, clarify and include possible consensus-building for candidate RITs or SRITs including those that initially do not fulfil the minimum requirements …
  …documentation and feedback resulting from this step can facilitate consensus building that might take place external to the ITU-R in support of Step 7.
Step 7 – Consideration of evaluation results, consensus building and decision
  WP 5D will consider the evaluation results of those RITs or SRITs that have satisfied the review process in Step 6.
  Consensus building is performed during Steps 4, 5, 6 and 7 with the objective of achieving global harmonization and having the potential for wide industry support … This may include grouping of RITs or modifications to RITs to create SRITs that better meet the objectives of IMT-2020.
  An RIT or SRIT will be accepted for inclusion in the standardization phase described in Step 8 if, as the result of deliberation by ITU-R, it is determined that the RIT or SRIT meets the requirements … for the five test environments….

## Slide 11: Path 5: Carry positive RIT evaluation into SRIT
opportunity to join with other players during “consensus building” period to become part of a complete SRIT
could join with small players
big players might be pressured by customers to join
positive evaluation would strengthen position in merger negotiations
could take Path 5 at initial IMT-2020 development or in revision process

## Slide 12: Path 6: Forward self-evaluation directly to independent evaluation groups
independent evaluation groups are independent
could invite independent evaluation groups to provide an assessment of a proposal, even if that proposal was not made to ITU
some evaluation groups would almost certainly decline
some evaluation groups might decide to evaluate
as with Path 4, could lead to support for self-evaluation, which could add credibility and form the basis for future developments

## Slide 13: Path 7: Develop Nendica activity
Final Report of IEEE 802 5G/IMT-2020 Standing Committee proposed “Action A” and “Action B”
Action B
  IMT-2020 proposal
  led to 802.11 AANI
Action A
  an IEEE “5G” specification
  led to IEEE 802 “Network Enhancements for the Next Decade” Industry Connections Activity (Nendica)

## Slide 14: Path 7/Note: Action A: Candidate Approach (from IEEE 802 5G/IMT-2020 CS Final Report)
specify an 802 access network
  could be based on P802.1CF
  provides an external view into general 802 access network
  could support many 802 MACs and PHYs
  could plug into incumbent mobile operator networks
    for example, expand the notion of LWA so that the cellular network supports 802 rather than 802.11
    gives 802 a strong supporting role in cellular 5G networks
  could support integration into other operator networks
  e.g. cable TV or fixed telecom
  gives 802 a central role in non-cellular 5G networks
  feasible for 802 access network to support both
  need not promote it as an “IEEE 5G” network

## Slide 15: Paths 8 to ∞
As you like.

## Slide 16: References
[1] R. Marks, “5G and IMT-2020: What it is, its relevance, and ways to participate,” 2016-01-22 (IEEE 802-ec-16-0010-00-00EC)
[2] IEEE 802 5G/IMT-2020 Standing Committee http://www.ieee802.org/Stand_Com/5G