## Slide 1: ISTA2RSTA LMR Feedback AP Policy and Negotiation
Date: 2019-05-01
Authors:

## Slide 2: Add a bit to the Extended Capabilities element
Yet to be named bit: 0
  The RSTA does not care about ISTA2RSTA LMR Feedback
  The RSTA shall not set ISTA2RSTA LMR Feedback in Initial Fine Timing Measurement frame to 1, if the ISTA has indicated that it is not willing to share (in IFTMR)
  The RSTA may set ISTA2RSTA LMR Feedback in Initial Fine Timing Measurement frame to 1, if the ISTA has indicated that it is willing to share (in IFTMR)
Yet to be named bit: 1
  The RSTA expects the ISTA2RSTA LMR Feedback to be negotiated in the IFTMR/IFTM exchange
  ISTA indicates that it can/cannot share ISTA2RSTA LMR using the ISTA2RSTA LMR Feedback subfield in IFTMR
  The RSTA could reject the session if the ISTA setting of ISTA2RSTA LMR Feedback in IFTMR frame is not acceptable
  RSTA indicates that it requires/does not require ISTA2RSTA LMR at the end of each measurement exchange using the ISTA2RSTA LMR Feedback subfield in IFTM
  The ISTA terminates the session if the RSTA setting of ISTA2RSTA LMR Feedback in IFTM frame is not acceptable

## Slide 3: Yet to be named bit – potential names
RSTA has no constraints on ISTA2RSTA LMR
Negotiate ISTA2RSTA LMR
ISTA2RSTA LMR Not Required
RSTA follows ISTA’s ISTA2RSTA LMR setting
ISTA2RSTA LMR Sharing Non-override/Negotiate
ISTA’s LMR Sharing Preserve/Negotiate
ISTA’s LMR Sharing Preference/Negotiate