## Slide 1: MAC Simulation Methodology: Insights from LC Channel Measurements
Date: 2019-05-15
Authors:

## Slide 2: Abstract
This contribution aims to develop a MAC layer simulation methodology for TGbb based on insights from an indoor LC channel measurement campaign with optical frontends similar to the ones modeled in doc. 11-18/1574r5.

## Slide 3: MAC layer simulations in TGbb
Objectives
Compare frequency-selective MAC (Bitloading, OFDMA) with any baseline
Derive performance metrics at MAC SAP (see doc. 11-19/0187r5)
  Per-STA throughput
  Per-BSS throughput
  Packet loss
  Transmission latency (i.e. MAC processing delay)
  End-to-end latency
Support the technical discussion and technology selection on MAC in TGbb

## Slide 4: MAC layer evaluation input
Single link
  Transmit Power P(f)
  Tx-Rx Frontends response F(f)
  Path loss G(f)
  Noise Power N(f)
Note: UL/DL are not reciprocal, cf. spatial characteristics of LED/PD
AP
STA
DL
UL
=

## Slide 5: Methodology for single link
Methodology
Start from SNR(f)
Estimate achievable rate
Select appropriate PHY mode
Model random packet loss
Derive performance metrics
=

## Slide 6: G(f): Insights from LC channel measurements
Using two optical frontends (OFE)
  IR LED 850 nm (4x SFH 4715AS)
  White LED (1x Cree XLAMP XM-L2)
  PD (5x Hamamatsu S6968)
Vector Network Analyzer
  Agilent E5061B-3L5
  Calibrated between OFE in- and outputs
Frontends response
  Place Tx and Rx in LOS at minimum distortion-free distance of 80 cm
  Measure Tx-Rx response, divide other results by it  channel frequency response

## Slide 7: Measured LC frontends response F(f)
Slide 7
LED driver and PD+TIA similar to model in doc. 11-18/1574r4
IR LED response is flat until 100 MHz and then it decays smoothly
White LED efficiency is reduced by 20 and 40 dB at low and high frequencies
  +10 dB correction factor applies for different spatial characteristics of IR vs. white LED
Colour conversion from blue to white causes significantly reduced bandwidth
Further results all use IR LED

## Slide 8: Measured LC path loss G(f)
Slide 8
All measurements at 1 m distance
LOS
  Both OFEs point to each other
  fairly flat frequency response
NLOS with 1st reflection
  Both OFEs point to the ceiling
  >20 dBel loss compared to LOS
  almost flat frequency response
NLOS multiple reflections
  Both OFEs point away from each other
  Decay at low frequencies (higher order reflections), frequency-selective fading

## Slide 9: G(F): NLOS results vs. distance
Slide 9
Including 1st reflection
Only higher order reflections

## Slide 10: Implications on MAC modeling
F(f): Frontends response
  Driver+LED and PD+TIA design lead to frequency-selective responses
  Differences between White and IR LED
G(f): Path loss LOS
  Links can be modeled by geometrical path loss and delay
  Delay is relevant for multilink scenarios with wide bandwidth
G(f): Path loss NLOS
  Significantly higher than LOS, relevant in case of blocking and in room corners
  Response depends on Tx and Rx positions (difference 1st/HO reflections)
  Often shows fading if not superimposed with LOS or 1st reflection signals

## Slide 11: Implications on MAC modeling
G(f): Frequency-selective path gain must be modelled realistically
  Depends on position and orientation of Tx and Rx
  Ray tracing for 10.000 random positions  derive metrics
  Simplifications needed due to high computational effort
  “Black box” channel t.b.d.
N(f): Noise response
  Sophisticated TIA design using bootstrap and peaking techniques
  Noise is not white, it can be enhanced at some frequencies
  Proposal is modeling based on measurements on exemplary frontends
  Noise model t.b.d.

## Slide 12: Multilink MAC modeling
2) Multiple links
  Transmit Powers Pj(f)
  Tx-Rx response F(f)
  Path loss matrix Gij(f)
  Noise Powers Ni(f)
  Applies to asynchronous transmissions, synchronous MIMO t.b.d.
AP
STA
AP
STA
AP
=

## Slide 13: Methodology for multiple links
Path loss matrix Gij(f) is obtained from „Black box“ channel model
Scheduling algorithm is expected to assign Pj(f)
Methodology
Compute SINRi(f) for each STA or at each BSS
Estimate achievable rate
Select appropriate PHY mode
Model random packet loss
Derive performance metrics
=

## Slide 14: MAC layer evaluation methodology
Estimate the achieveable rate
  only needed for bit-interleaved coded modulatioon (BICM)
  use L2S interface such as MIESM, know the appropriate correction factors
Select appropriate PHY mode
  With bitloading: Load bits so that a given PER target is achieved
  With BICM: Select appropriate PHY mode achieving a given PER target
Model random packet loss
  With bitloading: Random AWGN process, straight forward
  With BICM: More complicated, model is usually simplified and uncertain how realistic results are

## Slide 15: Open items for MAC layer evaluation in TGbb
Realistic channel model
  Frequency-selective channel model for multiple BSS and large number of STA positions (1k-10k realizations), Ray tracing might not be an option
Synchroneous SINR model
Noise modelling
  Can be supplied by measurements on realistic frontends
L2S interface for BICM
  Choice and parametrization
  Must be verified carefully using bit-true simulations
Realistic packet loss model for BICM

## Slide 16: Straw poll
Do you think TGbb should solve the open items for MAC layer simulation methodology and revisit the topic in July plenary?
Y / N / A =

## Slide 17: Reference
[1] Sreelal Maravanchery Mana, Peter Hellwig, Jonas Hilt, Pablo Wilke Berenguer, Volker Jungnickel, „Experiments in Non-Line-of-Sight Li-Fi Channels”, Proc. 2nd Global Li-Fi Congress, Paris, France, 12-13 June 2019.